## Slide 1: Chapter 10 – Treating Risk
Developed by Bruce Lyon, CSP, P.E., SMS, ARM, CHMM
Dr. Georgi Popov, CSP, QEP, ARM, SMS, CMC, FAIHA
Notes: In this chapter we will:
Review the concept of treating risk
Evaluating and selecting treatment strategies
And methods that can be used to treat risk

## Slide 2: Treating Risk
Treat risks to an acceptable level
Primary purpose of risk assessment
Output of risk assessment
Notes: To manage risk, is to treat those risks that are unacceptable. Risk treatment, the process to reduce risks that are considered unacceptable, involves the selection and application of one or more treatment strategies to achieve and maintain an acceptable level to the organization. It is arguably the most important step in the risk management process since it is designed to achieve and maintain an acceptable risk level.
Risk treatment is the ‘output’ of the risk evaluation and the primary purpose of risk assessment. Following the evaluation of risk, those risks that are judged to be unacceptable require treatment to reduce their risk level. Without treating risks that have been assessed, a risk assessment is of no value, and in fact may lead to negligence of the organization. When specific risks have been identified and assessed as being unacceptable, it is incumbent upon the organization to take action to treat the risk in an appropriate and timely manner.

## Slide 3: Treating Risk
formulating and selecting options
additional risk treatments needed
planning and implementing risk treatments
assessing their effectiveness
determining the acceptability of residual risks
Notes: As stated by ISO 31000, the purpose of risk treatment is to select and implement strategies that manage risk in an iterative process. The process includes formulating and selecting options, planning, and implementing risk treatments, assessing their effectiveness, determining the acceptability of residual risks, and additional risk treatments needed.

## Slide 4: Treating and Controlling Risk
Risk Treatment - “process to modify risk” and may include different or multiple strategies.
Risk Control - “measure that maintains and/or modifies risk”. The term risk control is often used in the insurance industry and OSH profession.
Notes: When an organization judges a level of risk to be unacceptable, it must make decisions to treat the risk in a way to modify its level. Such treatment of risk involves the careful selection and application of risk treatment strategies that will modify and reduce the risk to an acceptable level. These strategies can include avoidance, reduction, transfer, retention or pursuing certain opportunities depending upon the type of risk.
Risk treatment is defined as the “process to modify risk” and may include different or multiple strategies.
The term ‘risk control’ is often used in the insurance industry and occupational safety and health (OSH) profession. ‘Control’ is defined by ISO 31000 as a “measure that maintains and/or modifies risk”. Controls include any process, policy, device, practice or other conditions or actions that maintain and/or modify risk

## Slide 5: Treating and Controlling Risk
Notes: There are many forms of risk treatment, some more effective and reliable than others. Risk treatment options can be applied in many ways and are not necessarily mutually exclusive or appropriate in all circumstances. In many situations, more than one treatment strategy is required to adequately reduce and control the risk to an acceptable level. Risk treatment strategies available to an organization’s risk management include avoidance of risk, pursuing of risk, eliminating risk, reducing risk, transferring risk, sharing risk, and retaining risk.
Let’s review all the options.

## Slide 6: Treating and Controlling Risk
Notes: The most effective means of managing risks that are derived from hazards and operations, is to avoid the risk entirely. An organization may make an informed decision to not engage in a particular activity that presents a risk that is considered unacceptable. In a new facility, a design safety review can be used to identify and avoid new hazards from being introduced into the design. Avoiding risk may not always be possible, however, it should be the first consideration regarding pure risks.

## Slide 7: Treating and Controlling Risk
Notes: For speculative type risks that result from financial and strategic type ventures, it may be advantageous to pursue a risk for expected gains and benefits. Organizations are continuously looking for ways to create and protect value to achieve their business objectives. Through proper cost/benefit analysis and assessment of the risks, an organization may choose to pursue an opportunity such as an acquisition, expansion into a new market, or a financial investment to advance their financial or strategic position.
Example of Pursuing Risk
An international insurance firm decides to expand their market to areas in Asia by acquiring an existing Asian firm, balancing the increased market share opportunities with the political and cultural risks.
An organization decides to make a ‘significant’ investment in the Research and Development of robotics to increase their capacity, performance, and quality.

## Slide 8: Treating and Controlling Risk
Notes: For existing risks that are judged to be unacceptable, the most effective and immediate risk treatment is removal or elimination of the risk source. It is important to recognize that such controls may introduce other risk sources that require assessment, treatment, and management.
Examples of Eliminating Risk
Realizing that elevated work presents a potential for falls and a significant risk of fatalities and serious injuries, a manufacturing company decides to eliminate elevated work by removing elevated work platforms making all work at surface level through redesign of the facility.
An assembly operation with costly musculoskeletal injuries resulting from manual material handling decides to eliminate these exposures by installing an automated system that eliminates excessive manual material handling.
An organization eliminates all sharp edges on their workstations by rounding corners and rolling over edges.
A manufacturer eliminates the exposure to a hazardous chemical process in the facility by redesigning it as an enclosed system and relocating it outside of the workplace.

## Slide 9: Treating and Controlling Risk - Reduce Risk
Notes: Pure risk can be reduced by reducing the risk source’s likelihood of occurrence or by reducing the severity of its consequences through risk control measures. ​Risk reduction measures are used to minimize or reduce the likelihood and severity of an unwanted risk as shown in here. Risk reduction is defined as making risk smaller by reducing its severity of impact, reducing the chance for it to occur, or reducing the exposure. Let’s review the individual components of the risk reduction model.

## Slide 10: Treating and Controlling Risk - Reduce Risk
Prevention - keep something from occurring that would otherwise cause risk or harm.
Notes: Risk Prevention
Prevention is the act of keeping something from occurring that would otherwise cause risk or harm (reducing the likelihood of occurrence). Risk prevention is taken to reduce or eliminate the probability of specific undesirable events from happening. Examples of risk prevention include pressure relief valves to prevent over-pressurization or level indicators to detect levels in above ground storage tanks to reduce probability of overfilling. ​

## Slide 11: Treating and Controlling Risk - Reduce Risk
Mitigation - reduce the severity of something, making a condition or consequence less severe.
Notes: Risk Mitigation
Mitigation is the act of reducing the severity of something, making a condition or consequence less severe (reducing the severity of consequences). Mitigation is a reactionary measure used to reduce the impact on things at risk after the event occurs. Examples of risk mitigation include berms and containment dikes around tanks, evacuations, shelter-in-place, and emergency response plans. ​

## Slide 12: Treating and Controlling Risk - Reduce Risk
Protection - shield, cover, or keep something from harm.
Notes: Risk Protection
Protection is the act of shielding, covering, or keeping an asset from harm. Like mitigation, protection is a measure designed to limit the severity of harm or impact rather than prevent the event from occurring (reducing the severity of consequences). Examples of protection might include automatic fire suppression systems and sprinkler systems, fall protection systems, and protective shielding of computer systems and other high value assets. ​
​

## Slide 13: Treating and Controlling Risk - Reduce Risk
Control - reduce likelihood and/or severity of harm.
Notes: Risk Control
Control is to manage risk by reducing likelihood of occurrence and/or severity of its impact. A risk control is a measure that modifies risk and may include processes, policies, devices, practices, or other actions.
​

## Slide 14: Treating and Controlling Risk - Reduce Risk
Escalation factors – mechanisms/conditions that can lead to increased risk by defeating or reducing effectiveness of controls.
Notes: Escalation Factor
Escalation factors are control decay mechanisms or conditions that can lead to increased risk by defeating or reducing the effectiveness of preventive, protective or mitigative controls. Controls are seldom 100% effective due to escalation factors that can cause a control to degrade, fail or not work consistently or as expected. An escalation factor does not directly cause the top event or consequence rather it increases the likelihood that the scenario will progress because the associated control will be degraded or fail.
Now, let’s turn our attention to transfer of risk options.

## Slide 15: Transfer Risk
Transfer Risk
Insurance
Contracts
Hedging
Notes: Unacceptable risks that cannot be avoided, eliminated, or reduced through risk control measures may be transferred to third parties through insurance, noninsurance contracts or hedging. We’ll take a moment to discuss each risk transfer option.

## Slide 16: Transfer Risk
Transfer Risk
Insurance
Contracts
Hedging
Insurance - transfers potential financial consequences of specified events from the covered insured to the insurer.
Notes: Insurance
A common means of meeting the financial consequences of hazard and operational risk is achieved with the purchase of insurance coverage. Insurance is a form of risk transfer that involves transfers the potential financial consequences of certain specified events from the covered insured to the insurer. This form of risk treatment provides the insurance buyer a ‘known’ financial cost – the insurance premium – in place of an ‘unknown’, possibility large financial loss from covered claims paid by the insurer. As part of the agreed contract, the insurance carrier agrees to pay for all of the organization’s losses that are covered by the insurance contract as well as provide any specified services, such as risk control services, and claims handling.
Insurance is an important risk treatment component of a risk management program, and can include multiple layers of coverage (primary, secondary, excess, umbrella coverage) for liability, workers compensation, property, marine, inland marine, boiler and machinery, fleet, crime, cyber, directors and officers, business interruption, errors and omissions and other coverages.

## Slide 17: Transfer Risk
Transfer Risk
Insurance
Contracts
Hedging
Contracts – contractual risk transfer or noninsurance contracts are used to transfer financial consequences of an event or activity to a third party.
Notes: Contracts
Contractual risk transfer or noninsurance contracts are sometimes used as a risk treatment to transfer financial consequences of an event or activity to a third party. As with any contract, contractual risk transfer is an agreement between the risk owner and a third party to transfer financial or legal responsibility associated with specified activities, events, injuries, or damages. The contracted third party agrees to indemnify and hold the risk owner harmless in a contract, transferring the risk. Noninsurance contracts that assign responsibility for a particular event or activity that can produce risk to a third party are known as hold-harmless agreements or indemnity agreements.

## Slide 18: Transfer Risk
Transfer Risk
Insurance
Contracts
Hedging
Hedging – diversifying risks to offset uncertainties.
Notes: Hedging
A form of risk treatment for financial risks where there are uncertainties associated with costs or returns is known as ‘hedging’. In essences, it is a form of diversifying one’s risks, so as to not have too much risk in one place. Hedging is often used to reduce risk of adverse price variability of an investment and requires making a second investment that offsets the potential consequences or losses of the original investment.
‘Hedging’ Example: Hedging might involve spreading a company’s exposure to global investments to balance out their U.S. investments. Or the use of a ‘futures contract’ with a supplier to purchase a quantity of a product or commodity at a pre-agreed price to avoid price fluctuation. For example, during the fuel crisis, Southwest Airlines purchased jet fuel for a set price to avoid price fluctuations and uncertainty. South West airlines “hedged” the fuel costs when the price of barrel of crude oil is going “north” of $100 per barrel.

## Slide 19: Treating and Controlling Risk
Notes: Now, we’ll go back to our treating and controlling risk model. Let’s discuss risk sharing opportunities.
Share Risk
Risk sharing is the practice of distributing or sharing risks among other industries, organizations, company divisions, investors, and other external or internal stakeholders. The theory is that the risk burden and its financial consequences are lessen to a level that is acceptable to each individual risk owner. It involves sharing or dividing risk among two or more entities for financial gain. Risk sharing is a measure used to diversify and reduce the concentration of risks retained by a single organization.
‘Risk Sharing’ Example: Financial institutions use risk sharing practices in large loans to organizations where they share in the profits, as well as potential losses. Other examples of risk sharing include insurance products designed to ‘pool’ risks among companies within a region or industry group, and the forming of partnerships.

## Slide 20: Treating and Controlling Risk
Notes: Retain Risk​
Risk retention is a decision to intentionally retain a particular risk rather than transfer the risk with insurance or noninsurance contracts. Risk retention generally involves setting aside self-funding reserves by an organization to pay for losses as they occur, rather than shifting the risk to an insurer. An organization may choose to retain risks when they believe that the cost of doing so is less than the cost of fully or partially insuring against it.
Self-funding risk retention is generally used for pure risks (hazard or operational) when there is an internal fund within the organization to pay the cost of losses and when the cost for insurance is prohibitive or unavailable. For these reasons, it is sometimes the risk financing treatment of last resort.
We’ll discuss risk retention options in greater details next. We will review retention plans next.

## Slide 21: Selecting Risk Treatments
Figure 10.4, Risk Treatment Combinations
Notes: Risk treatment strategies and options should be selected according to their perceived effectiveness, reliability, advantages, and benefits as well as their costs, potential disadvantages, and other possible negative factors. Selection of the most appropriate risk treatment options requires an optimum balance of expected benefits and gains over the potential costs and negative aspects. Methods such as cost/benefit analysis, financial and non-financial benefits analyses, pay-back period analysis, return on investment (ROI) and others can be useful in selecting and justifying appropriate risk treatments.
The combination of risk treatments is also often used as illustrated here. For example, an organization may decide to accept and retain low severity/high frequency risks, while transferring high severity/low frequency risks through insurance. Such decisions are very often based on previous claims experience and statistical analysis.

## Slide 22: Selecting Risk Treatments
Figure 10.5, The Prouty Approach Model
Notes: One way to make decisions regarding risk retention and risk transfer is to apply the approach developed by Richard Prouty. He proposed an analysis and evaluation of risk exposures based on loss frequency and severity. This proposed methodology has since became widely known as the “Prouty Approach”. The Prouty Approach can be presented in a 3 x 4 risk matrix shown here.
Risk professionals should be aware of possible shortcomings of a qualitative risk matrix approach. For instance, slight and moderate severe outcomes are placed in the same category “Reduce or Prevent”. The monetary difference between “Slight”, “Moderate” and “Severe” outcomes could be millions of dollars. In addition, some modern methods would suggest a combination of prevention and mitigation layers. For instance, even for the “Slight Severity” events that are branded “Definite” on the Prouty matrix, both preventive and mitigation measures can be added. A good example is a slippery floor in a food processing facility where it is almost “Definite” that slips, and falls will occur. In the event the organization cannot “Prevent” 100% of the slips, mitigation controls such as return to work management plan can be implemented to reduce the severity of impact or loss.

## Slide 23: The Hierarchy of Risk Treatment Strategies
Figure 10.6, Hierarchy of Risk Treatment Model
Notes: The selection of risk treatments and controls for risk sources resulting from hazards and operations (pure risk) should be made in accordance to the hierarchy of risk controls concept. The concept is based on the ranking of control strategies from most effective and reliable in risk reduction to the least effective and reliable.
There are a number of existing hierarchy models, most of which include five strategies: elimination, substitution, engineering, administration, and personal protective equipment. Several include additional strategies including avoidance, minimization, simplification, passive engineering, active engineering, and warning devices. An example of a risk control hierarchy known as HoRT is provided here.

## Slide 24: Design-level Risk Control Strategies
Notes: The most effective and reliable risk control strategy is the avoidance of a potential risk sources. This strategy is applied in the design phase by intentionally identifying and designing facilities, processes, products, or activities that avoid the introduction of specific hazards and risk sources. This strategy is also used in redesigns, modifications and additions to existing systems and workplaces.

## Slide 25: Design-level Risk Control Strategies
Notes: A second strategy is elimination of existing risk sources from a system. Existing hazards and risks are eliminated or removed from systems/workplaces through redesign. Risk elimination is achieved by eliminating the need for a hazard or hazardous element in an existing process by redesigning the process. This may include removing and isolating a particular hazard away from people or assets, eliminating its exposure.

## Slide 26: Design-level Risk Control Strategies
Notes: A third strategy that should be considered when the first two options are not feasible, is substitution. Substitution can be applied for new or existing hazards and risks. The strategy involves intentionally evaluating and selecting a less hazardous materials, equipment, method, or activity that meet the needs of the system or workplace, while reducing the potential risk.
Examples of Risk Substitution
A winery substitutes a much less hazardous product, granulated potassium meta-bisulfite for pure sulfur dioxide liquid which is extremely toxic for the winemaking process.
The risk of exposure to COVID-19 from in-person meetings is reduced by using virtual meetings instead.

## Slide 27: Design-level Risk Control Strategies
Notes: Another strategy that can be used is minimizing the quantity or intensity of a particular hazard or risk source. The amount or quantity of a particular hazard is minimized to a level that presents a lower severity risk.
Examples of Risk Minimization
A food process operation reduces the size and weight of materials and ingredient handled by employees.
An existing chemical processing operation is redesigned to reduce the quantities of hazardous materials needed and reduce on-site storage.
A new manufacturing facility is designed to operate at lower voltages, lower temperatures, and lower pressures, and overall, less energy.

## Slide 28: Design-level Risk Control Strategies
Notes: Complicated or confusing systems and methods are potential risk sources for errors and adverse effects. Simplification is the strategy of reducing complexity in the system, its layout, controls, and methods to reduce the likelihood of error, and improve the likelihood of expected performance.
Example of Risk Simplification
An automobile manufacturer simplifies the design of controls and displays to improve ergonomics and human performance.
A complex chemical storage, piping and connecting system is simplified, color coded and streamlined to reduce the potential for mis-matching chemicals.
The number of steps to complete a critical task are reduced and simplified to reduce the potential for human error.

## Slide 29: Design-level Risk Control Strategies
Notes: For risk sources that cannot be avoided, eliminated, or reduced through design, engineering controls should be considered. Engineering-level Risk Control Strategies include two categories, passive and active.
Passive-type engineering controls are controls that function continually without activation. Passive engineering controls provide more reliable control than active-type controls.
Examples of Passive Engineering
Containment dikes and secondary containment around hazardous material storage tanks
Fixed or permanent guarding on machines
Guard rails on highways and bridges

## Slide 30: Design-level Risk Control Strategies
Notes: Active-type engineering controls are controls that only function upon activation or a trigger mechanism. Active engineering controls are less reliable since they can fail to function or be bypassed. They should not be the sole control measure; however, they can be incorporated in addition to other risk controls in a ‘layer of controls’ fashion.
Examples of Active Engineering
Presence sensing devices on machines
Two hand trips and interlocks
Process controls and safety instrumented systems (SIS)
Automatic fire suppression systems and sprinkler systems

## Slide 31: Design-level Risk Control Strategies
Notes: Warning and awareness controls are devices, sensors, alert systems, signage, labeling or other methods that inform or warn of residual risks by sight, sound, or touch. They provide limited protection since they require the individual to detect and respond to the warning.
Examples of Warning and Awareness Controls
Carbon monoxide detectors and fire alarms
Tornado warning sirens
Forklift backup alarm and flashing red light
Perimeter warning cones, rope, or tape
Warning or instructional signage
Highway ‘rumble strips’ to indicate drifting off road

## Slide 32: Design-level Risk Control Strategies
Notes: Administrative-level Risk Control Strategies are measures developed by management to educate, guide, and monitor employee performance. They are widely practiced; however, administrative controls should be used in support of higher-level controls rather than the sole measure due to their lack of effectiveness and reliability.
Examples of Administrative Controls
Written operating procedures and safety programs
General Lockout/tagout procedures; Machine-specific lockout/tagout procedures
Work Instructions
Orientation, training, education, and meetings
Supervision; equipment spotter; permit system; confined space entry attendant
Behavior-based safety efforts

## Slide 33: Design-level Risk Control Strategies
Notes: Personal protective equipment (PPE) is the least effective and least reliable control strategy, and the last line of defense. In this strategy, the exposure to hazards is hopefully reduced by proper donning and wearing of protective clothing and equipment. PPE is used to prevent or reduce contact, reduce exposure, and reduce impact or harm from physical, chemical, or biological hazards. Proper selection of appropriate equipment for the risk exposure is necessary for this control measure to be useful.

## Slide 34: Selecting Risk Treatments
Figure 10.7, Risk Treatment Decision Tree
Notes: Risk treatment strategies should be selected according to their effectiveness and reliability using the hierarchy of risk controls concept. Beginning with the most effective strategy, risk avoidance or elimination, each risk treatment strategy should be considered for its feasibility in reducing risk to ‘as low as reasonably practicable’ or ALARP. This approach to selecting risk control strategies in accordance to the hierarchy model is illustrated in the risk treatment decision tree shown here.
Decision makers should begin by asking is it possible to avoid or eliminate the risk? If not, then is it possible to substitute a less hazardous element to achieve ALARP? Decision makers continue down the decision tree until they are satisfied that the risk is ‘as low as reasonably practicable.’ This often requires multiple layers of controls such as a combination of engineering-level devices, administrative procedures and training, supervision and inspection, and finally personal protective equipment.

## Slide 35: Layering Risk Treatments
Figure 10.8, Layering of Risk Treatments Example
Notes: The concept of applying different risk treatments in layers to address more complex risks is an important aspect of reducing and managing risk. Rarely is a single control adequate in reducing and maintaining risk to a level that is considered acceptable. Layers of risk treatments and controls should be selected in accordance to their effectiveness and reliability using the hierarchy of risk treatments concept.
‘Layers of Protection’ is a concept whereby several independent devices, systems, or actions are provided to reduce the likelihood and severity of an undesirable event. Such control layers should be constructed, implemented, verified, and monitored to achieve a level that is ‘as low as reasonably practicable’ or ALARP.
Techniques such as barrier analysis, layers of protection analysis (LOPA), bow-tie analysis and modified methods such as Layers of Control Assessment (LOCA) can be used to assess existing controls and determine whether risks are at an acceptable level or if further risk reduction strategies are necessary to achieve and maintain ALARP.

## Slide 36: Acceptable Risk and ALARP
Zero risk is not possible
Tolerable risk – ‘level of risk that is accepted in a given context based on the current values of society’.
ALARP - ‘level of risk which can be further lowered only by an increase in resource expenditure that is disproportionate in relation to the resulting decrease in risk.’
Notes: Attaining a level of ‘zero risk’ is not possible. After applying risk treatments, risks can be reduced, however, there will always be some level of residual risk. Therefore, an organization must strive for a level of risk that is relatively acceptable in terms of the potential severity and likelihood. Acceptable risk is defined as ‘that risk for which the probability of an incident or exposure occurring and the severity of harm or damage that may result are as low as reasonably practicable (ALARP) in the setting being considered
In ISO/IEC Guide 51: Safety Aspects - Guidelines for its inclusion in standards, section 5 "The Concept of Safety", it states that “safety is achieved by reducing risk to a tolerable level, defined in this Guide as tolerable risk." The guide defines ‘tolerable risk’ as the “level of risk that is accepted in a given context based on the current values of society”. The guide further notes that the terms “acceptable risk” and “tolerable risk” are considered to be synonymous.
ALARP is defined as ‘that level of risk which can be further lowered only by an increase in resource expenditure that is disproportionate in relation to the resulting decrease in risk. (ANSI/ASSP Z590.3-2011 R2016) Risk treatment involves the selection and application of one or more risk control options to reduce ‘pure’ risk to a level that is 'as low as reasonably practicable' (ALARP) and acceptable to the organization. ​

## Slide 37: Risk Treatment Plans
proposed actions and timeline
rationale and justification for selections
benefits to stakeholders
responsibilities and accountabilities
performance metrics
monitoring and communicating results
Notes: As a result of the risk assessment, plans are made for treating the risk. Such plans can involve a single treatment or control; however, it is more likely that multiple risk treatment measures will be required to reduce and manage risk to an acceptable level. The plan should also specify the sequence and order various risk treatments are to be integrated and implemented. As outlined in ISO 31000, risk treatment plans should include information regarding: proposed actions and their timeline for implementation; rationale and justification for risk treatment selections; benefits to stakeholders; responsibilities and accountabilities for their implementation; performance metrics; and monitoring and communicating results.

## Slide 38: Risk Treatment Plans
inherently safer designs
layers of protection
recognized and generally accepted good engineering practices
safer technology and alternatives
Notes: Risk treatment plans may incorporate strategies such as ‘inherently safer designs’, ‘layers of protection’, ‘recognized and generally accepted good engineering practices’ and ‘safer technology and alternatives’ selected according to the hierarchy of controls.
Used in the chemical processing industry, Inherently safer design is a concept that requires designers to attempt to eliminate or reduce hazards that are identified at each stage in the system’s life cycle, and design safety systems to control hazards rather than accept them.
The use of layers of protection or risk treatment (discussed earlier) is a concept whereby several independent devices, systems, or actions are provided to reduce the likelihood and severity of an undesirable event.
Introduced in 1992 by OSHA in the process safety management (PSM) standard, Recognized and generally accepted good engineering practices or RAGAGEP involves the selection and application of appropriate engineering, operating and maintenance knowledge when designing, operating and maintaining chemical facilities with the purpose of ensuring safety and preventing process safety incidents.
Safer Technology and Alternatives or STAA is the concept of integrating various risk reduction strategies that work toward making a facility and its chemical processes as safe as possible that is used by EPA.

## Slide 39: The Concept of Residual Risk
Residual risk is the risk remaining after ‘risk treatment’.
Risks that remain after an assessment and treatment should be continually monitored and assessed for secondary risk, hidden risk, or previously undiscovered risks.
Notes: Residual risk is the risk remaining after ‘risk treatment’. It is also known as ‘retained risk’ (ISO Guide 73, 2009) and can contain unidentified, unknown risk as well. The concept of residual or ‘remaining’ risk is important to understand when managing risks both internally and externally. Risk and its management are ‘dynamic’ in nature, and continue beyond the initial risk treatment, similar to continual improvement. For this reason, risks that remain after an assessment and treatment should be continually monitored and assessed for secondary risk, hidden risk, or previously undiscovered risks. Following the implementation of risk treatments such as risk avoidance, elimination or risk control, the residual risk should be evaluated to verify that it is acceptable to the organization.

## Slide 40: Treating Risk throughout the Continuum
Figure 10.9, The Risk Continuum
Notes: Risks will change with the variables, conditions, or risk drivers affecting it and will change over time. Risk can be viewed as being in a continuum depending upon its point in the risk management cycle. For this reason, risk must be continually managed and treated as it evolves or changes in the organization. Existing, new or emerging risks as well as those risks that have been previously treated should be continually monitored and assessed. An illustration of the risk continuum which includes inherent or untreated risk, initial risk, secondary and residual risk and future state risk is shown here.

## Slide 41: Treating Risk throughout the Continuum
Notes: Emerging Risks
New risks are created from new risk sources introduced into the system and can also develop and emerge from new technologies, activities, or expansions into different areas which requires scanning, detecting and monitoring. Such emerging risks can come from known risks that previously were not considered a threat (pure risks) or opportunity (speculative risks), however, have increased in new or unfamiliar way that has a potential to effect objectives. Detection systems should be in place to identify and monitor their development.

## Slide 42: Treating Risk throughout the Continuum
Notes: Inherent Risk
Inherent risk is described ‘as the risk to an entity apart from any action to alter either the likelihood or impact of the risk’. It is the ‘untreated risk’ that resides and existing in the system before any risk management is applied. With new acquisitions, systems or activities there are associated inherent risks which require assessment and management. Inherent risks are derived from risk sources, risk drivers, and potential exposures associated with the endeavor or system.

## Slide 43: Treating Risk throughout the Continuum
Notes: Initial Risk
Initial risk is defined as ‘the first assessment of the potential risk of an identified hazard. Initial risk establishes a fixed baseline for the hazard’. It is estimated and determined in the initial risk assessment and can be considered a ‘baseline’ risk level. The initial risk level considers the effectiveness of existing controls and is used to determine whether further risk treatment is required.

## Slide 44: Treating Risk throughout the Continuum
Notes: Residual Risk
Since risk cannot be completely eliminated, there will always be some ‘residual risk’. ‘Residual risk’ is the risk level that remains after applying the selected risk treatments from the initial risk assessment. Residual risk can also include previously unidentified or hidden risks, secondary risks, knowingly retained risks, shared risks or transferred risked.

## Slide 45: Treating Risk throughout the Continuum
Notes: Future State Risk
Future state risk is the estimated risk level expected from the application of prescribed risk controls. Future state risk is used to show a measure of risk reduction or risk reduction percentage (RR%) for a proposed control compared to the current risk level or initial risk level. When proposing additional control measures for a current risk level, a “future state” risk level is estimated considering new control measures’ anticipated effect in risk level.

## Slide 46: Treating Risk throughout the Continuum
Notes: Secondary Risk
As previously mentioned, risk treatments can inadvertently cause new risks or increase existing ones. A secondary risk is a risk that arises as the result of implementing a risk treatment or control measure. If the risk treatment was not taken, the secondary risk would not exist.
The creation of secondary risks or ‘side-effects’ must be carefully considered when selecting and developing risk treatments. The potential for secondary risks should be assessed when considering the various risk treatment options, anticipating and identifying possible unintended affects or interferences with other controls. Ongoing monitoring and reviewing of treatments should be performed to detect and correct any additional risks that might develop or be created. Proposed risk treatments that pose a potentially high secondary risks may be disqualified from consideration if the secondary risk falls outside of the project risk tolerance.

## Slide 47: Methods for Selecting Risk Treatment
Figure 10.10, Risk Management Process and Risk Treatment Techniques
Notes: There are multiple methods and tools available to can be used to select and justify risk treatment options as illustrated in Figure 10.10. ISO 31010 and other standards provide some guidance on such methods and their use.

## Slide 48: Methods for Selecting Risk Treatment
Table 10.1, Risk Treatment Selection Methods
Notes: There are many methods available for evaluating and selecting risk treatment strategies. Some of these have been previous discussed.
Cost benefit analysis is a simple method of weighing the expected costs with the expected benefits to determine the most profitable option.
Multi-criteria analysis uses a range of criteria to compare the performance of options.
Financial and non-financial benefits analyses are used to analyze monetary values as well as those benefits that can not be easily tied to financial numbers such as reputation, or public image.

## Slide 49: Methods for Selecting Risk Treatment
Table 10.1, Risk Treatment Selection Methods
Notes: Other methods include:
Business impact analysis which is used to analyze potential effects of interruption to business commonly used in business continuity planning.
And other financial methods listed here.

## Slide 50: Summary
Risk treatment
most important step in risk management
an iterative approach to selecting the most appropriate risk treatments
the process of modifying risk to an acceptable level
Notes: Risk treatment, the process of modifying risk to an acceptable level is the primary reason to assess risk.
It is considered the most important step in the risk management process.
Without treating risks that have been assessed, a risk assessment is of little value to an organization.
An iterative approach to selecting the most appropriate risk treatments should be part of the risk management process.