## Slide 1: Assessing and Managing Risk: An ERM Perspective
Chapter 13
Practical Applications of Risk Management Methods: Part 1
Developed by Bruce Lyon, CSP, P.E., SMS, ARM, CHMM
Dr. Georgi Popov, CSP, QEP, ARM, SMS, CMC, FAIHA
Notes: The purpose of this chapter is to demonstrate how risk management principles and methods can be put into practice within each process step. We will demonstrate this through the use of a number of case studies using practical applications of various risk management methods.
As we will demonstrate, it is important to modify and combine selected methods to properly address risks in their work environments. In this module, you will learn how risks are assessed through the process of risk identification, risk analysis and risk evaluation. You will also learn how the risk assessment process is aligned with OSH goals with the ERM model. We will introduce case studies and examples to reinforce deeper learning. Let’s get started.

## Slide 2: Part 1 – Applying Methods for Establishing Context and Assessing Risk
Notes: This chapter presentation is broken up into four sections including the first steps in the risk management process including:
Establishing the Scope, Context and Criteria
Identifying Risk
Analyzing Risk
And Evaluating Risk.
In the second part, we’ll cover the remaining sections of the risk management process using case studies.

## Slide 3: Establishing Context and Assessing Risk
Notes: As we discussed earlier in the course, the risk management process begins with establishing the scope, context and criteria. These are critical elements that must be well defined and understood to guide the risk management process. As shown in the figure, risk management is an ongoing process and requires the assessor to revisit the context periodically to ensure it is current, valid and effective.

## Slide 4: Methods
Notes: As shown here, there are a number of methods available, some of which are more appropriate for certain steps in the risk management process. Most if not all can be used in various stages of the risk management process with a great deal of overlap as demonstrated in the following sections and case studies. These are only suggested applications and should not limit the assessor from considering their use in other areas.
As we discussed in the first module, Risk is fluid and therefore, its management must also be fluid and ongoing. The examples that we will discuss are designed to provide you with ideas on how some methods can be applied throughout the risk management process, acknowledging that there are many different ways of identifying, analyzing, assessing, and treating risk.

## Slide 5: Establishing Context
Notes: In the planning process before the risk assessment can be conducted, the context must be established. There are many considerations necessary when setting the parameters of a risk assessment including its scope, purpose, variables, limitations, risk criteria, resources, and stakeholders, among other elements. As discussed in Module 1, Lesson 3 Planning the Assessment, various methods can be used to establish the context and plan the assessment. Some of these methods such as selecting risk criteria, risk assessment matrices, and defining acceptable risk and risk action levels are covered. Here, we’ll provide several additional examples of methods including:
Pareto analysis
Radar or spider charts and
SWOT Analysis.

## Slide 6: Pareto Analysis
Establishing Context
Notes: Pareto analysis or Pareto charting is a method used to identify and evaluate factors that contribute to the greatest frequency of unwanted outcomes displayed in a diagram or chart. It is considered a data analysis tool which is based on Italian economist Vilfredo Pareto who in 1906 observed that 80 percent of the land in Italy was owned by 20 percent of the population thus creating the 80/20 rule.
The Pareto principle states that 80 percent of the impact of the problem will show up in 20 percent of the causes and is referred to as the ‘Vital Few’ concept.
It is most useful as a method to analyze and select among multiple competing outcomes or options at an operational level.
Specifically, it is used to prioritize elements or areas of focus when establishing the context and planning risk assessment.
For example, risk professionals may use Pareto Analysis to screen, analyze and select which hazards cause most costly losses or which operational issues are most significant and in need of assessment and treatment.

## Slide 7: Pareto Analysis
13.2, Pareto Chart Example
Establishing Context
Notes: In the example presented here, an auto supply company analyzed the types of injuries and the associated average cost per injury type. The first two causes (back injuries from overexertion, and strains from pushing and pulling) contribute to 80% of the direct costs of the workplace injuries. In the second lesson of this module, we will see how this company was able pinpoint where they have concentrated their efforts to reduce their hazard, operational, financial and strategic risks by using the Pareto analysis method.

## Slide 8: Radar Chart
Establishing Context
Notes: Next, a radar chart or spider chart can be used to visually illustrate the differences between categories.
A radar chart is a graphical method of displaying multiple variates of data in a two-dimensional chart with three or more quantitative variables represented on axes (or spokes) starting from the center point and radiating outward much like a spider web.
Each spoke has a graduated data length proportional to the variable for each data point and consistently proportioned across all data points.
A line is drawn connecting the data values for each spoke which gives the plot a star-like appearance.
Radar charts are suited for showing outliers and commonality, imbalances among chart variables.

## Slide 9: Radar Chart
Figure 13.4, Risk Management Radar Chart Example
Establishing Context
Notes: In this example, the Radar Chart shows risk management related variables including:
OSH Management System,
2) Quality Management,
3) Hazard Risks,
4) Operational Risks,
5) Financial Stability, and
6) Strategic Risks.
Each category has data points plotted on their axis/spoke and connected to create the star-shaped polygon graph. The OSH Management System is visually displayed as deficient in comparison with the other variables providing an indication that efforts in this area will be most appropriate.

## Slide 10: SWOT Analysis
Establishing Context
Notes: Another method that can be used to establish the context is a SWOT analysis. SWOT is an acronym for Strengths, Weaknesses, Opportunities, and Threats.
A SWOT analysis is a strategic planning method used to help an organization identify its strengths, weaknesses, opportunities, and threats related to achieving business objectives or project planning. Strengths and weakness are generally internal, while opportunities and threats typically come from the external environment. A typical SWOT analysis uses a matrixas as shown here to identify the various categories which can then be rated or ranked.

## Slide 11: SWOT Analysis
Figure 13.6, SWOT Category Ratings
Establishing Context
Notes: The categories can be subdivided into risk categories with risk ratings from 1 to 5 as shown here. Note that for Strengths and Opportunities a rating of 5 is the most beneficial outcome, while for Weaknesses and Threats, the highest value is the most negative outcome. These categories/rankings are somewhat subjective; however, they provide a way to visualize and rank the results. Let’s take a look at how a SWOT analysis can work using an example.

## Slide 12: SWOT Analysis
Figure 13.8, SWOT with Ratings
Establishing Context
Notes: In this example, the organization has a patent that expires in two years, and ships most of the product to another country. The organization has difficulties hiring and retaining talented employees due to significant number of shoulders, neck, and back injuries/disorders. By the time the packaging employees are trained and productive, they complain about shoulders and back pain. Due to low unemployment rate in the area, HR informed upper level management that they have to increase the hourly rate by 3 US dollars per hour. However, due to recently imposed tariffs by the receiving country, ABC Supply cannot afford to increase the hourly rate. In addition, the US dollar declined in value relative to the other currency. That creates additional financial pressure.
Fortunately, ABCs Research and Development department created a new formulation that will reduce the size of the individual packages and increase productivity. The new product will increase crops yield by 15%. No such product exists on the market. In addition, our engineering department in collaboration with the risk manager had developed a plan to completely redesign the current operation. It is estimated that the new operation will reduce the MSDs by 75%.
A SWOT analysis can be completed for this situation. First the top two or three benefits or negative effects for each category are selected and entered into the spreadsheet. Each SWOT element identified is rated on the 1-5 scales presented here. The ratings are automatically averaged for each category.

## Slide 13: SWOT Analysis
Establishing Context
Notes: To further demonstrate the use of customized and combined methods, the authors developed a simple four variables ‘radar chart’ based on the ‘SWOT analysis’. The average rate for each category is transferred to the radar chart. The radar chart here is a good visual representation of the SWOT analysis results. With these results, the scope and purpose of the risk management effort are better defined. Many other methods are used to develop and establish the context and risk criteria including brainstorming, Delphi Technique, Nominal Group Technique, and other methods of reaching consensus and identifying key risk indicators. The important point is that risk assessors know the fundamentals of various methods, and which methods can be useful in the specific application.

## Slide 14: Identifying Risk
Notes: Once the context is established with a defined scope, purpose and criteria, the risk assessment can be performed. As we have discussed, the first step of risk assessment is identifying risks. This includes identifying the risk sources, existing controls, exposures, risk drivers, and causes or failure modes, as well as the potential consequences they could impose. There are a number of risk identification methods available as previously discussed. In this section, several additional methods are reviewed using a case study that include:
Trending analysis
incident mapping,
barrier analysis (for existing controls),
change analysis,
five why analysis and multiple five why, and a
causal factor tree diagram.

## Slide 15
Figure 13.10, Number of fatal work injuries by employee status
Trend Analysis
Identifying Risk
Notes: As risk management efforts continue to make progress in reducing injuries and illnesses, their remains a serious concern - the number of fatalities and serious incidents (FSI) events that occur each year. In fact, the numbers for fatalities are trending upward. Recent numbers cited by BLS indicate a total of 5,147 workers died from an occupational injury in 2017. BLS published a new interactive tool that visualizes the number of fatal work injuries by employee status. The latest available data is presented here and it shows an alarming increase of fatal work injuries from 2013 to 2017. Using such trending analysis is commonly used to identify leading categories or causes in incidents as a first step in risk identification. Once the categories or causes are ranked, the priority issues can be further investigated as we will discuss next.

## Slide 16: Identifying Risk - Case Study
Figure 13.11, Forklift operating between pipe rack and manifold
Notes: Let’s examine a specific incident to demonstrate how risks and their causal factors can be identified.
At the ABC Drilling Rig Site, around 4:05 pm on a Friday the work crew were about to “nipple up” (assemble the blowout preventer stack on the wellhead at the surface). There were three employees using an all-terrain forklift in muddy conditions to hang pipe near the catwalk. Another employee (injured party - IP) was working on a choke manifold adjacent to the forklift work approximately 15” away.

## Slide 17: Identifying Risk - Case Study
Reenactment of injured party’s leg in path of forklift and the soft mud
Notes: The operation required the forklift to maneuver between the manifold unit and the pipe rack to supply employees connecting pipe on the opposite end. As the employees were connecting pipe, the employee working on the manifold was completing his work. Once completed, the employee knelt and leaned over one of the diverter lines to reach inside the manifold unit to grab a wrench he left behind as shown in the reenactment pictured here. As he reached from a kneeling position, he extended his leg into the path of the moving forklift as it was backing.
With the employee’s leg in the direct line of the forklift tire, the forklift operator began backing up to re-position without seeing the employee. As the operator backed up, he did not know the employee was there in the path of the forklift and backed over his ankle in the soft mud. The employee screamed, notifying the operator of his presence and the forklift pulled forward.

## Slide 18: Identifying Risk – Incident Map
Notes: With the information and facts collected during the investigation, the team lays out the sequence of events and related conditions of the incident known as an incident map. Only events and conditions that lead to the incident are used. Four events were identified in this incident which included
forklift operating in congested area between pipe rack and manifold unit;
2) the injured employee was working on a manifold unit adjacent to the forklift activity;
3) the injured employee was unaware of the forklift and extended his led in the path of the forklift;
4) the forklift operator could not see the other employee when backing up.
Two conditions were identified which were
reduced visibility on the site, and
2) muddy conditions which reduced the severity of the injury.

## Slide 19: Identifying Risk – Incident Map and Barrier Analysis
Barrier Legend
Notes: After completing the incident map, a barrier analysis of available controls is performed. Using the color-coded legend, controls are labeled, placed in the map and connected to the affected events and/or conditions as shown here. The barrier legend shown here has five different conditions that can apply to an existing barrier or control including:
Green – existing control functioned as intended
Yellow – existing control was ignored
Orange – existing control was less than adequate
Red – existing control failed
Purple – a new control is needed.
In the case study, the barrier analysis determined:
One new control - pre-job planning - is needed (the purple octagon)
Seven existing controls were ignored or not used (yellow octagons) including:
  Pre-shift briefing
  Review of the JSA
  Pre-job walk-around inspection
  Stop Work Authority
  Use of a Spotter
  Use of tool belt
  Use of High-visibility vests.
One control failed - forklift backup alarm (red octagon)

## Slide 20: Identifying Risk Change Analysis
Notes: The significant events are described and compared to what should have occurred to determine discrepancies. Using the form shown here, the most significant event from the case is described, along with existing controls, deviations that occurred causing the control to be ineffective, the underlying causal factors tied to the deviation, and actions necessary to address the underlying causes. It is important to consider the underlying causal factors tied to the deviation to understand what corrective actions are needed to prevent recurrence.

## Slide 21: Identifying Risk Multiple Path 5 Why Analysis
Notes: To dig down to the underlying management system causal factors, a 5 Why Analysis can be used. In this case, a Multiple Path 5 Why Analysis was used to analyze the multiple contributing causal factors that were discovered for the event as shown in here. Similar to a singular 5 why, a multiple path method can uncover various factors that can contribute to an incident.

## Slide 22: Identifying Risk Causal Factor Tree
Notes: To further link causes to their underlying roots, a causal factor tree can be constructed. The incident’s causal factors are broken down and traced back to the management level elements using a causal factor ‘fault-tree’ diagram shown here. Along with the diagram, a report narrative is provided to management. The report describes the facts of the incident, the events and conditions, the performance of control measures, and the recommended actions that will address direct causes, intermediate causes, and most importantly, the management-level causal factors.
As a result of the analysis, several key management system level causal factors were uncovered. Those included:
a ‘lack of planning’,
‘lack of consistent enforcement of rules and lack of accountability’,
‘lack of effective communication’, and
‘inconsistent or ineffective preventive maintenance, auditing, and reporting.’
There are many other methods that can be used to identify risk. Methods such as checklists, preliminary hazard lists, hazard identification studies or HAZIDs, among can be considered when selecting the proper methods for the application.

## Slide 23: Analyzing Risk
Notes: Once the risk has been identified, it is analyzed. Risk analysis, the second step in risk assessment, is used to estimate the risk level, and is the input for the risk evaluation step. In this section, we will review the differences between hazard analysis, risk analysis and risk assessment. We will continue our case studies using a traditional ‘what-if hazard analysis’ and modify the method to include risk estimation using a what-if risk analysis and risk matrix.

## Slide 24: Analyzing Risk
Figure 13.17, Comparison of Hazard Analysis, Risk Analysis and Risk Assessment Steps
Notes: Many methods are used in hazard analysis, risk analysis and risk assessment. As previously discussed, it is important to understand the differences in these term.
Hazard analysis only analyzes the hazard without estimating the risk.
Risk analysis goes beyond hazard analysis by analyzing and estimating both severity of consequence and likelihood of occurrence.
Risk assessment includes the elements in risk identification and analysis and compares the estimated risk levels with the established risk criteria to determine if the risk is acceptable.
We will begin our case study using a hazard analysis example.

## Slide 25: Hazard Analysis Case Study
Chlorine gas release caused by mixing sulfuric acid and sodium hypochlorite (bleach)
Notes: Our case study is a chemical release that was caused by inadvertent mixing of incompatible chemicals at a chemical processing facility as described by the Chemical Safety Board investigation. The primary facts of this incident involved:
The mixture of the two chemicals, sulfuric acid and sodium hypochlorite (bleach), which produced a cloud containing chlorine and other compounds.
The cloud impacted workers onsite and members of the public in the surrounding community.
The incident occurred during a routine chemical delivery of sulfuric acid from a chemical supplier cargo tank motor vehicle (CTMV) at the chemical facility tank farm.
The County Department of Emergency Management ordered thousands of community members to shelter-in-place and other community members to evacuate in some areas.
Over 140 individuals, including members of the public, employees of the chemical processor, and a chemical supplier employee, sought medical attention; one employee and five members of the public required hospitalization as a result of exposure to the cloud produced by the reaction.

## Slide 26: Case Study
Chemical unloading operations at the time of the incident (Source: MGPI)
Notes: While two specific substances were involved in this incident, the accidental mixing of many acids and bases or other incompatible chemicals during unloading operations and other activities can lead to potentially dangerous reactions. Chemical unloading operations from chemical supplier cargo tank motor vehicles (CTMVs) may be perceived as simple compared to other processes in fixed facilities, but because these operations can involve extremely large quantities of chemicals, the consequences of an incident may be severe.
As described in the CSB report, the chemical delivery drivers rely on local operators to unlock and identify the fill line designated for the chemical being transferred. Operators then show drivers the appropriate fill line. Once the equipment is unlocked, operators return to the control room. Drivers then remove the dust cap and connect their chemical discharge hose from the cargo tank to the fill line. Note that both connections for the sulfuric acid and sodium hypochlorite look the same and they were very close to each other.

## Slide 27: Case Study
Figure 13.18, State of connection area
Notes: The CSB found that the proximity of the sulfuric acid fill line to the sodium hypochlorite fill line increased the likelihood for an incorrect connection during chemical unloading. The five chemical fill lines in the Mod B chemical transfer area were all located near each other; significantly, the sodium hypochlorite fill line was about 18 inches from the sulfuric acid fill line. In addition to the incompatibility of sodium hypochlorite and sulfuric acid, the other chemicals delivered to the process unit - presented reactivity hazards if mixed. Let’s review the risk pathway next.

## Slide 28: Case Study – Risk Pathway
Chemicals
Communication
Operators and Local Population
Mixed connection
Chlorine Release
Hospitalizations, Lung damage, Property Damage,
EPA & Legal Fees >$2M, Reputation damage
Notes: Risk is derived from its risk source (i.e. hazards, operations, etc.) and influenced by risk drivers.
In this case the chemicals are the risk source.
The risk driver is the poor communication between the operator and the driver.
Plant operators and the local population could be exposed in case of chemical release.
The trigger event is the mixed connection.
Risk treatments are designed to maintain control of the risk and prevent exposure to assets or objectives.
When a loss of control occurs from a trigger or cause, exposure to the risk source results in an incident (like in this case study).
The incident is the Chlorine gas release. It should be noted that Chlorine was the first Chemical Warfare Agents used during WW I.
A simplified relationship of elements within the risk pathway is represented in the Figure here. Although the illustration is linear, risk is often multi-dimensional and must be considered as such.

## Slide 29: Case Study – What If
Imagine if the company had conducted a traditional ‘what-if analysis’ and asked:
What-if it were possible to mis-match connections?
What if an operator inadvertently connects the wrong chemical while filling tanks?
What if the operator had noticed that lines were mixed and was able to shut down the supply line on time?
What if only minor quantities of Chlorine gas were released?
Notes: “What-if’ is a powerful question when used in a risk assessment approach. The concept of using the what-if question to determine potential effects is important and fundamental to assessing and controlling risk. It is essentially reasoned curiosity for the purpose of discovery to reduce uncertainty. Some of the benefits of using what-if analysis technique are that it is easy to use, employees with little risk assessment expertise can participate meaningfully, and it leads to deeper insight, especially for those conducting the analysis.
Regarding the case study, imagine if the company had conducted a traditional ‘what-if analysis’ prior to the incident and asked:
  What-if it were possible to mis-match connections?
  What if an operator inadvertently connects the wrong chemical while filling tanks?
  What if the operator had noticed that lines were mixed and was able to shut down the supply line on time?
  What if only minor quantities of Chlorine gas were released?
Asking the right questions early in the process is key to avoiding such incidents.

## Slide 30: Case Study – What If
Figure. 13.19, Traditional ‘what-if analysis’ – mixed connections
Notes: Let’s take a look at a traditional ‘what-if analysis’. The method typically a worksheet that includes columns for selected “what-if” questions and their related consequences, causes, controls and recommended actions such as the one presented here.
Regarding the chemical release incident, a ‘what-if analysis’ of the system prior to the event could have helped identify and prevent some of the causes to the incident, however, a traditional ‘what-if analysis’ has certain limitations and possible deficiencies. For example, an inexperienced facilitator may not ask the right questions or lead the team to brand the findings as a “near miss” and recommend better procedures and additional training.
A more experienced facilitator would ask more revealing questions regarding ‘how’ and ‘why’ such events could occur. The facilitator may consider what-if questions where the consequences from the previous what if question would become the next what-if question exploring the potential cascading effects, much like a ‘5 Why Method’.
A question might be: What if Chlorine gas was released? The consequences might be a Clean Air Act violation and EPA fine of up to $1.7 million. Such consequences of a $1.7 million fine and severely damaged reputation of the organization might be considered catastrophic. In the CSB case, both companies were indicted by the U.S. Attorney’s office for violations of the federal Clean Air Act (CAA) and if convicted, are looking at fines of up to $1.7 million.

## Slide 31: Case Study – What-If Risk Analysis
Notes: A traditional What-If Hazard Analysis usually does not include a risk level estimation. By including an estimation of likelihood and severity, the risk level can be estimated.
If the control measures are less than satisfactory, the team further considers risk treatment tasks and potential controls are defined. It is normal to use a qualitative or semi-quantitative risk assessment method to rank the actions created in terms of priority. (ISO 31010). To estimate risk levels based on the possible consequences, risk professionals can add severity of consequences, likelihood and risk level columns to the traditional what-if analysis. To demonstrate the additional risk assessment steps, a simple 5x4 risk assessment matrix can be used.

## Slide 32: Case Study – Matrix, Risk Factor Levels and Actions
Risk Level | Risk Score | Action
Very High | 12 or greater | Operation not permissible, stop work; immediate action required
High | 8 to 10 | Remedial action required; high priority
Moderate | 4 to 6 | Remedial action suggested
Low | 1 to 3 | Remedial action discretionary
Notes: To estimate risk, defined risk factor levels for likelihood and severity are need as shown in the two tables along side the risk matrix. By combining the risk factors a risk level is estimated as shown in the matrix. Risk levels and their required actions are defined and provided in the blue table.

## Slide 33
Semi-Quantitative What-if Risk Analysis
Notes: Using a what-if risk analysis for our case study, we begin with ‘what if’ questions such as ‘what if the operator mixes sulfuric acid and sodium hypochlorite connections?’, the answer might be ‘Chlorine gas generation’. The causes may be found in the design of the filling ports and filling nozzles. If it is possible to inadvertently insert and fill the wrong chemical into a tank, an unwanted event is possible. The designers could have considered incompatible connections for these two chemicals. Imagine if the only control of preventing this event is to rely on human verbal communication for two fill lines. Would this be considered an effective control measure? The likelihood of mixing the lines with only human verbal communication could be estimated as “Probable” or a risk factor of 4, with the consequence severity at “Critical” or a risk factor of 3. With a likelihood of 4 and a severity of 3, a risk level of 12 is determined on the 5x4 risk matrix which is considered an unacceptable risk level.
Not surprisingly, the risk levels for all three scenarios are in the High-risk category.

## Slide 34: Evaluating Risk
Notes: The final step in risk assessment is risk evaluation. As discussed in module 2, risk evaluation is used to compare the estimated risk with the established risk criteria to determine whether the risk is acceptable or if it requires treatment. We will continue our case study using several risk evaluation methods including a structured what-if risk assessment, the ALARP graph, and the established risk criteria and matrix to compare and determine required actions for each risk.

## Slide 35: Evaluating Risk
Notes: Following the risk analysis, a judgement is made whether the estimated risk is acceptable or if it requires some form of risk treatment.
Continuing with the CSB investigation of a chemical release, a Structured What-if Risk Assessment is used to illustrate risk evaluation as part of a full risk assessment. A Structured what-if risk assessment or SWIFRA is a modified what-if analysis that includes columns for risk analysis and risk evaluation, as well as recommended treatments and a projected future state risk level based on the recommended treatments. By providing a current state risk level and future state risk levels along with a risk reduction percentage, decision makers can visually compare the potential risk reductions.

## Slide 36: Summary
Notes: We have applied several different methods throughout our case studies for the first two steps of the risk management process: establishing the context, and performing the risk assessment. In the next lesson, we will continue our case studies for the following four steps of the process.

## Slide 37: Evaluating Risk
Notes: Looking at the first question, ‘what-if the operator mixes the chemical connections?’ the resulting consequence of a Chlorine gas release is estimated to have a risk level of 12. We can see that on the established risk matrix, a risk level of 12 is ‘high’ and ‘not allowed’ or in other words, unacceptable. Remember, the risk matrix and defined risk criteria are established upfront by the organization before the assessment for the purpose of measuring and evaluating risks consistently within the organization.

## Slide 38: Evaluating Risk
Notes: For risk levels that are unacceptable, work must immediately stop until they are reduced. The ALARP model shows how risk level categories can be divided into layers with associated actions. The blue table provides a more detailed guide for actions for each risk score. Each organization will define these categories based on their own criteria, industry, culture and stakeholders.
For our case study of the Chlorine gas release, the operation is not permissible and must immediately be halted until corrective action is taken to reduce the risk level.

## Slide 39: Evaluating Risk
Notes: Here we see the SWIFRA with the three ‘what-if’ questions from our case study. All three concerns are estimated with risk levels between 12 and 16 which have evaluated as unacceptable according to our risk evaluation shown in the circled area. Each risk will require immediate risk treatment to reduce the risk to ALARP, which we will cover in the next lesson.