## Slide 1: Assessing and Managing Risk: An ERM Perspective
Chapter 13
Practical Applications of Risk Management Methods: Part 2
Developed by Bruce Lyon, CSP, P.E., SMS, ARM, CHMM
Dr. Georgi Popov, CSP, QEP, ARM, SMS, CMC, FAIHA
Notes: The purpose of this chapter is to demonstrate how risk management principles and methods can be put into practice within each process step. We will demonstrate this through the use of a number of case studies using practical applications of various risk management methods.
As we will demonstrate, it is important to modify and combine selected methods to properly address risks in their work environments. In this module, you will learn how risks are assessed through the process of risk identification, risk analysis and risk evaluation. You will also learn how the risk assessment process is aligned with OSH goals with the ERM model. We will introduce case studies and examples to reinforce deeper learning. Let’s get started.

## Slide 2: Part 2 – Applying Methods for Treating, Monitoring, Recording and Communicating Risk
Notes: In this Chapter 13 Part 2, we will apply risk management methods to the final steps in the risk management process including:
Treating Risk
Monitoring Risk
And Communicating Risk.

## Slide 3: Treating Risk
Notes: Risk treatment is the action taken following the risk assessment to reduce and manage risks. Without it there is no value in assessing risks. We will review several methods used in selecting and treating risk using several case studies as examples.

## Slide 4: Treating Risk
Hierarchy of Risk Treatment Model
Notes: As previously discussed, the hierarchy of risk treatment model (shown here) should be used when selecting risk treatments. Higher level treatments which are more effective should be first considered in an effort to achieve risk that is ‘as low as reasonably practicable’ or ALARP.

## Slide 5: Layers of Control
Notes: Also, it is rare that a single risk treatment is adequate in reducing and managing risk. Most often, layers of treatments are needed.
In the chemical processing industry, this concept is referred to as layers of control or protection. Layers of protection are constructed with ‘independent protection layers’ or IPLs. An IPL is defined as a device, system or action capable of preventing an event or exposure from occurring that is independent from other controls and is verifiable or auditable for effectiveness. In other words, IPLs are considered physical barriers or devices (typically engineering controls) that prevent the ‘initiating cause’ of an event from proceeding to an unwanted consequence.
The use of layers of control is illustrated here with:
design-level controls (prevention through design) in the center, and additional layers extending out including
prevention controls (in the green circle),
protection controls (in the blue circle) and
mitigation controls (the outer red circle).

## Slide 6: Layers of Control
Notes: This concept is further illustrated in James Reason’s Swiss cheese model shown here. Reason postulates that all workplace accidents have at least three common features: 1) hazards, 2) failed defenses and 3) losses.
Of these three features, the ‘failed defenses’ offer the greatest potential for risk reduction improvement.
Controls can exist at many levels and take a variety of forms; however each control serves one or more of the following functions:
to create understanding and awareness of the hazards;
to give guidance on how to operate safely;
to provide alarms and warnings when danger is imminent;
to place barriers between the hazards and the potential losses;
to restore the system to a safe state after an event;
to contain and eliminate the hazards should they escape the barriers and controls; and
to provide the means of escape and rescue should the defenses fail catastrophically.

## Slide 7: Chlorine Gas Release Case Study
Notes: Let’s continue our review of the Chlorine gas release case study.
In the previous lesson, we performed a risk assessment of the chemical release incident using the Structured What-if Risk Assessment or SWIFRA model. In the case study, the risk assessment identified ways that the risks could be reduced, both from a likelihood of occurrence, and severity of impact.

## Slide 8: Treating Risk
Figure 13.27, SWIFRA with proposed controls
Notes: Following the risk evaluation, the risk assessment team considered additional controls using the hierarchy of risk treatment. The proposed controls were listed in the SWIFRA and used to re-assess the risk. With the implementation of these additional layers of controls, the updated SWIFRA may look like the one presented here. Notice how we can estimate % risk reduction if we use semi-quantitative risk assessment ratings. Now, let’s review the proposed risk treatments.

## Slide 9: Treating Risk
Additional Layers of Control for the Chemical Filling Operation
Vertical Striped Bow Tie Diagram
Notes: In our case study, special focus was placed on the chemical unloading lines, transfer valves, transfer piping, tanks, and associated equipment.
Looking at our vertical striped bow tie model, we see the layers of new risk treatments from top to bottom. The top layers are preventive in nature, while those that follow the event are mitigative. The proposed actions include:
Removing the acetic anhydride process entirely, reducing the overall amount of flammable liquids which are example of elimination, and minimization.
Upgrading chemical unloading and transfer equipment with chemical portal separation, signage, unique locks, and fittings which are examples of redesign, passive engineering, warnings, and administrative controls.
Upgrading transfer equipment systems, an example of active engineering.
Implementing an innovative key control and chemical unloading sequences, examples of administrative controls.
Conducting Process Hazard Analyses (PHAs) of chemical processes, an example of administrative control.
Installing an automated detection and shutdown system for over pressurization, which is a mitigative engineering treatment.
Upgrading monitoring, detection and warning equipment, an example of mitigative warnings.
Adding upgraded emergency shutdown devices, examples of mitigative engineering, and
Installing additional emergency supplied air packs along the egress path, which are mitigation PPE controls.

## Slide 10: Treating Risk
Unique fill line shapes and sizes to avoid mis-matching chemicals during deliveries
Notes: One treatment designed to specifically prevent mis-matching of chemicals during deliveries is the installation of unique fill line connectors in the filling process as shown here. As we can see, each filling portal has a unique shape and size that only allows the matching connection to fit and attach.

## Slide 11: Treating Risk
Additional Layers of Control for the Chemical Filling Operation
Notes: To further illustrate how these new layered treatments will function, we have placed the treatments within the risk pathway model. The treatment layers include:
Design-level controls such as removing the acetic anhydride chemical process affect the risk source and are the most effective. These are considered preventive.
Design and engineering controls such as redesigning the portal fittings to only accept the correct chemical affect the risk drivers and are the next best risk reduction treatment and are also preventive.
Moving the control console away from the tank farm is a redesign measure to distance employees from the potential event; and installing a key control unloading sequence affect the exposure.
Remote shutdown systems are engineering controls that detect pressure and stop the flow of chemicals to prevent a release affecting the trigger or cause.
Should these preventive measures fail and the incident occurs, mitigative measures including an automatic monitoring, detection and warning system, emergency shutdown, emergency response, supplied air packs affect the impact of the consequences.

## Slide 12: Metal Dust Explosion Case Study
Notes: Now let’s take a look at our next case study. Here we will examine a metal dust explosion investigated by the CSB that resulted in three fatalities and one serious injury, fire damage to the building and closure of the plant.

## Slide 13: Metal Dust Fire Case Study
Metal Blender
Notes: In this case study, the CSB determined that the explosion likely initiated when particulates ignited in the blender that was processing zirconium. Sparks or heat produced by metal-to-metal contact between the blender blades and the blender sidewall ignited the zirconium. Mechanical impacts, such as the blender blades against the sidewall, can produce sparks (ignition source) where metal to-metal contact occurs. In rotating machinery, repeated impacts can result in hot spots with temperatures high enough to result in ignition.
Employees noted mechanical problems with the blender days before the explosion. Blender paddles were striking the sidewall and scoring the housing. To address these problems, maintenance adjusted the blender blades to increase clearance from the blender wall, but the problem returned. Maintenance then decided to replace parts of the blender. While disassembling the blender, they discovered a large groove cut in the shaft and an 8-inch to 12-inch crack in the sidewall of the blender, most likely caused by the paddle blades scraping the sidewall. The maintenance worker welded this crack, and operators continued to use the blender.
On the morning of the incident, an operator requested that maintenance replace a worn paddle in the blender. Maintenance retrieved a paddle from an old blender and attached it to the blender two hours before the incident. The maintenance performed on the blender only temporarily addressed the metal-to-metal contact. The company did not repair or replace the blender to avoid exposing combustible metal dusts to sparks or heat produced by the mechanical impact from the paddles.

## Slide 14: Metal Dust Fire Case Study
Fire Triangle
Dust Explosion Pentagon
Notes: Like all fires, a dust fire occurs when fuel (the combustible dust) is exposed to energy (an ignition source) in the presence of oxygen (typically from air). Removing any one of these elements of the classic fire triangle eliminates the possibility of a fire. A dust explosion requires the simultaneous presence of two additional elements: dust dispersion and confinement. Suspended dust burns rapidly, and confinement enables pressure buildup. Removal of either the suspension or the confinement element can prevent an explosion, although the CSB notes, a dust fire can still occur.
In this case, four of the five elements were continually present:
The combustible zirconium dust being generated in the blender,
Dust dispersion created from the blending action
Dust confinement within the blender and
Oxygen
With the addition of an ignition source from the metal-to-metal contact, the dust explosion pentagon is complete

## Slide 15: Metal Dust Explosion Case Study
Modified What-if Risk Assessment
Notes: Here we have a modified what-if risk assessment to assess the risks in the metal dust explosion. Considering that there were relatively few existing controls, none of which were sufficient to prevent the incident, the risk levels for each what-if question were very high and unacceptable. As a result, additional preventive measures were added including:
re-design of the blender to prevent metal-to-metal contact
Use of an inert gas blanket to eliminate oxygen in the blender
Improved ventilation to reduce combustible dust concentration
New housekeeping procedures
Redesign of the operation to eliminate operator exposure
In this example, likelihood and severity are reduced for all three hazards by 63% and 75%. The remaining 37% and 25% respectively may be retained if the organization assumes that the risk is within acceptable limits.

## Slide 16: Metal Dust Fire Case Study Risk Pathway
Notes: So taking the metal dust incident factors and placing them in the risk pathway model, we see:
the combustible dust as the risk source
Dust buildup, dispersion and confinement as the risk drivers
The workers, building, and business as the exposures
The ignition source as the trigger
The resulting explosion and fire are considered the incident
And the resulting fatalities, injuries, damage and business loss are the consequences.

## Slide 17: Metal Dust Fire Case Study Risk Pathway and Layers of Controls
Notes: Now let’s apply recommended risk treatment layers selected according to the hierarchy of risk treatment to the risk pathway model. This helps illustrate were certain controls are used and how they function in terms of their preventive or mitigative effects.

## Slide 18: Risk Treatment Assessment Methods
Notes: For selected risk treatments, it is important to analyze and assess their effectiveness in reducing risk to as low as reasonably practicable. Several methods that can be used to assess risk treatments are:
Barrier analysis which we previously reviewed in our previous lesson,
Bow tie analysis and striped bow risk assessment
Layers of protection analysis or LOPA
Layers of control analysis.

## Slide 19: Striped Bow Tie Risk Assessment
Notes: First, let’s look at a striped bow tie risk assessment diagram. It is similar to a traditional bow tie, however, it includes risk estimation and layers of control for assessing a particular event. One of the benefits of this method is that it communicates the risk pathway and the individual risk treatments in one diagram. By considering the preventive risk treatments and mitigating treatments using a hierarchy of risk treatment stratification, risk assessors can make a case for higher level controls with decision makers.

## Slide 20: Layers of Protection Analysis
Notes: Layer of protection analysis or LOPA is a special form of event tree analysis, which is used to analyze existing or proposed protective layers.
The main purpose of LOPA is to ensure that there is an appropriate layer of protection against the accident scenario. Scenarios may require one or more layers of protection depending on the complexity of the process and the severity of a consequence. For the given scenario, only one layer of protection must work to prevent consequence.
Typically, a high-consequence scenario – which usually involves a combination of equipment and human failures – is identified during a qualitative hazard evaluation, such as a Process Hazards Analysis (PHA) or a Hazard and Operability study (HAZOP). LOPA is then implemented for a closer, more careful assessment of this scenario. LOPA is a quantitative screening tool which provides a consistent, objective, and defensible approach.

## Slide 21: Layers of Control Analysis
Notes: A new method called Layers of Control Analysis takes the same concept as LOPA and applies it to both preventive measures and mitigative measures. Similar to the Stripe Bow Tie, risk treatments both preventive and mitigative, are analyzed for a top event to understand the entire risk of such a scenario.
Now that we have reviewed risk treatments, let’s discuss the next step.

## Slide 22: Monitoring and Recording Risk
Notes: A crucial part of risk management is verifying risks are properly controlled, monitoring, and reviewed, as well as documented and reported to stakeholders. These steps obviously tie into the communication and consultation aspects of risk management.

## Slide 23: Monitoring, Reviewing, Testing and Validating
test and validate outputs
reduce uncertainty and improve risk
Verify results
Notes: Part of monitoring and reviewing risk involves testing and validating of outputs from the selected risk treatments. In other words, are we getting what we expected from the implemented risk treatments. This is critical in reducing uncertainty and improving risk. Such testing is needed to verify the results of the implemented treatments. Let’s examine another case study involving an auto parts supply company.

## Slide 24: Auto Part Supplier Case Study
Notes: Now let’s take a look at our next case study. Here we will examine a metal dust explosion investigated by the CSB that resulted in three fatalities and one serious injury, fire damage to the building and closure of the plant.

## Slide 25: Auto Parts Supplier Case Study
Notes: An auto supply company operates an auto parts fulfilment center in the Midwest.
The company rents a warehouse facility for $50,000 annually.
The fulfillment center sells 25,000 auto parts per year with an average price of $50 a part.
The company’s average cost to buy the auto parts is $25 per part.
The fulfillment employees fulfill customers’ orders within the fulfillment center and perform production duties such as pick/pack orders, receive/stow product at elevated levels, ensure inventory accuracy, and unload/load trucks.
Unfortunately, during the past year, four employees suffered back injuries with an average cost per injury of $50,000 for a total of $200,000. This increase in injury costs was unexpected and affected the bottom line of the company. The company lost $125,000 that year.

## Slide 26: Auto Parts Supplier Case Study
Pareto Analysis
Notes: As a result, the risk manager constructed a Pareto Analysis and discovered that the highest loss category was ‘back injuries from overexertion’. The obvious solution was to reduce the exposure to back injuries from overexertion; however, it would require a complete redesign of the warehouse and the addition of process automation. As a result, management decided to perform a sensitivity analysis and evaluate all the options.

## Slide 27: Auto Parts Supplier Case Study
Sensitivity Analysis
Notes: Management estimated that if they increase the average auto part price, they will sell fewer auto parts. On the other hand, if they lower the price, they will sell more auto parts, but the profit margin will be significantly reduced. The risk manager was experienced in performing sensitivity analysis and developed an Excel file. A sensitivity analysis example is presented here.
If management decides to increase the price to $75 per part and assume that they will sell 15,000 parts instead of 25,000, the company will break even next year.
The obvious preference would be to keep the price constant and reduce the cost of injuries.
The sensitivity analysis shows that at the current price per auto part, $50, even if the parts sales increase to 29,000 the operation is still not profitable – in fact, they will lose $25,000.

## Slide 28: Auto Parts Supplier Case Study
Notes: A decision was made to evaluate several different branching scenarios. The risk management team decided that they could improve the operation by using robots. It was estimated that four warehouse robots would cost $500,000 and the annual payment would be $113,896 at 4.5% interest rate as shown here.

## Slide 29: Auto Parts Supplier Case Study
Branching scenario
Notes: The proposed solution will eliminate the back injuries (no manual tasks) however, it is difficult to convince management to invest $500,000 without proper analysis. Based on experience, it is better to present three or more different scenarios to management providing enough information for decision makers to understand the options.
As a result, the risk manager prepared a branching scenario with four different options: Full automation; partial automation; administrative controls and PPE controls.
Considering the current cost of back injuries at $200,000, it is estimated that fully automated operation would reduce the cost of back injuries by 80-100%. At a conservative estimate of 80% back injuries cost reduction, the expected annual cost avoidance would be $160,000.
Partially automated operation may reduce the back injuries costs by an estimated 20-50%. However, that will reduce the back injuries cost by only $40,000.
On the “lower end” of the branching scenario, we see that administrative and PPE (back belts) type of controls would be much cheaper options – only $100,000. However, the annual cost reduction would be between $10,000 and $20,000. Therefore, a longer-term financial analysis would be a good supplement to the branching scenario analysis.

## Slide 30: Auto Parts Supplier Case Study Full Automation
Notes: According to the financial analysis of the full automation option, there is a return on investment of 18% with a payback period of 3.1 years.

## Slide 31: Auto Parts Supplier Case Study Partial Automation
Notes: For the partial automation option, there is a negative return of investment of -63% with a payback period of 10.7 years.

## Slide 32: Auto Parts Supplier Case Study Administrative
Notes: For job rotation administrative measures, there is a negative return on investment of -35% and a payback period of 6.2 years.

## Slide 33: Auto Parts Supplier Case Study PPE
Notes: And finally, the analyses of the Back-Belt PPE option there is a negative return on investment of -67% with a payback period of 17.4 years. It follows the old British maxima, “I'm not that rich to buy cheap things”.
Considering the four options, full automation with a payback period of 3.1 years is the most beneficial.

## Slide 34: Auto Supply Company Case Study
Figure 13.42, Sensitivity Analysis
Notes: If the risks are further analyzed using another sensitivity analysis, it would indicate that the best option is the fully automated/robotized operation. This would also reduce the payroll by $100,000 making the operation profitable - generating $61,104 in profit as indicated in the Future state sensitivity analysis presented here.
This case study is a good example of how hazard and operational risks can become financial risks due to injury costs affecting the profitability of the organization. In addition, injury rates affect an organization’s experience modification rate or EMR. Many organizations rely on EMRs to qualify for contracts. In this case, the company was facing cancelation of contracts due to their EMR approaching 1.00.
EMRs affects much more than the annual insurance cost. Understanding and lowering EMR is essential for organizations looking to reduce insurance costs and qualify for contracts. The number of injuries, delayed orders completions, financial losses and EMR affecting the reputation of the company reflect on all four quadrants of the ERM model.

## Slide 35: Recording and Reporting Risk
Risk Registers
Risk Hierarchies
Risk Performance Measurement
Notes: The steps taken to manage risk and the resulting outcomes should be recorded in accordance with the organization’s documentation policies and reported to decision makers and appropriate stakeholders
Methods used to record risk include risk profiles, risk registers and risk logs, risk hierarchies and risk performance measurement. In addition, many organizations use software applications and spreadsheets to track risk performance, risk reduction, and the status of risk treatments.
Risk reporting is a form risk communication and critical for management and decision makers. Methods of risk reporting include dashboards, risk matrices, heat maps and key performance metrics that provide a quick view of the current status.

## Slide 36: Auto Parts Supplier Case Study Risk Register
Notes: Revisiting our auto parts supplier case study, the organization began conducting risk assessments of their operations. They used a simple Excel spreadsheet to document and track risk levels for each location and task. This risk register example includes current state risk levels and recommended additional controls with a future state risk level estimations. Such tools can be used to track progress and dedicate resources to priority areas.

## Slide 37: Risk Recording and Reporting
Combined Threat and Opportunity Matrix Example
Notes: Risk matrices can be designed to not only provide ‘pure risk’ or negative risk ranges, but also ‘opportunity or strategic’ risks such as the example provided here. Visual tools such as these should be along with more detailed and in-depth data.

## Slide 38: Monitoring Effectiveness of Decisions
Notes: An important component of risk based thinking and decision making is the ongoing monitoring and review of key performance indicators (KPIs), key risk indicators (KRIs) and effects of decisions made. The results of implemented decisions such as risk treatments can be measured and evaluated using KPIs and KRIs.
The results and their impact on the organization’s objectives can then be assessed to determine whether they are successful. If issues or problems that were not anticipated arise, specific adjustments can then be determined and implemented. The specific problems and their causes within an implementation should be identified in order to make appropriate improvements. Many of the methods described in this course can be used to identify such problems.

## Slide 39: Communicating Risk
Notes: Communication and consultation are integrated into the entire risk management process to enable effective risk dialogue with stakeholders, from establishing the scope, to assessing and treating risk, to monitoring, recording and reporting risk. Where communication is ineffective or inconsistent, problems are likely. Most risk professionals can recount events and experiences where inadequate communication led to unwanted and sometimes severe consequences.

## Slide 40: Key Practices for Risk Communication and Management
Prepare for plausible scenarios and crises;
perform formal assessments;
define the context and objective of each assessment;
understand the organization’s acceptable risk level;
assemble the best team to perform the assessment;
use the most appropriate assessment techniques;
be objective and unemotional in the assessment process;
identify risk sources that create risks and consider the whole-system risk;
consider the hierarchy of controls and failure to prioritize based on risk;
perform assessment during the design/redesign phases;
communicate before, during and after the assessment with affected stakeholders;
be timely and measured in the message; and
learn and improve.
Notes: Those involved should understand how risk-based information is communicated to decision makers and emphasize that risk assessments are conducted with the organization’s objectives in mind. Risk communication is essential for routine situations and also in times of crisis. Risk professionals must be well-versed effective risk communication principles, so they can determine how best to apply them to their own situations and needs, among all of the challenges that exists.
While every situation is different and may require a different type of response, five common elements can help in developing a risk communication plan. First,
prepare for plausible scenarios and crises;
Perform formal risk assessments
Define the context for each assessment
Understand the risk criteria and acceptable risk level
Assemble a qualified risk assessment team
Use the most appropriate methods
Be objective and unemotional
Identify risk sources and consider whole-system risk
Consider the hierarchy of risk treatment
Perform assessments during design and redesign
Communicate before, during and after with stakeholders
Be timely
And continue to learn and improve.

## Slide 41: Methods of Risk Communication
Notes: Risk communication methods should be considered upfront for emergencies and times of disruption. Such an example of a public or external risk communication may include the list of elements shown here taken from the U.S. Federal Emergency Management Agency (FEMA).

## Slide 42: Closing
The Quadrants of Risk
Notes: As we close this course, the assessing and managing of risk, both pure risk and strategic risk is vitally important to an organization’s ability to achieve their goals and objectives. Managing uncertainty and ultimately risk enables decision makers to have a level of confidence in their ability to make better decisions resulting in better outcomes. Organizations and risk professionals that recognize and implement the risk management principles, framework and process presented in this course will have greater opportunities for success.