## Slide 1: Assessing and Managing Risk: An ERM Perspective Chapter 7 – Identifying Risk
Developed by Bruce Lyon, CSP, P.E., SMS, ARM, CHMM
Dr. Georgi Popov, CSP, QEP, ARM, SMS, CMC, FAIHA
Notes: In this module, you will learn how risks are assessed through the process of risk identification, risk analysis and risk evaluation. You will also learn how the risk assessment process is aligned with OSH goals with the ERM model. We will introduce case studies and examples to reinforce deeper learning. Let’s get started.

## Slide 2: Chapter 7 – Identifying Risk
Notes: In this chapter we will:
introduce the concepts of risk identification
The elements that are included in risk identification
And the methods available for identifying risk as the first step of risk assessment.

## Slide 3: Risk Assessment
Risk Identification
Risk Analysis
Risk Evaluation
Notes: Risk assessment is the ‘core’ of the risk management process. It is an iterative and systematic process for identifying, analyzing, and evaluating risk so that decision makers can better understand the risk and determine the appropriate risk treatment and management.
The risk assessment process has three distinct and sequential components:
risk identification
risk analysis and
risk evaluation as illustrated in the Figure here adapted from the ISO 31000 Risk Management standard.
Using a standardized approach allows an organization to consistently anticipate, discern and identify risks, measure and compare risks, formulate risk treatment measures, and prioritize treatment based on risk levels.
The first step of risk assessment, ‘risk identification’, is most crucial since risks that are not anticipated, recognized, or identified go unmanaged. Risk identification is used to find, describe, and document risks that are of importance to the organization and that warrant further assessment. Based on an organization’s defined context and scope, risks that can ‘impact’ the ability to achieve stated objectives are identified, described, and recorded for further assessment.

## Slide 4: Risk Identification
More than simply identifying hazards or risk sources
It involves identifying and describing the uncertainties and their effects, the related circumstances or concerns
Notes: Risk identification is more than simply identifying hazards or risk sources. It involves identifying and describing the uncertainties and their effects, the related circumstances or concerns, any existing controls and their effectiveness, how the risk my occur, related events in the past, and the potential human and organizational factors that might apply.

## Slide 5: Risk Management Standards
Relationship Between Risk Management Standards
Notes: To gain a perspective of how risk is identified, a review of several key risk management standards is provided. The ISO 31000 Risk Management standard provides a larger context encompassing the management of all types of risk - pure risks and speculative risks. Within ‘risk management’ is ‘risk assessment’ of those risks which are covered in ISO 31010 and ANSI RA.1 risk assessment standards. And within risk assessment is a more specific ‘safety’ standard, ANSI/ASSP Z590.3-2011(R2016), Prevention through Design (PtD). The PtD standard which is focused on assessing pure risks such as hazard-based and operational-based risks resides within the larger risk assessment sphere as illustrated in the Figure here.

## Slide 6: Risk Identification and ISO 31000
“The purpose of risk identification is to find, recognize and describe risks that might help or prevent an organization from achieving its objectives.”
Organizations must be able to manage both pure risks and speculative risks
Notes: To better understand risk identification, let’s review how several key standards define the first step of risk assessment.
The ISO 31000 risk management standard states that “the purpose of risk identification is to find, recognize and describe risks that might help or prevent an organization from achieving its objectives.” The statement ‘might help or prevent an organization from achieving its objectives’ reflects the view enterprise risk management takes with risk – that risks can have positive effects (i.e. opportunity or speculative risks), negative effects (i.e. pure or absolute risks such as hazards and operations), or both.
When identifying, assessing, and managing risk, organizations must be able to manage both pure risks and speculative risks to fully achieve their objectives.
It is recommended that organizations take account of their risks, including those that have current controls or are considered controlled. In some cases, there are multiple types of outcomes, consequences or objectives affected by certain risks

## Slide 7: Risk Identification and ISO 31010
“Identifying risk enables uncertainty to be explicitly taken into account”, both beneficial and detrimental dependent upon the context and scope of the effort
Risks should be identified as early as possible so that any unacceptable risks are known and addressed.
Notes: The risk assessment standard, ISO 31010 states that “identifying risk enables uncertainty to be explicitly taken into account”, both beneficial and detrimental dependent upon the context and scope of the effort. In Annex B, the standard includes ‘techniques for eliciting views’ in B.1, ‘techniques for identifying risk’ in B.2, and methods for ‘determining sources, causes and drivers of risk’ in B.3.
Key factors that should be identified include:
sources of risk,
existing controls and their effectiveness,
how certain events might occur,
Any past experiences and incidents, and
human aspects and organizational factors.
Obviously, risks should be identified sooner rather than later so that risks are found and treated before losses can occur.
In addition, a mechanism for detecting, anticipating and recognizing new or emerging risks should be in place as part of the risk management process.
Risk identification, like the entire risk assessment, should be performed in a methodical and iterative way that is thorough and efficient.

## Slide 8: Risk Identification and ANSI RA.1
Ascertain “the sources and nature of risk and the effect of uncertainty on achieving the organization’s objectives”
Identify risk characterization, criticality to the organization, and potential consequences
Notes: The ANSI RA.1 Risk Assessment standard says the purpose of risk identification is to ascertain “the sources and nature of risk and the effect of uncertainty on achieving the organization’s objectives”. Risk identification should include natural, unintentional, and intentional events for risks that can lead to negative outcomes as well as risks pursued as an opportunity. Identification of malevolent, criminal, technical, institutional, logistical, logical, demographic, environmental, and social/political events should be considered. Risk identification should seek to answer basic questions regarding ‘what’, ‘where’, ‘when’, ‘why’, ‘how’, and ‘who’, so that the risk analysis and evaluation can occur.
In addition to identifying sources of risk or uncertainty, the assets at risk, their characterization and criticality to the organization, and potential consequences should also be identified.
Methods discussed in RA.1 include threat and opportunity analysis, vulnerability/capability analysis, and criticality and consequence (impact) analysis.

## Slide 9: Risk Identification and ANSI Z590.3 PtD
Similarities
Subtle differences
focusses on hazard-risk throughout life cycle of system
‘hazard analysis and risk assessment’
ISO 31000 principles, framework and process
Notes: ANSI Z590.3, Prevention through Design
The ANSI/ASSP Z590.3 Prevention through Design (PtD) standard operates within the same fundamental principles, framework and process as ISO 31000 and ISO 31010 for assessing risk. However, being a safety standard, it has some subtle differences. First, Z590.3 focusses on hazard-risk from design to decommission (life cycle) of a system. Rather than risk assessment, Z590.3 calls the process ‘hazard analysis and risk assessment’. And, its first step in the process is “Anticipate/identify the hazards”.
The word ‘anticipate’ means to ‘give advance thought, discussion or treatment’ (Merriam-Webster) (https://www.merriam-webster.com/dictionary/anticipate). For the context of risk identification, ‘anticipate’ also seems to imply that risk sources/hazards may not be known to currently exist, hidden and difficult to observe, or only occur under specific circumstances. The ability to anticipate hazards requires the assessor to have knowledge and foresight in hazard types and the operation or system being reviewed. Hazard/risk identification involves finding, anticipating, recognizing, and describing hazards that could affect the achievement of an organization’s objectives

## Slide 10: Emerging Risks
new processes, technologies, or types of work
changes in the organization,
environmental, social, public, or political change
Notes: Emerging risks can be characterized as new, developing risks that have been detected and apparent, or existing risks that are changing and increasing in new or unfamiliar conditions.
These emerging risks present effects of uncertainty on objectives and can be caused by:
new threats or hazards
changes in frequency of occurrence,
changes in consequences or their severity or
in the case of speculative risks, new opportunities, and potential gains.
Sources of emerging risk can include new processes, technologies, or types of work. They may also develop from changes in the organization, or from environmental, social, public, or political change.
Emerging risks may have a low likelihood or frequency potential, however, have significant consequences such as black swan events. Risks can emerge, develop, increase, or disappear as an organizations external and internal context changes. The risk management process must be designed to anticipate, detect, identify, acknowledge, and respond to those changes and events in an appropriate and timely manner.

## Slide 11: Emerging Risks
Notes: After the emerging risks are characterized, a formal decision is made regarding which emerging risks should be selected to be analyzed more thoroughly. The outcome of characterizing the emerging risk would be a decision to “discard”, “monitor” or “assess” the risk.

## Slide 12: Risk Source
an element by itself or in combination that has potential to create risk and uncertainty
  risk and uncertainty are derived from risk sources
  for pure risk (R-), the most effective means of managing the risk is at its source
Notes: Risk has an origin – a risk source.
A risk source can be defined as an element either by itself or in combination that has potential to create risk and uncertainty. In other words, risk and uncertainty are derived from risk sources. For pure risk (risk that can only result in negative outcomes), the most effective means of managing the risk is at its source. If the risk source can be avoided, eliminated or reduced to an acceptable level of risk (ALOR), it will require little if any management going forward.

## Slide 13: Risk Source
Sources of risk can include events, decision, or actions and/or conditions that alone or combined create risk.
Events and consequences can have multiple causes or causal chains.
Notes: Sources of risk can include events, decision, or actions and/or conditions that alone or combined create risk. Events are occurrences or things that happen at a point in time or that have a potential to occur. An event can be something that is expected to occur but does not, or something that is not expected that does occur. Actions are an intentional act, movement or physical activity carried out to accomplish a particular goal and can have intended and/or unintended consequences. A condition is the state of something that exists or has the potential to exist regarding its properties or characteristics. Conditions, such as hazards, can exist or have a potential to be created that present certain inherent properties or characteristics that give rise to risk. Events and consequences can have multiple causes or causal chains.

## Slide 14: Hazard/Risk Sources
Chemical (Toxic)
Chemical (Flammable)
Chemical (Corrosive)
Explosion (Chemical Reaction)
Explosion (Over Pressurization)
Electrical (Shock/ Short Circuit)
Electrical (Fire)
Electrical (Static/ESD)
Electrical (Loss of Power)
Ergonomics (Strain)
Ergonomics (Human Error)
Excavation (Collapse)
Fall (Slip, Trip)
Fire/Heat
Mechanical/ Vibration (Chaffing/ Fatigue)
Mechanical Failure
Mechanical
Noise
Radiation (Ionizing)
Radiation (Non-Ionizing)
Struck By (Mass Acceleration)
Struck Against
Temperature Extreme (Heat/Cold)
Visibility
Weather Phenomena (Snow/Rain/Wind/Ice)
Notes: Hazards exist in many places and forms, some of which include operational functions, operational failure modes, actions, inactions, interactions, upsets, changes, energy sources, existing conditions, conditions created, materials, chemicals and substances, and combined elements or conditions that create synergistic effects. There are many references and resources for categories of hazards including the following list in the Table taken from OSHA’s “Job Hazard Analysis”, Appendix 2 found in Publication 3071

## Slide 15: Risk Driver
factor that has a major influence on risk
  influence the status and development of risk
  can affect more than one risk
Notes: A risk driver is a “factor that has a major influence on risk” – definition from (ANSI/ASSP/ISO 31010, 2019). Risk drivers influence the status and development of risk exposures and can affect more than one risk. Because of their potential influence on multiple risk sources, risk drivers can require more attention and scrutiny.

## Slide 16: Risk Exposure
something of value that is subject to risk
  People
  Property
  Objectives
  Environment
  Community
Notes: A risk exposure is something of value that comes in direct contact, proximity or path of a risk. These things of value consist of the organization’s business objectives (profits, cash flow, growth, stability, public relations and good well, customers, regulatory and legal compliance and reputation), assets, people, property, equipment, and the local community and environment. These things of value that are exposed to a risk have an increased likelihood of an occurrence and resulting consequences, while those that are not exposed have a very low likelihood of the occurrence. It is important to identify which things of value are at risk of exposure in the identification process.
Identification of the exposure routes or pathways for identified risk sources is also needed to then analyze, evaluate and control the risk.

## Slide 17: Existing Controls
description
what is controlled/protected
type of control
  preventive, mitigative or both
effectiveness and reliability
  independency or dependency
  gaps, weaknesses
  secondary risks?
Notes: Risk identification should include the identification and description of existing controls, and their effectiveness and reliability. As stated in ISO 31010, consideration should be given to:
the mechanism by which the controls are intended to modify risk;
whether the controls are in place, are capable of operating as intended, and are achieving the expected results;
whether there are shortcomings in the design of controls or the way they are applied;
whether there are gaps in controls;
whether controls function independently, or if they need to function collectively to be effective;
whether there are factors, conditions, vulnerabilities or circumstances that can reduce or eliminate control effectiveness including common cause failures;
whether controls themselves introduce additional risks.
It should be noted that multiple controls can be in place for certain risks, as well as multiple risks controlled by a single control. Identification of existing controls should also describe how the control modifies the risk such as:
prevents exposure (changes likelihood)
mitigates or reduces impact (changes severity)
prevents and controls (changes likelihood and severity)
how the burden of risk is shared between stakeholders (insurance, risk transfer and risk financing).
Control effectiveness and reliability assumptions made during the identification process should be verified during the risk analysis All assumptions made during risk analysis about the actual effect and reliability of controls should be validated where possible, with a particular emphasis on individual or combinations of controls that are assumed to have a substantial modifying effect. This should consider information gained through routine monitoring and review of controls.

## Slide 18: Failure Modes
a condition where a system fails to perform as expected or deviates from its design tolerances resulting in a potential for harm or a hazardous event
  pre-mature operation
  failure to start or stop
  failure during operation
  degraded operation
  exceeded capacity
  reasonably foreseeable uses/misuses
Notes: As part of the risk identification, potential failures of the system should be identified and described. A failure mode is described as a condition where a system fails to perform as expected or deviates from its design tolerances resulting in a potential for harm or a hazardous event. In identifying failure modes, methods such as ‘what-if’ can be used to identify potential system failures by exploring various ways something might go wrong.
Failure modes where the system fails to perform as designed or expected can exist in systems or equipment such as conveyors, pumps, press brakes, local exhaust ventilation, containment vessels, and forklifts for example. These conditions or states might include:
pre-mature operation (i.e. unexpected startup or release of energy)
failure to start operation (i.e. sump pump fails to operate when water level rises beyond flood level)
failure to stop operations (i.e. press brake fails to stop when interlock is activated)
failure during operation (i.e. local exhaust system fails during welding operation)
degraded or deterioration of operation (i.e. leak in containment vessel)
exceeded capability/capacity of operation (i.e. over pressurization of vessel)
reasonably foreseeable uses and misuses of operation (i.e. using forklift to raise worker to reach component)
The end result is to identify credible circumstances and potential failures that could arise and result in an undesirable incident or exposure. As ANSI Z590.3 states, each failure mode should include a description of the circumstances and events that could lead to the failure so that it can be understood.

## Slide 19: Causes and Triggers
circumstance, condition, action or inaction that can lead to exposure to a risk source
  Acute
  Chronic or cumulative
Notes: Causes or triggers are the circumstances, conditions, actions, or inactions that can expose a hazard or initiate a hazardous event. Hazards can be of an acute nature causing immediate harm from a single exposure, or cumulative in nature developing over time from prolonged or repeated exposure.

## Slide 20: Causes and Triggers
Notes: Fundamental causes include:
Machinery, processes or facilities and their design, selection, condition, use or maintenance
Human-related resulting from actions, inactions, knowledge level, skill level, ability or capability, attention level, interaction, or communication
Management-related causes include oversight, direction, supervision, enforcement level, consistency of these elements, and overall communication
Methods can be causes or triggers if the design is flawed, or the method leads to exposure to failure modes, or risk sources
Materials can result in incidents by their very nature, element or constituents such as chemicals, or their handling, storage, use or disposal
And the environment can be a cause due to its layout or design in the workplace, the conditions such as weather, or other external factors.

## Slide 21: Consequences
What can happen as a result of the exposure to the risk and a resulting incident
  What is affected
  To what degree of impact or severity
Notes: Consequences are the result or outcome of a risk exposure event. They are what can be expected to occur should the incident happen. Risk identification should include identifying the potential consequences, and assets (people, property, business objective, etc.) that are exposed to a risk have an increased likelihood of an occurrence, while assets that are not exposed have a very low likelihood of the occurrence.
For a risk source to present a risk to the organization, there must be an ‘objective’ at risk (something of value to the organization) and a consequence. Most often, there are multiple potential consequences associated with a risk. Sometimes the risk presents only negative effects from hazards or operations, while speculative risks present positive and/or negative potential affects.
The anticipated or reasonably foreseen consequences that might result from exposure to the risk sources should be identified. The subject of its impact such as objectives, people, property, liability, reputation, environment or other should be identified. A general description of types of consequences associated with the risk source is needed to conduct the risk assessment.

## Slide 22: Identification Methods
Notes: Methods for identifying risk include the collection of information such as document reviews, interviews, and observations.
Historical reviews of available data on losses, incident investigations and near hit reports can help identify the types of incidents, hazards and causes at the site, the organization, or industry sector.
Regulatory reviews of applicable codes, regulations and consensus standards can be used to identify common compliance needs, hazards, and controls.
Document reviews and examinations of design plans, specifications; operational manuals or instructions; procedural instructions; maintenance documents and instructions; complaints and hazard reports; perception surveys; and audits, inspections and survey reports can be valuable information to consider.
Similar operations, energy sources, site surveys, checklist surveys, interviews and brainstorming can help identify existing, potential, and less obvious hazards in the operation.

## Slide 23: Identification Methods
Checklists
HAZID
Brainstorming
Notes: Checklists are a quick and easy way to identify hazards; however, it is important to remember that checklists serve as a guide and should not limit the focus too narrowly as to miss hazards not on the list. Checklist findings can be summarized in other methods like HAZID or Hazard Identification Study, brainstorming sessions, or nominal group technique for further study. Although there are many means of identifying and describing risks, a single systematic and consistent approach to their use is most important.

## Slide 24: Conducting Risk Identification
Review Context
Define Responsibilities
Initiate Identification Process
Document and Track Risks
Communicate Results
Develop Plan
Notes: A systematic and iterative approach to identifying risks and their related elements should always be used. Having a basic plan for conducting risk identification is recommended. The following steps for such a plan are adapted from the MIL-STD-882E standard Task 101:
To begin, a review of the organization’s established context for risk assessment should be performed in preparation of developing a plan.
Then, the specific purpose, methods for identification along with the team members and facilitator, resources, budget, timeline, and other elements needed for the effort should be defined as part of the plan.
The plan should also clearly define the roles and responsibilities, interrelationships, and lines of communication within the organization and affected stakeholders. The plan and responsibilities should be communicated and understood by stakeholders.
Following the plan, the assessment team uses the selected methods to find, identify and document existing and potential risks, risk drivers, causes, possible consequences, and existing controls.
The identified risks should be documented and tracked for further analysis, evaluation, and treatment.
The documented risks and tracking system should be shared and communicated with affected stakeholders and decision makers for further steps in the risk assessment.

## Slide 25: Summary
Success dependent upon identification of:
risk source,
risk drivers,
causes or triggers,
exposures,
existing controls and
potential consequences.
The better the risk is understood, the more likely it can be analyzed, evaluated and controlled.
Notes: The success of a risk assessment is dependent upon proper identification of risks and the associated elements. Risk identification includes the identification and description of the risk source, associated risk drivers, causes or triggers, exposures, existing controls and the potential consequences. The better the risk is understood, the more likely it can be analyzed, evaluated and controlled.