## Slide 1: Chapter 8 – Analyzing Risk
Notes: In this chapter we will:
Review the concept of analyzing risk
The elements of risk that are analyzed
And methods that can be used to analyze risk

## Slide 2: Introduction
Once a risk has been identified and described, it can then be analyzed
Risk analysis is considered the heart of risk assessment
Notes: Once a risk has been identified and described, it can then be analyzed to determine its estimated risk level.
Risk analysis is considered the heart of risk assessment and is used to gain an understanding of the risk, its consequences, and likelihood of occurrence. It is used to estimate risk levels so that risks can be evaluated, prioritized, and treated according to the established risk criteria. To properly analyze risks, a standardized and iterative approach must be used throughout the risk management process.

## Slide 3: Risk Analysis Defined
ISO Guide 73 - “process to comprehend the nature of risk and to determine the level of risk.”
ANSI RA.1 - “process to characterize and understand the nature of risk and to define the level of risk”.
ANSI/ASSP Z590.3 - not considered a risk analysis until the ‘estimation of likelihood’ is complete.
Notes: Risk analysis is defined by ISO Guide 73 as the “process to comprehend the nature of risk and to determine the level of risk.” It notes that “risk analysis provides the basis for risk evaluation and decisions about risk treatment” (ANSI/ASSP Z690.1, 2011).
ANSI RA.1 defines ‘risk analysis’ as the “process to characterize and understand the nature of risk and to define the level of risk”. It further notes that “risk analysis assesses the likelihood and consequences of a risk to provide the basis for risk evaluation and risk treatment decision-making” (ANSI/ASIS/RIMS RA.1, 2015).
From a safety or hazard-risk standpoint, ANSI/ASSP Z590.3 Prevention through Design standard uses the term ‘hazard analysis’ to include both hazard identification and analysis. It defines hazard analysis as “a process that commences with the identification of a hazard or hazards and proceeds into an estimate of the severity of harm or damage that could result if the potential of an incident or exposure occurs.” (ANSI/ASSP Z590.3, 2016). It is not considered a risk analysis until the ‘estimation of likelihood’ is complete.

## Slide 4: Risk Analysis Defined
Notes: Without risk analysis, a risk cannot be evaluated as to it acceptability or need for treatment by an organization. As indicated in the Figure here, risk analysis is preceded by risk identification, and followed by risk evaluation within the risk management process. It is also important to remember that all risk analyses and assessments are ‘estimations’, albeit educated estimates, since risk deals with future uncertainty. ISO Guide 73 supports this assertion in a note that states that “risk analysis includes risk estimation”

## Slide 5: Understanding the Nature of Risk
Elements within Risk Analysis
Notes: ISO 31000 states that “the purpose of risk analysis is to comprehend the nature of risk and its characteristics including, where appropriate, the level of risk” (ANSI/ASSP/ISO 31000, 2018).
It involves analysis of:
identified uncertainties,
risk sources, consequences,
likelihood,
events and scenarios,
existing controls and their effectiveness and reliability.
Events and scenarios can have multiple causes and multiple consequences, as well as affect multiple objectives. This should be kept in mind during risk analysis.

## Slide 6: Understanding the Nature of Risk
adapted from ANSI/ASIS/RIMS RA.1- Risk Assessment, 2015
Notes: Risk analysis is used to gain an understanding of risk.
The ANSI/ASIS/RIMS RA.1 risk assessment standard outlines the analysis process as a way an organization can take information generated from the risk identification process and analyze it within the context of its operations and the established risk criteria. This involves assessing the likelihood of its occurrence, and the resulting consequences should it occur to determine the level of risk it presents. As shown here, “the output from risk identification provides the input to risk analysis.”

## Slide 7: Fundamental Terms
hazard
risk
hazard analysis
risk analysis
risk assessment
occasionally misused or used interchangeably
Notes: There are some fundamental terms in risk management that are critical for the risk professional to understand and use properly. These terms are ‘hazard’; ‘risk’; ‘hazard analysis’; ‘risk analysis’; and ‘risk assessment’ and are occasionally misused or used interchangeably. For instance, the term ‘hazard’ is often used in place of ‘risk’. Some use the terms ‘hazard analysis’, ‘risk analysis’ and ‘risk assessment’ incorrectly or to mean the same thing. It is important to recognize the differences when applying risk management principles.

## Slide 8: Fundamental Terms
Hazard
“Source of potential harm” that if left uncontrolled, can create risk (ISO Guide 73).
‘source of risk’
Risk
“Affect of uncertainty on objectives” (ISO Guide 73).
The likelihood of occurrence and severity of consequence
Notes: Hazard
ISO Guide 73 defines hazard as a “source of potential harm” that if left uncontrolled, can create risk. (ANSI/ASSP Z690.1, 2011) A hazard is considered a ‘source of risk’. Hazards are created by equipment or machinery, technology, energy sources, substances and chemicals, materials, or by human actions or inactions. Basic workplace hazard classifications include physical and mechanical, chemical, biological, ergonomic, and psychosocial. For a hazard to create risk, there must be a series of elements that interact as shown here. A hazard or ‘risk source’ is influenced by ‘risk drivers’ and if ‘exposure’ to the hazard exists, a trigger or cause can result in an ‘event’ that leads to ‘consequences’ which in summation is ‘risk’.
Risk is defined as the ‘affect of uncertainty on objectives’. It is generally determined by the likelihood of an occurrence and the severity of the consequence. As illustrated here, risk can be viewed as the complete risk pathway including the risk source, risk drivers, exposures, controls, causes or triggers, the event itself, and the consequences.
Risks are derived from risk sources such as hazards and operational aspects which are considered pure risks that can only produce negative consequences.

## Slide 9: Fundamental Terms
Hazard Analysis
Risk Analysis
Notes: Hazard analysis
Hazard analysis is considered the fundamental process of determining if a hazard or failure can lead to an incident or undesired event. Hazard analysis involves analyzing the identified hazards, their existing controls, and potential exposures. As a result, the analysis produces a range of possible consequences and severity estimates. Note: A hazard analysis does not estimate risk derived from the hazard.
Risk Analysis
ISO Guide 73 defines ‘risk analysis’ as the “process to comprehend the nature of risk and to determine the level of risk”. (ANSI/ASSP Z690.1, 2011) It includes the steps of a hazard analysis (identified hazards, existing controls, and potential exposures), as well as several additional steps. In a risk analysis, a consequence is selected to determine how the event could occur, and estimate its severity (S), likelihood (L), and risk level (R). A risk analysis allows for the ranking and prioritizing of risks using risk level estimations. Note: A risk analysis does not determine whether risks are acceptable or if risk treatment is required.

## Slide 10: Fundamental Terms
Notes: Risk Assessment
Risk assessment is the sequential process of identifying, analyzing, and evaluating risk. It goes beyond a risk analysis by including an ‘evaluation’ or judgement of risk acceptability. A comparison of the ‘estimated risk level’ with the established risk criteria is performed to determine whether the risk level is acceptable or if actions are needed to reduce the risk to an acceptable level. The Figure shows a comparison of the steps of a hazard analysis, risk analysis and risk assessment.

## Slide 11: Hazard Analysis Methods
Hazard Analysis Methods | Descriptions
Bow Tie Analysis | A barrier type analysis using a visual diagram to describe and analyze risk pathways of hazards, their causes, preventive controls, the hazardous event, mitigating controls and consequences. Traditionally, there is no risk estimation, however, it can be modified to include risk analysis.
Cause and Effect Analysis | A team-based method of generating and sorting potential causes and contributory factors for a defined problem that is typically illustrated in a fishbone type diagram. Traditionally, there is no risk estimation, however, it can be modified to include risk analysis.
What-if Analysis | A team-based, brainstorming process that uses the question ‘what if’ to identify deviations and analyze hazards of a system or process. Traditionally, there is no risk estimation, however, it can be modified to include risk analysis.
Job hazard analysis | A method used to break down a job into its main steps, identify the hazards associated for each step, and the controls for each hazard. It is documented in a three-column spreadsheet and used for job training, and accident investigation. Traditionally, there is no risk estimation, however, it can be modified to include risk analysis.
Notes: A hazard analysis is the identification of hazards, existing controls and the exposures to the hazards, and an analysis of the potential severity of consequences. It is the fundamental step in a risk assessment, however, by itself, it does not estimate risk or evaluate its acceptability. Examples of hazard analyses are presented in the slide. It should be noted that these traditional hazard analysis techniques can be modified to include risk estimations that would convert them to risk analysis methods.

## Slide 12: Process Hazard Analysis
OSHA
Process Safety Management of Highly Hazardous Chemicals
EPA
Risk Management Plan
Notes: A process hazard analysis is a set of organized and systematic analyses of identified hazards and controls associated with a process. It provides information to assist in making decisions for improving safety and reducing operational risk associated with a process. Process hazard analyses such as ‘What-if’ analyses are used to breakdown a series of actions or steps to understand process-related hazards and their causes and effects. These methods are often used to analyze potential causes and consequences of fires, explosions, releases of highly hazardous, toxic, or flammable chemicals. Process safety and analysis focuses on equipment, instrumentation, utilities, human actions, and external factors that may impact the process. One additional benefit of conducting such an analysis is a more thorough understanding of the industrial process, leading to opportunities for improving process efficiency and cost reduction.
Risk assessments have been legally required of businesses in the United Kingdom, since 1999 by the Health and Safety Executive. However, for businesses in the United States, there are only two standards that mandate the assessment of risk. These are the Occupational Safety and Health Administration (OSHA) Process Safety Management of Highly Hazardous Chemicals, and the Environmental Protection Agency (EPA) Risk Management Plan, both of which require process hazard analyses.
Process hazard analysis methods such as ‘What-if Analysis’ can be applied at any point of the lifecycle of a system and are commonly used to identify failures or deviations and the resulting affect so that proper controls can be implemented.

## Slide 13: Traditional What-if Analysis
Notes: What-if Analysis is a qualitative hazard analysis method that uses team-based brainstorming to determine what can go wrong in a given scenario. Originally used by chemical and petrochemical industries as an easier alternative to HAZOP, ‘What-If’ and its variations (What-if/Checklist and Structured What-if Analysis Technique or SWIFT) are commonly used in energy, manufacturing, high-tech, food processing, transportation, healthcare and other industries.
A cross-functional team knowledgeable of the system being analyzed is used to discuss aspects in a brainstorming fashion using ‘what if’ questions to identify weaknesses, deviations, or hazards. The team should include ‘subject matter experts’ in the system or component being analyzed and be led by an experienced facilitator. Through the process, potential hazards, their causes, effects, and controls are identified. As a result, additional controls to prevent the hazard from occurring are identified. The ‘what if’ questions along with resulting consequences, existing safeguards, risks levels and recommended additional controls are recorded on a what-if spreadsheet such as the example in the Figure here.

## Slide 14: Traditional What-If Hazard Analysis Example

## Slide 15: Risk Analysis Methods
Risk Analysis Methods | Descriptions
Business Impact Analysis | An analysis of critical functions of an organization and the resources needed to maintain them in the event of a disruption or change.
Cause and Consequence Analysis | A combination of fault and event tree analysis that allows inclusion of time delays. Both causes and consequences of an initiating event are considered.
Design Safety Review | A structured review of plans, specifications, and safety related factors during the design or redesign phase to identify and avoid or eliminate potential hazards and failure modes.
Event Tree Analysis | Models the possible outcomes from a given initiating event and the status of controls thus analyzing the frequency or probability of the various possible outcomes.
Failure Mode and Effects Analysis (FMEA) | A qualitative or semi-quantitative method that lists systematically the failure modes, their effects, existing safeguards, and any additional controls that are needed to reduce risk to an acceptable level
Notes: In a risk analysis, the hazards, controls, exposures, and severities are all identified; however, specific consequences are selected for further analyses and risk estimation.
Each consequence is analyzed as to how it could occur and its likelihood or probability of occurring. Risk estimates are derived from the analysis for severity level, likelihood level and risk level. To take the risk analysis to a ‘risk assessment’, the risk analysis and its risk estimates are evaluated and compared against the established risk criteria to determine whether each risk estimation is acceptable, or if addition risk treatment is required. The established risk criteria and the risk treatment actions for each risk level is used to determine action steps. The sequential application of risk identification, analysis and evaluation are required to complete a ‘risk assessment’. It is important understand the similarities and differences of hazard analysis, risk analysis and risk assessment. Table in the textbook 8.2 provides an example list of risk analysis methods commonly used.

## Slide 16: Risk Analysis Methods
Fault Tree Analysis | A deductive technique which starts with an undesired event (top event), determines the ways in which it could occur, and uses a logical tree diagram. After completing the fault tree, consideration should be given to ways of reducing or eliminating potential causes/sources.
Hazard Analysis and Critical Control Points (HACCP)* | A systematic and preventive system for hazard identification and placement of controls at critical points in a process to effectively prevent hazards from occurring. Used in food safety related processes.
Hazard and Operability Study (HAZOP)* | A qualitative method used to identify hazards and operability problems using ‘guide words’ to prompt team members in identifying deviations that can lead to the failures.
Notes: Here the table is continued with Fault tree analysis, HACCP and HAZOP.

## Slide 17: Risk Analysis Methods
Human Reliability Analysis | A technique used to identify the potential for human error and its causes, so the probability of error can be reduced.
Layers of Protection Analysis (LOPA) | A barrier type analysis of existing physical controls and their effectiveness for controlling a hazard.
Management Oversight and Risk Tree (MORT) | Generally used following an incident or exposure, MORT is a comprehensive type analysis following a disciplined approach for identifying and analyzing weaknesses in a system’s design and procedures.
Notes: Additional risk analysis methods include human reliability analysis, LOPA and MORT.

## Slide 18: Risk Analysis Methods
Multi-Criteria Analysis | A method for comparing options that makes trade-offs explicit. Provides an alternative to cost benefit analysis that does not need a monetary value to be allocated to all inputs.
Preliminary Hazard Analysis (PHA) | A simple method used to identify and analyze hazards and risks that can cause harm for a given activity, facility or system.
Risk Indices | Rates the significance of risks based on ratings applied to factors which are believed to influence the magnitude of the risk.
Striped Bow Tie Risk Assessment | A modified version of Bow Tie Analysis which incorporates the hierarchy of controls, layers of control analysis, and a risk scoring system.
Notes: And finally, multi criteria analysis, PHA, risk indices, and striped bow tie, to list a few.
*It should be noted that HAZOP, HACCP and PHA methods could be used early in the hazard identification step or as hazard analysis methods without adding the likelihood of consequences/impact.

## Slide 19: Analyzing and Understanding Consequences
Cascading Effects of Consequences Example
Notes: To analysis risk, the identified consequences must be characterized and understood. Their potential impact and magnitude of the impact on the organization’s objectives and assets must be identified and analyzed. Depending upon the context and complexity of the system being analyzed, consequences or outcomes may be described generally or in more detail using quantitative modelling or vulnerability analysis. Consequential cascading effects where one consequence leads to another should be considered in the analysis.
Example: For instance, in bio-diesel manufacturing process methanol is a key ingredient. Methanol, a flammable liquid is generally stored in atmospheric above ground storage tanks. However, physical, and chemical properties of methanol are unique and are not the same as those of other bulk-stored flammable liquids. Due its corrosive nature, cathodic protection, and regulator inspection of methanol storage tanks and trim hardware is required to avoid tank failure (Methanol Institute, 2016).
Methanol is the risk source in this example. Risk drivers may include corrosion, lack of inspection or maintenance, and other factors influencing the rise of risk. A single trigger such as over pressurization relief valve failure can cause a release of methanol.
This loss of product is an operational risk, affecting the manufacturing process. However, it the operational risk cascades into a hazard risk with the exposure to people and operations at the facility due to methanol’s flammable properties. This can result in fatalities, serious injuries and property and equipment loss or damage. Depending upon the amount of methanol releases the risk can cascade into a catastrophic event and result in an enterprise risk from the threat to the local community, a significant loss of business and damage to the organization’s public image as illustrated in the Figure here.

## Slide 20: Analyzing Consequences, Interactions and Dependencies
Notes: When analyzing a risk’s consequences, remember that a single risk can result in multiple consequences, some more severe than others, and some that have low severity but a potential for cascading effects.
Consequences can also affect different objectives or assets of the organization. Risk estimations should first consider the most credible worst-case scenario and resulting consequences and then prioritize the remaining risks and their impacts. For example, in the figure here the Striped Bow Tie Risk Diagram illustrates a methanol release that results in multiple consequences including fire and explosion loss to the facility, injury to workers, damage to the corporate image, financial loss, and liability claims and compliance losses to the organization.
In addition, risks can have interactions and dependencies with other risks, consequences, and occurrences. As shown in the figure here,
a single cause can result in multiple consequences;
a single consequence can result from multiple causes; or
certain occurrences may influence the occurrence of other events resulting in cascading effects.
Causal mapping can be used to link interactions or dependencies between risks, events, causes or consequences.

## Slide 21: Analyzing Likelihood
Likelihood (probability) can refer to a specific event or consequence and must be clearly defined as part of the context of the assessment.
Likelihood of occurrence should consider the parameters, exposure, and duration, and can be described as a frequency, an expected probability or in qualitative terms.
Notes: The second factor used in the risk analysis is likelihood. Likelihood (sometimes referred to as probability) can refer to a specific event or consequence and must be clearly defined as part of the context of the assessment. Likelihood of occurrence should consider the parameters, exposure, and duration, and can be described as a frequency, an expected probability or in qualitative terms. Qualitative descriptors such as ‘very high’, ‘high’, ‘moderate’, etc. must be well defined as to their meaning so that they are applied consistently. When using percentages to express measures of likelihood, the nature of the ratio and its justification should be clearly explained. In addition, the time period and exposed population or objective should be identified and defined in accordance with the context. It should be remembered that likelihood ratings like other risk factor ratings are informed ‘estimates’ and that biases can sometimes influence ratings. The assessor must be aware that individual and cultural biases are possible, and that interpretation of the likelihood estimate may vary depending on the context.

## Slide 22: SWIFRA – Structured What-if Risk Assessment
Notes: The traditional What-If Analysis method is a hazard analysis rather than a risk analysis since it does not include an estimation of risk level. Hazard analyses, like job hazard analyses, are useful in identifying and analyzing hazards, however, they do not provide risk-based information needed for prioritizing and treating risks. By including an estimation of risk to a hazard analysis, a more complete method is formed. To convert a hazard analysis to a risk assessment, three additional steps are needed.
First, specific consequences are selected to be analyzed and evaluated.
Second, for each consequence, an estimate of its severity (S) level, likelihood of occurrence (L) level, and resulting risk level (R) are determined.
Third, the estimated risk levels are then compared and evaluated with the established risk criteria to determine acceptability and required action.
An additional feature to the SWIFRA model shown here is a ‘what-how-why’ questioning process that includes 1) ‘what-if’ it occurs, then 2) ‘how’ can it occur, and 3) ‘why’ is it possible for it to occur. These are followed by identifying the effects of the occurrence, and existing controls to prevent it from occurring. Current state risk is determined considering the existing controls. If current state risk level is unacceptable, additional controls are recommended and a future state risk estimation made. A risk reduction percentage is them calculated to demonstrate the proposed controls effectiveness to decision makers.

## Slide 23: The Concept of Risk Summation
‘Whole-system risk’ – the combined or synergistic effects of multiple risk sources
The potential effect of combined or whole-system risks is often greater than any single risk in a system
Notes: An important concept in risk assessment is understanding ‘whole-system risk’ – the combined or synergistic effects of multiple risk sources. Conventional risk assessment methods can be described as “linear” or singular in nature. For instance, many risk assessment methods used such as failure mode and effects analysis (FMEA) or preliminary hazard analysis are applied in a manner that analyzes hazards individually, hazard-by-hazard, rather than considering the multiple hazards as a whole. As such, a hazard-by-hazard analysis approach would only consider partial risks within the system or operation. In certain cases, the partial risks may be found to be acceptable, leading to the judgement that the system or operation is “safe”. However, such conclusions may be misleading if there are combined or synergistic effects from multiple risk sources or hazards.
The potential effect of combined or whole-system risks is often greater than any single risk in a system. Risk assessors that identify and catalog individual hazards as line items may miss the potential for certain risks occurring at the same time producing additive or synergistic effects. An example of such an effect might be found in the meat processing industry where cold temperatures combined with hand-arm vibration from pneumatic hand tools increase risk of soft-tissue damage. If such risks are analyzed individually, the true ‘whole-risk’ may not be considered

## Slide 24: Summary
Risk analysis is considered the heart of risk assessment and the most involved step in risk assessment.
It is used to gain an understanding of the risk, its consequences, and likelihood of occurrence and to estimate risk levels so that risks can be evaluated, prioritized, and treated according to the established risk criteria.
Notes: Risk analysis is considered the heart of risk assessment and the most involved step in risk assessment. It is used to gain an understanding of the risk, its consequences, and likelihood of occurrence and to estimate risk levels so that risks can be evaluated, prioritized, and treated according to the established risk criteria. To properly analyze risks, a standardized and iterative approach must be used throughout the risk management process. One potential pitfall in risk analysis is the tendency for assessors to try and achieve perfection in their risk analysis estimations. However, it is more important and useful to ensure risk estimations are consistent, and guided by experience, knowledge, and available information.