## Slide 1: Chapter 9 – Evaluating Risk
Developed by Bruce Lyon, CSP, P.E., SMS, ARM, CHMM
Dr. Georgi Popov, CSP, QEP, ARM, SMS, CMC, FAIHA
Notes: In this chapter we will:
Review the concept of evaluating risk
The elements of risk that are evaluated
And methods that can be used to evaluate risk

## Slide 2: Risk Evaluation
the judgement and decision-making step in risk assessment
used to determine a risk’s acceptability to the organization
Notes: Risk evaluation is the judgement and decision-making step in the risk assessment process. It is defined as the “process of equating the results of risk analysis with risk criteria to determine whether a particular risk level is within an acceptable tolerance or presents a potential opportunity” (ANSI/ASIS/RIMS RA.1, 2015). Risk evaluation is used to determine a risk’s acceptability to the organization. Without a judgement as to the acceptability or tolerance of a particular risk, there would be no decision to prioritize or act upon risks.

## Slide 3: Risk Evaluation
The purpose of risk evaluation is to support decisions by comparing the results of the risk analysis with the established risk criteria to determine where additional action is required.
This may lead to
the decision to take no action
consider treatment options
conduct further analysis
maintain existing treatments
reconsider the objectives
Notes: As ISO 31000 describes, the purpose of risk evaluation is to support decisions by comparing the results of the risk analysis with the established risk criteria to determine where additional action is required. This may lead to the decision take no action; consider treatment options; conduct further analysis; maintain existing treatments; or reconsider the objectives. Any decision made should consider the context and the consequences to stakeholders.

## Slide 4: Risk Evaluation
Risk Identification
Risk Analysis
Risk Evaluation
Output used to analyze risk
Output used to evaluate risk
Output used to make decision
Notes: As stated earlier, the output from risk identification is used to analyze the risk. The risk analysis produces a risk estimation which is then used in the risk evaluation to ‘evaluate or judge’ the risk as to its acceptability. The evaluation’s output is used to help decision makers in their decisions as to what actions might be taken.
The risk evaluation decision is made by comparing the estimated risk level to the established risk criteria. In essences, risk evaluation can be considered ‘risk-based decision making’.

## Slide 5: Risk Evaluation
Estimated Risk
Established Risk Criteria
Notes: The risk evaluation decision is made by comparing the estimated risk level to the established risk criteria. In essences, risk evaluation can be considered ‘risk-based decision making’.

## Slide 6: Risk Evaluation and the ‘Significance of Risk’
used to determine risk acceptability
based on severity and likelihood, and other factors:
  Potential worst credible consequence
  Effectiveness of controls
  Stakeholder’s views and perceptions
  Cost and practicability of treatments
  Interactions between risks
Notes: The estimation of a risk’s significance or magnitude is derived from risk analysis and is used to determine whether the risk should be accepted or if it requires action to reduce the risk to an acceptable level. This decision is based on a comparative evaluation of the risk relative to the objectives and performance thresholds of the organization. This evaluation is an important and primary input into the decision regarding the risk and how it should be treated. The significance or magnitude of risk is the first consideration in risk evaluation, and those risks that are outside of the acceptable range and are not tolerable to the organization.
Risk significance is based on the severity and likelihood of occurrence and generally expressed in a risk matrix (example shown here). Other factors in determining risk significance include:
potential worst credible consequences
effectiveness of existing controls
stakeholders’ views and perceptions
the cost and practicability of treatments
interactions between risks.
It is important that an iterative approach to evaluating risk be used. Decisions as to the significance of risk and its acceptability to the organization must be consistent.

## Slide 7: Prioritizing Risk for Treatment
Notes: A second judgement made in risk evaluation is the prioritizing of risks for treatment. This is based on the degree of risk as it relates to the established risk criteria and action levels. As stated in ISO 31010, this type of decision is often made using expert judgement based on the understanding from an analysis of the options concerned and the risk associated with each, taking into account: trade-offs that may need to be made between competing objectives; the organization's appetite for risk; and the different attitudes and beliefs of stakeholders.
Defined risk criteria, risk levels and corresponding actions are established in the context and can range from a simple method of two risk categories (those that require treatment, and those that do not require treatment) to more complex methods that use multiple risk levels with graduated degrees of actions. For example, a simple method of dividing risks into three bands could be used where risks are 1) unacceptable, 2) marginal or 3) acceptable. Such an approach follows the concept of ALARP – ‘as low as reasonably practicable’, which is used to determine when the cost of further risk reduction exceeds the benefit gained from the resulting risk reduction or ‘point of diminishing returns’.

## Slide 8: Risk-Based Decision Making
Notes: As presented in Module 1, risk-based decision making (RBDM) is the practice of risk management in the decision-making process. The RBDM model presented here provides a systematic approach for making decisions using risk-related information to reduce risk and uncertainty, and ultimately achieve better outcomes. The decision made in the RBDM process is conducted in risk evaluation and risk treatment phases of the risk assessment. Risk evaluation uses the established risk criteria to determine whether the risk is acceptable or if risk reduction is required, and the priority level for action

## Slide 9: Risk Evaluation Methods
Notes: The process of evaluating risk usually will include the use of one or more methods or tools. There are a number of methods available for evaluating risk as shown in the Figure here. Several techniques are listed that range in application, complexity, and ease of use including the organization’s established risk criteria, risk matrices, risk indices, ALARP (as low as reasonably practicable), SFAIRP (so far as is reasonably practicable), and Monte Carlo analysis. No matter which methods are selected, the organization should consider modifying or customizing methods to meet their specific needs and applications.

## Slide 10: Risk Evaluation Methods
Notes: Some of these methods are briefly described in the table. Consequence Likelihood matrices are also known as risk matrices and are commonly used to visually plot and rank risks.
F/N diagrams or Frequency/ Number curves are a method for graphing a chart of frequency of an event compared to the number of events to consider tolerability of the risk.
Cause and consequence analysis is a combination of fault tree and event tree analysis that allows inclusion of time delays.
Risk indices are used in rating the significance of risks based on numerical ratings which are influential to the magnitude of the risk.

## Slide 11: Risk Evaluation Methods
Notes: Risk Heat maps, similar to risk matrix, are a visual tools to show the ranking of risk points in a color-coded two-dimensional map.
ALARP – as low as reasonably practicable – is the concept of reducing risk to a point of ‘diminishing returns’ or where the costs exceed the expected risk reduction benefits. ALARA – as low as reasonably achievable – is a similar concept originating in the Nuclear Energy industry based on minimizing ionizing radiation doses to an acceptable level. SFAIRP – so far as is reasonably practicable – is also similar and used as a criterion for assessing controls or treatments.

## Slide 12: Risk Matrices
NFPA 70 E
MIL 882E
ASSP TR-31010-2020 Technical Report: Risk Management - Techniques for Safety Practitioners
Notes: Risk assessment matrices and heat maps based on defined risk criteria are commonly used by organizations to visually compare risk levels within the graduated risk level categories.
Risk matrices are generally constructed in two dimensional grids with one axis for severity of consequences, and the other for likelihood of occurrence. Matrices can be expressed in qualitative, semi-quantitative, or quantitative terms and range from very simple (2 x 2) to complex (10 x 10 or larger).

## Slide 13: Risk Matrices and Heat Maps
Notes: Such matrices can be modified to include both threats (pure risks) as well as opportunities (speculative risks). This two-dimensional matrix provides a visual measure of risk opportunities levels and risk threats levels based on defined likelihood and magnitude levels. Such methods are useful in prioritizing risks for treatment or action.
.

## Slide 14: Risk Matrices and Defined Risk Factor Levels
Notes: Risk matrices are based on defined risk factor levels for severity and likelihood. These definitions are decided upon by the organization during the planning and establishing context phase.

## Slide 15: Heat Maps
Notes: A risk heat map uses colors on a grid or matrix as shown in the Figure here to visually represent risk rankings to decision makers in their evaluation and treatment of risk. Such maps are generated from risk indices and risk analyses like What-if analyses, FMEAs and Process Hazard Analyses. Individual risks are plotted on the heat map grid according to the colors corresponding to the level of the risk. The heat map is typically constructed as a two-dimensional matrix measuring severity of risk and the frequency or likelihood of occurrence. The number of levels can range from a simple 2 x 2 model to a more complex model. Risk criteria and risk level definitions developed by the organization should be used to characterize the heat map risk levels.
Methods such as risk matrices and heat maps provide a means of visually communicating risks in relationship to established risk criteria

## Slide 16: Risk Frontier Curve
Risk Frontier Graph adapted from ANSI/ASIS/RIMS RA.1-2015
Notes: Another similar method uses a graph to determine risk acceptability called a Risk Frontier Curve. Similar to a heat map or risk matrix, a risk frontier graph plots the risk’s likelihood of occurrence and severity of consequence on a two-dimensional axis graph with a ‘acceptable risk frontier’ curve. By considering the risk and the factors affecting it acceptability, the assessors make a determination using risk-based information to accept or treat the risk.

## Slide 17: ALARP and SFAIRP
Notes: The concept of ALARP, as low as reasonably practicable, establishes risk level boundaries between unacceptable, ALARP and broadly acceptable regions. The middle category can be further divided into sub-categories where certain actions are requires such as cost benefit analysis for lower risks and required risk reduction for higher risks as illustrated in the figure here.
A similar concept, SFAIRP or ‘so far as is reasonably practicable’ generally refers to safety related risk, however, it makes no reference to the level of risk. SFAIRP is usually interpreted as a criterion by which controls are assessed to see if further treatments are possible; then, if they are possible, whether they are practicable.

## Slide 18: Risk Indices
Notes: Risk indices use a combined likelihood and severity of a hazardous event or consequence, anticipated from an identified hazard.
They are used to rank and compare risks as part of the risk evaluation.
A risk index is designed to help distinguish those risks which are unacceptable to the organization and provide a ranking of risks by risk level to prioritize treatment.
They are typically developed to summarize the risk of an event or condition by using numbers or categorical values for the purpose of identifying and comparing risks.
Risk indices models can be qualitative (word descriptors, letters and colors), semi-quantitative (numerical rankings based on non-statistical data) or quantitative (numerical rankings based on statistical data) in nature and are used to describe and communicate the level of risk to stakeholders and decision makers.
A fairly well-known example of a risk index is the U.S. Occupational Safety and Health Administration’s (OSHA) Heat Index. The Heat Index uses an index system developed by the U.S. National Oceanographic and Atmospheric Administration (NOAA) and combines both air temperature and relative humidity into a single value that indicates the apparent temperature in degrees Fahrenheit. This reflects how hot the weather will feel to the human body.

## Slide 19: Risk Indices
Risk indices are developed using historical data and analysis tools such as fault tree analysis, event tree analysis and general decision analysis.
It is important that sufficient data are used to validate the index.
Notes: Risk indices are developed using historical data and analysis tools such as fault tree analysis, event tree analysis and general decision analysis. It is important that sufficient data are used to validate the index. Generally, values and scores are applied to each factor and combined using an equation to represent the relationship between them. Factors that increase the level of risk are multiplied together and divided by those that decrease the level of risk.

## Slide 20: Value at Risk
Image source: Wikipedia
Notes: According to ISO 31010, the value at risk (VaR) method is used widely in the financial sector as an indicator of the amount of possible loss in a portfolio of financial assets over a specific time period within a given confidence level. Losses greater than the VaR are suffered only with a specified small probability. The distribution of profit and loss is usually derived in one of three ways. These include:
Monte Carlo simulations used to model the drivers of variability in a portfolio and create the distribution;
historical simulation models that make projections based previously observed outcomes and distributions; and
analytical methods based on assumptions that underlying market factors have a multi-variate normal distribution.

## Slide 21: Summary
Risk evaluation, the third step within risk assessment
Judgement as to whether risks are acceptable, and whether risk treatment is required occurs in the risk evaluation step
Risk-based information produced from the first two steps is evaluate
Notes: Risk evaluation, the third step within risk assessment, is the act of reviewing risk-based information produced from the first two steps, risk identification and analysis, to determine whether the risk is acceptable to the organization. This requires an established set of risk measurements by the organization to compare with those risk estimated by the analysis. Judgement as to whether risks are acceptable, and whether risk treatment is required occurs in the risk evaluation step. Without proper risk evaluation by an organization, existing risks are not prioritized for treatment, and may go untreated.