## Slide 1: Risk Management Tools for Safety Professionals – Part I, Chapter 4
RISK MANAGEMENT METHODS AND TOOLS
Chapter 4 – Risk Identification
Authors: Bruce K. Lyon, P.E., CSP, ARM, CHMM
Georgi Popov, Ph.D., QEP, SMS, ARM, CMC

## Slide 2: Chapter 4 – Risk Identification
Introduction
The process of assessing risk is considered the ‘core’ of risk management. The fundamental process of risk assessment enables those responsible for making decision to better understand the risk and its need for reduction or management.
Risk assessment, as defined in ISO Guide 73 (ANSI Z690.1-2011), Vocabulary for Risk Management standard, embodies three distinct, sequential components. These components are:
  Risk Identification - finding, recognizing and recording hazards
  Risk Analysis - understanding consequences and probabilities and existing controls
  Risk Evaluation – comparing levels of risk and considering additional controls
Of the three elements, risk identification is arguably the most critical aspect of risk assessment.

## Slide 3: Chapter 4 – Risk Identification
Introduction
For risks to be managed, they must first be identified and assessed. Otherwise unidentified risks remain unknown and uncontrolled (Lyon, Hollcroft, 2012).
The risk management process from the ISO 31000 Risk Management standard is shown to the right.
Figure 4.1 The ISO 31000 Risk Management Process reprinted with permission from ASSP

## Slide 4: Chapter 4 – Risk Identification
Risk Identification and the ISO 31000 Series
As mentioned in previous chapters, the International Organization for Standardization (ISO) released three standards for the management of risk in 2009. These three standards which were nationally adopted by the American National Standards Institute (ANSI) in 2011 are:
  ISO Guide 73:2009 (ANSI/ASSE Z690.1-2011), Vocabulary for Risk Management
  ISO 31000:2009 (ANSI/ASSE Z690.2-2011), Risk Management Principles and Guidelines
  IEC/ISO 31010:2009 (ANSI/ASSE Z690.3-2011), Risk Assessment Techniques
It is important to remember that these standards are designed for managing risk of all types, including risks that have potential positive outcomes, as well as risk that present negative impacts.

## Slide 5: Chapter 4 – Risk Identification
Hazard Identification and the ANSI Z590.3 PtD Standard
In the American National Standard, ANSI/ASSE Z590.3-(R2016), Prevention through Design (PtD), the focus is on assessing and reducing hazard-related risks (which present negative impacts) during the design and redesign phases.
ANSI Z590.3 operates within the same principles and framework as ISO 31000 and ISO 31010.
ANSI Z590.3 is a safety standard, and incorporates the concept of ‘hazard analysis’ into the risk assessment process. ISO 31000 does not include hazard analysis, only risk analysis.

## Slide 6: Chapter 4 – Risk Identification
Hazard Identification and the ANSI Z590.3 PtD Standard
In addition to identifying hazards, ANSI Z590.3, Section 7.5 includes the need to ‘Consider the Failure Modes’ as part of the identification process. Failure mode refers to a state or condition where a system fails to perform correctly possibly resulting in harm. Failure modes include functions that do not perform within a defined parameter, perform inadequately or intermittently, or do not perform as intended.
The differences and relationship between hazards and risks are important to understand. Risks are derived from the exposure to hazards.

## Slide 7: Chapter 4 – Risk Identification
Hazard Identification and the ANSI Z590.3 PtD Standard
PtD Standard is unique in that it is designed to be applied throughout the life-cycle of a system including 1) the pre-operation stage, 2) operational stage, and 3) post incident and/or post operational stages. The standard also contains the hierarchy of controls concept used for selecting and applying the most effective controls for the hazard.
For these reasons, Z590.3 provides guidance that is more closely aligned with the roles and responsibilities of OSH professionals, while the ISO 31000 standards provide broader overarching guidance in enterprise risk management.

## Slide 8: Chapter 4 – Risk Identification
Hazard/Risk Identification
Hazard/risk identification involves finding, anticipating, recognizing, and describing hazards that could affect the achievement of an organization’s objectives. Specifically, the process of hazard identification (illustrated in the next slide) includes identifying the following:
  existing and potential hazards
  potential exposures to hazards
  possible failure modes
  events or circumstances that can cause or trigger a failure mode or present an exposure
  existing controls
  potential consequences

## Slide 9: Chapter 4 – Risk Identification
Hazard/Risk Identification

## Slide 10: Chapter 4 – Risk Identification
Hazard/Risk Identification
Existing and Potential Hazards – Identification of hazards is the most important step in risk assessment.
If hazards, the source of risk, are not recognized and identified, risks cannot be assessed, reduced and managed. The identification of existing and potential hazards within the context of the assessment should be performed.
In addition to listing these hazards, a description or characterization of the hazards should be included.
There are many references and resources for common categories of hazards including the list in OSHA’s “Job Hazard Analysis”, Appendix 2 found in Publication 3071 at https://www.osha.gov/Publications/osha3071.pdf

## Slide 11: Chapter 4 – Risk Identification
Hazard/Risk Identification
Exposures to Hazards – The existence of a hazard alone does not necessarily translate to a risk. Risk is derived from the ‘exposure’ to a hazard. Therefore, in addition to identifying the hazards, the potential exposure to people, property, assets, the environment, and other things of value must also be identified. Exposure to hazards can occur in various ways including:
  direct contact with hazard
  indirect contact with hazard
  proximity to hazard
  duration of exposure
  magnitude of exposure
  concentration or dose of exposure

## Slide 12: Chapter 4 – Risk Identification
Hazard/Risk Identification
Possible Failure Modes – The potential ways a system, product, or element can fail and lead to harm should be identified and described. Failure modes are the state or condition where a system fails to perform as expected or deviates from its design tolerances resulting in a potential for harm or a hazardous event. To identify possible failure modes, the assessor should consider how the process or product can fail in a way that will lead to harm. A simple ‘what-if’ approach can be used to help identify potential failures in a system by exploring various ways something might fail. Examples of failure modes include:
  pre-mature operation (i.e. unexpected startup or release of energy)
  failure to start operation (i.e. sump pump fails to operate when water level rises beyond flood level)
  failure to stop operations (i.e. press brake fails to stop when interlock is activated)
  failure during operation (i.e. local exhaust system fails during welding operation)
  degraded or deterioration of operation (i.e. leak in containment vessel)
  exceeded capability/capacity of operation (i.e. over pressurization of vessel)
  reasonably foreseeable uses and misuses of operation (i.e. using forklift to raise worker to reach component)

## Slide 13: Chapter 4 – Risk Identification
Hazard/Risk Identification
Causes or Triggers – It is important to understand the circumstances, conditions, actions or inactions that can cause exposure to a hazard or trigger a hazardous event. Hazards can be acute in nature causing immediate harm from a single exposure, while cumulative-type hazards develop gradually from prolong or repeated exposure. A simple causal analysis can be used to help identify causes that can lead to hazard exposure. Basic causes may include:
  Machinery - design, selection, condition, use, maintenance
  Human – actions, inactions, knowledge, skill, capability, attention, interaction, communication
  Management – direction, supervision, enforcement, communication
  Methods – design, system, process, procedure, task, consistency
  Materials – elements/constituents, selection, handling, storage, use, disposal
  Environment – design/layout, condition, external factors

## Slide 14: Chapter 4 – Risk Identification
Hazard Identification Methods
A number of formal and informal hazard/risk identification techniques are available including those mentioned in this manual and in ISO 31010 as illustrated in Figure to the right. Each method varies in complexity, application, strengths and limitations. The context of the assessment should be considered when selecting methods. In some cases, more than one technique may be needed to properly identify hazards and risks (Lyon, Popov, 2016).

## Slide 15: Chapter 4 – Risk Identification
Conducting Hazard/Risk Identification
Hazard identification can be used as a stand-alone technique or as an initial step in more detailed risk assessment methodologies. OSH professionals should have a firm knowledge of hazard types, causes, and consequences as well as experience in identification methods. A systematic approach to identifying hazards and their related elements is recommended. The following systematic steps are adapted from the MIL-STD-882E standard Task 101:
  Develop Plan
  Define Responsibilities
  Initiate Hazard Identification Process
  Record and Track Hazards
  Communicate Results

## Slide 16: Chapter 4 – Risk Identification
TOOLS USED TO IDENTIFY RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #7: Brainstorming
Purpose: Brainstorming is a process commonly used to stimulate and generate a free-flowing dialogue to collect and identify a list of ideas. It is used to generate as many ideas as possible regarding a particular concern or problem. Brainstorming sessions are a relatively quick and easy way of collecting ideas. In risk assessment, it is used to generate a list of potential failures, hazards, risk and controls.
Application: Brainstorming sessions are often used as an initial identification method in a sequence of other analysis and assessment methods. To allow free flow of ideas, the session requires an environment free of criticism or judgment of ideas/items and should encourage participation and creative thinking.

## Slide 17: Chapter 4 – Risk Identification
TOOLS USED TO IDENTIFY RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #7: Brainstorming
Process: Brainstorming is generally performed by a qualified, knowledgeable group of stakeholders and is either structured or non-structured.
A skilled facilitator can vastly improve the outcome of a brainstorming effort.
Figure 4.5 Brainstorming Process

## Slide 18: Chapter 4 – Risk Identification
TOOLS USED TO IDENTIFY RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #8: Delphi Technique
Purpose: The Delphi Technique is used to gain a consensus on a subject matter from a group of knowledgeable stakeholders or experts. The technique uses a series of questionnaires to collect and collate opinions from a group of experts. An important aspect of the technique is that opinions are made independently and anonymously while having access to the other opinions or views during the process.
Application: The method is used for complex problems or systems to identify risk where expert judgment is needed. It can be used to identify risks, threats and opportunities and to gain consensus view on the likelihood and consequences of future events. It has application in reconciling differences among experts, generating consensus on decisions such as selection of risk treatments, and in developing forecasts and policies.

## Slide 19: Chapter 4 – Risk Identification
TOOLS USED TO IDENTIFY RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #8: Delphi Technique
Process: The Delphi Method works through a number of cycles of anonymous written discussion and argument, managed by a facilitator. Participants in the process do not meet, or even necessarily know who else is involved: the facilitator controls the process, and manages the flow and consolidation of information. The anonymity and remoteness of the process helps to avoid issues of groupthink and personality conflict. More than this, it gives people time to think issues through properly, critique arguments rigorously and contribute fully. The process steps are listed in the next slide.

## Slide 20: Chapter 4 – Risk Identification
TOOLS USED TO IDENTIFY RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #8: Delphi Technique
Figure 4.6 Delphi Technique Process

## Slide 21: Chapter 4 – Risk Identification
TOOLS USED TO IDENTIFY RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #9: Hazard Identification Study (HAZID)
Purpose: A hazard identification study or HAZID is a qualitative, structured technique using guide words and/or checklists for early identification of existing and potential hazards, their causes and consequences. It purpose is to anticipate, identify and list hazards associated with an operation, system, product or task in the first step of the risk assessment.
Application: HAZID is used early in the process for existing operations as well as conceptual or design phase efforts. It is often used in advance of other risk assessment methods. The technique can include a qualitative analysis to determine the potential severity and likelihood of occurrence which is sometimes referred to as a Risk Identification Study or RISKID.

## Slide 22: Chapter 4 – Risk Identification
TOOLS USED TO IDENTIFY RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #9: Hazard Identification Study (HAZID)
Process: HAZID is generally conducted by an experienced multi-discipline team using documents, diagrams, guide words, checklists, and brainstorming to identify hazards, causes, consequences and controls. Generally, an experienced facilitator and team are used in a workshop setting. The specific part or node of an operation is selected for the study. The process steps are represented in below

## Slide 23: Chapter 4 – Risk Identification
TOOLS USED TO IDENTIFY RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #9: Hazard Identification Study (HAZID)
Figure 4.8 HAZID Flow Chart

## Slide 24: Chapter 4 – Risk Identification
TOOLS USED TO IDENTIFY RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #10: Design Safety Review
Purpose: A design safety review is used to anticipate and identify potential hazards during the design and redesign process of new facilities, expansions in existing buildings, new or modified processes and systems, equipment and machines, and products. The purpose of a Design Safety Review is to avoid anticipated hazards through design of a new system or redesign of an existing system.
Application: Design safety reviews are most effective when performed at an early stage when design objectives are being discussed according to Z590.3, and should be considered in any major planned changed.

## Slide 25: Chapter 4 – Risk Identification
TOOLS USED TO IDENTIFY RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #10: Design Safety Review
Process: The design safety review process is a systematic method used to anticipate, identify, avoid, eliminated or controlled hazards at the design stage. Management commitment and support are required to integrate prevention through design concepts.
Figure 4.10 Design Safety Review Process Steps

## Slide 26: Chapter 4 – Risk Identification
References
ANSI/ASSE/AIHA Z10-2012 (R2017). American National Standard—Occupational Health and Safety Management Systems. Fairfax, VA: American Industrial Hygiene Association, 2012.
ANSI/ASSE Z590.3-2011 (R2016). Prevention through Design: Guidelines for Addressing Occupational Hazards and Risks in Design and Redesign Processes. Des Plaines, IL: American Society of Safety Engineers, 2011.
ANSI/ASSE Z690.1-2011. American National Standard - Vocabulary for Risk Management. Des Plaines, IL: American Society of Safety Engineers, 2011.
ANSI/ASSE Z690.2-2011. American National Standard – Risk Management Principles and Guidelines. Des Plaines, IL: American Society of Safety Engineers, 2011.
ANSI/ASSE Z690.3-2011. American National Standard - Risk Assessment Techniques. Des Plains, IL: American Society of Safety Engineers, 2011.
ASSE’s Risk Assessment Institute website (http://www.oshrisk.org/videos/)
Chevron. (2013). Chevron Pipe Line Company – Hazard Analysis Procedure Available at http://www.chevronpipeline.com/pdf/hazard_analysis_procedure.pdf

## Slide 27: Chapter 4 – Risk Identification
References
Main, Bruce, W. Risk Assessment: Challenges and Opportunities. Ann Harbor, MI: Design Safety Engineering, Inc., 2012.
Manuele, Fred. A., Advanced Safety Management: Focusing on Z10 and Serious Injury Prevention. Hoboken, NJ: Wiley, 2008.
MIL-STD-882E. Standard Practice for System Safety. Washington, DC: Department of Defense, 2012.
Popov, G., Lyon, B., Hollcroft, B., Risk Assessment: A Practical Guide to Assessing Operational Risks. Hoboken, NJ: Wiley, 2016
Risk Assessments – Top 10 Pitfalls & Tips for Improvement, Bruce K. Lyon and Bruce Hollcroft, Professional Safety, December 2012, American Society of Safety Engineers
The Art of Assessing Risk: Selecting, Modifying, and Combining Methods to Assess Operational Risks, Bruce K. Lyon and Georgi Popov, Professional Safety, March 2016, American Society of Safety Engineers
OSHA. (2002). Job Hazard Analysis. Publication 3071 Washington, DC: U.S. Department of Labor, Author. Retrieved from https://www.osha.gov/Publications/osha3071.pdf