## Slide 1: Risk Management Tools for Safety Professionals – Part I, Chapter 6
RISK MANAGEMENT METHODS AND TOOLS
Chapter 6 – Risk Evaluation
Authors: Bruce K. Lyon, P.E., CSP, ARM, CHMM
Georgi Popov, Ph.D., QEP, SMS, ARM, CMC

## Slide 2: Chapter 6 – Risk Evaluation
Introduction
The ultimate purpose of risk assessment is to gain an understanding of a risk’s nature, its causes, potential severity of impacts and likelihood of occurrence, and to determine whether additional controls are necessary so that it is acceptable to the organization and to society (Lyon, Popov, 2016).
Risk evaluation is the act of reviewing the risk-based information developed from the hazard identification and risk analysis, and comparing that risk level against the organization’s established risk criteria to determine acceptability.

## Slide 3: Chapter 6 – Risk Evaluation
Introduction
The risk management process from the ISO 31000 Risk Management standard is shown to the right.
Figure 6.1 The ISO 31000 Risk Management Process reprinted with permission from ASSP

## Slide 4: Chapter 6 – Risk Evaluation
Risk Evaluation and the ISO 31000 Risk Management Standards
Risk Assessment Techniques, risk evaluation is the process of comparing estimated risk levels with an established baseline - the defined risk criteria in context of the assessment - to determine the appropriate action (ISO 31010/ANSI/ASSE Z690.3-2011).
Risk is evaluated using the estimated risk levels of consequences and likelihood of occurrence developed in the hazard/risk identification and risk analysis phases.
The understanding of the nature and magnitude of risk derived from the risk analysis is used to decide whether a particular risk is acceptable and what future actions are required.

## Slide 5: Chapter 6 – Risk Evaluation
Risk Evaluation and the ISO 31000 Risk Management Standards
Methods for defining risk criteria can range from simple two risk categories (those requiring treatment, and those that do not require treatment), to more complex methods using multiple risk levels with graduated degrees of actions. ISO 31010 presents a simple concept of dividing risks into three bands used in evaluating risk. These categories can be described as follows:
  unacceptable - where the activity is to be avoided or reduced before continuing
  marginal or ALARP – where the costs and benefits of further risk treatment are evaluated before continuing
  acceptable – where the risk level is considered negligible requiring no further risk treatment

## Slide 6: Chapter 6 – Risk Evaluation
Risk Evaluation and the ISO 31000 Risk Management Standards
Example of dividing risks into three bands used in evaluating risk
Figure 6.2 The ALARP Model reprinted with permission from ANSI/ASSE Z690.3-2011 (Courtesy of the ASSP) and Fred Manuele

## Slide 7: Chapter 6 – Risk Evaluation
Risk Evaluation and the ISO 31000 Risk Management Standards
Many organizations use risk assessment matrices or heat maps based on defined risk criteria to visually compare risk levels within the graduated risk level categories (Lyon, Popov, 2017).
Examples are presented here
Figure 6.3, Qualitative Risk Matrix (5x4) Example reprinted from MIL-STD 882E
Semi-quantitative Risk Matrix (5x6) Example from ANSI/ASSE Z690.3-2011
Numerical Scoring Risk Matrix (5x5) Example reprinted with permission from ANSI/ASSE Z590.3-2011 (R2016)

## Slide 8: Chapter 6 – Risk Evaluation
Prevention through Design and Risk Evaluation
The ANSI Z590.3-2011 (R2016) PtD standard’s approach to risk assessment follows the basic concepts found in ISO 31000, however, from a OSH perspective. Risk assessment includes the sequential steps of
1) hazard identification,
2) hazard and risk analysis and
3) risk evaluation.
However, the ANSI Z590.3 risk assessment model (which was originally adapted from Bruce Main, 2004) differs slightly with several additional steps as illustrated in the next slide

## Slide 9: Chapter 6 – Risk Evaluation
Prevention through Design and Risk Evaluation
Comparison of ISO 31000 and ANSI Z590.3 Risk Assessment Processes

## Slide 10: Chapter 6 – Risk Evaluation
Evaluating Risk in Risk-based Decision Making
Using the defined risk criteria and results of the risk analysis, an evaluation of the risk is performed.
The evaluation process involves comparing the estimated risk level with the organization’s established acceptable risk level to determine if the risk is acceptable, and prioritizing actions for those risk that are not acceptable.
After risk treatment, the risk is again evaluated to determine if it is acceptable.

## Slide 11: Chapter 6 – Risk Evaluation
Evaluating Risk in Risk-based Decision Making
Considerations in evaluating risk should include the following as identified in ANSI-ASIS-RIMS RA.1-2015, Risk Assessment Standard:
  the objectives of project
  both tangible and intangible effects
  legal, regulatory, and contractual requirements
  critical control points
  tolerability of risks to external stakeholders or society
  whether a risk needs treatment
  deciding whether risk is acceptable
  whether an activity should continue
  priorities for treatment

## Slide 12: Chapter 6 – Risk Evaluation
Evaluating Risk in Risk-based Decision Making
For risks that are deemed unacceptable, a decision to immediately stop and discontinue the operation or process until the risk is reduced to a level acceptable to the organization.
Figure 6.7, Risk-based Decision Making process

## Slide 13: Chapter 6 – Risk Evaluation
Risk Evaluation Methods
Risk can be evaluated using a variety of tools, some of which are covered in this chapter. ISO 31010 lists a number of techniques ranging in application, complexity and ease of use. Figure 6.8 illustrates several methods for risk evaluation as well as Table 6.1 (next slide)
Figure 6.8, Risk Evaluation methods and the ISO 31000 Risk Management Process adapted and reprinted with permission from ASSP

## Slide 14: Chapter 6 – Risk Evaluation
Risk Evaluation Methods
Table 6.1
Table 6.1. Methods used to Evaluate Risks

## Slide 15: Chapter 6 – Risk Evaluation
TOOLS USED TO EVALUATE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #17: Risk Indices
Purpose: A risk index refers to the combined likelihood and severity of a hazardous event or consequence, anticipated from an identified hazard.
A risk index is used to rank and compare risks as part of the risk evaluation. Its main purpose is to help distinguish those risks which are unacceptable to the organization, and provide a ranking of risks by risk level to prioritize treatment.
Risk indices are developed to summarize the risk of an event or condition by using numbers or categorical values for the purpose of identifying and comparing risks. Indices can be qualitative using word descriptors, letters and colors, or semi-quantitative featuring numerical rankings or measures to describe and communicate the level of risk to stakeholders and decision makers.

## Slide 16: Chapter 6 – Risk Evaluation
TOOLS USED TO EVALUATE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #17: Risk Indices
Application: Often included in risk scorecard and formulas, risk indices can be used to calculate the index values and further evaluate risk.
They are often specific to a particular type of risk and used to compare different situations where that risk occurs.
While numbers are used, this is simply to allow for manipulation. In cases where the underlying model or system is not well known or not able to be represented, it is usually better to use a more overtly qualitative approach which does not imply a level of accuracy which is impossible using ordinal scales.

## Slide 17: Chapter 6 – Risk Evaluation
TOOLS USED TO EVALUATE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #17: Risk Indices
Process: The risk measures that drive or influence the risk are selected to form the index. To form an index, an understanding of the risk sources, and how consequences can occur is required. In other words, the ‘risk measures’ (how the risk is measured) must be identified. A ‘risk measure’ is a numerical summary of risk, while a ‘risk index’ can also be a real number or a vector of real numbers, but it is often composed of numbers, letters, words, or colors to better communicate risk to the user. A risk measure is considered a subset of risk indices (MacKenzie, 2014.)

## Slide 18: Chapter 6 – Risk Evaluation
TOOLS USED TO EVALUATE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #17: Risk Indices
Process: One such example is the OSHA Heat Index. It uses an index system developed by the U.S. National Oceanographic and Atmospheric Administration (NOAA) that combines both air temperature and relative humidity into a single value that indicates the apparent temperature in degrees Fahrenheit, or how hot the weather will feel.
Figure 6.9, NOAA’s Temperature and Humidity Index
Figure 6.10, OSHA’s Heat Index Summary

## Slide 19: Chapter 6 – Risk Evaluation
TOOLS USED TO EVALUATE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #17: Risk Indices
Examples

## Slide 20: Chapter 6 – Risk Evaluation
TOOLS USED TO EVALUATE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #17: Risk Indices
Process: When selecting or developing a risk index, the following steps should be considered:

## Slide 21: Chapter 6 – Risk Evaluation
TOOLS USED TO EVALUATE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #18: Risk Heat Maps
Purpose: A risk heat map is a table or matrix that uses colors representing risk levels. Its primary purpose is to visually communicate risk rankings to decision makers in their evaluation and treatment of risk.
Application: Risk heat maps are generated from risk indices and risk analyses such as What-if analyses, FMEAs and Process Hazard Analyses. They are used by decision makers and stakeholders in the evaluation, prioritization and treatment of risks.

## Slide 22: Chapter 6 – Risk Evaluation
TOOLS USED TO EVALUATE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #18: Risk Heat Maps
Process: Individual risks are plotted on the heat map grid according to the colors corresponding to the level of the risk. The heat map is typically constructed as a two dimensional matrix with an axis measuring severity of risk and an axis measuring the frequency or likelihood of occurrence. The number of levels for each axis can range from a simple 2 x 2 or 3 x 3 model to a more granular model. The established risk criteria and risk level definitions developed by the organization are used to characterize the heat map risk levels.

## Slide 23: Chapter 6 – Risk Evaluation
TOOLS USED TO EVALUATE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #18: Risk Heat Maps
Process: The risk scores produced from the risk analysis tool (such as the RISKID presented in Figure 6.12) are plotted in the risk heat map (Figure 6.13) for visual comparison.
Figure 6.12, RISKID Risk Analysis Tools used to produce risk scores for Risk Heat Map
Figure 6.13, Risk Heat Map showing risk scores produced from the risk analysis

## Slide 24: Chapter 6 – Risk Evaluation
TOOLS USED TO EVALUATE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #19: ALARP
Purpose: ALARP is the concept of achieving a risk level of 'as low as reasonably practicable'. It is defined by ANSI Z590.3 as ‘that level of risk which can be further lowered only by an increase in resource expenditure that is disproportionate in relation to the resulting decrease in risk’ (ANSI Z590.3-2011 (R2016).)
The concept of ALARP was originally developed in the United Kingdom’s Health and Safety at Work 1974 Act and further developed by the UK Health and Safety Executive.

## Slide 25: Chapter 6 – Risk Evaluation
TOOLS USED TO EVALUATE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #19: ALARP
Application: The ALARP model illustrated in the Figure to the right is used to classify risks as belonging to specific categories ranging from 4) Unacceptable Risk where further risk assessment and risk reduction are required before operations can continue; 3) ALARP Risk which is given highest priority for risk reduction; 2) ALARP Risk which further risk reduction is taken at appropriate time; and 1) Very Low Risk that is broadly acceptable and risk reduction discretionary.
ALARP Model

## Slide 26: Chapter 6 – Risk Evaluation
TOOLS USED TO EVALUATE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #19: ALARP
Process: The ALARP concept is used to assist organizational decision making in order judge whether the level of risk is acceptable, as low as reasonably practicable, or unacceptable.
It is applied within the context of the organization’s culture and workplace environment, as well as industry norms, regulatory requirements, and community setting.

## Slide 27: Chapter 6 – Risk Evaluation
TOOLS USED TO EVALUATE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #19: ALARP
Process:
Risk Criteria using ALARP concept

## Slide 28: Chapter 6 – Risk Evaluation
References
ANSI/ASSE Z590.3-2011 (R2016). Prevention through Design: Guidelines for Addressing Occupational Hazards and Risks in Design and Redesign Processes. Des Plaines, IL: American Society of Safety Engineers, 2011.
ANSI/ASSE Z690.1-2011. American National Standard - Vocabulary for Risk Management. Des Plaines, IL: American Society of Safety Engineers, 2011.
ANSI/ASSE Z690.2-2011. American National Standard – Risk Management Principles and Guidelines. Des Plaines, IL: American Society of Safety Engineers, 2011.
ANSI/ASSE Z690.3-2011. American National Standard - Risk Assessment Techniques. Des Plains, IL: American Society of Safety Engineers, 2011.
ASSE’s Risk Assessment Institute website (http://www.oshrisk.org/videos/)
Communicating & Managing Risk: The Key Result of Risk Assessment, Bruce K. Lyon and Georgi Popov, Professional Safety, November 2017, American Society of Safety Engineers
Health & Safety Executive, 2006. The development of a fatigue / risk index for shiftworkers, http://www.hse.gov.uk/research/rrhtm/rr446.htm
Highly Unusual: CSB’s Comments Signal Long-Term Effects on the Practice of Safety, Manuele, Fred. A., Professional Safety, March 2017, American Society of Safety Engineers

## Slide 29: Chapter 6 – Risk Evaluation
References
ANSI/ASSE Z590.3-2011 (R2016). Prevention through Design: Guidelines for Addressing Occupational Hazards and Risks in Design and Redesign Processes. Des Plaines, IL: American Society of Main, Bruce, W. Risk Assessment: Basics and Benchmarks. Ann Harbor, MI: Design Safety Engineering, Inc., 2004.
Summarizing Risk Using Risk Measures and Risk Indices. MacKenzie, Cameron A., Calhoun: The NPS Institutional Archive DSpace Repository, 2014, Calhoun Institutional Archive of the Naval Postgraduate School at file:///F:/ASSE%20Risk%20Management%20Manual/Chapter%206.%20Risk%20Evaluation/risk%20indices.pdf
MIL-STD-882E. Standard Practice for System Safety. Washington, DC: Department of Defense, 2012.
Popov, G., Lyon, B., Hollcroft, B., Risk Assessment: A Practical Guide to Assessing Operational Risks. Hoboken, NJ: Wiley, 2016
Risk Assessments – Top 10 Pitfalls & Tips for Improvement, Bruce K. Lyon and Bruce Hollcroft, Professional Safety, December 2012, American Society of Safety Engineers
The Art of Assessing Risk – Selecting, Modifying and Combining Risk Assessment Methods to Assess Risk, Bruce K. Lyon and Georgi Popov, Professional Safety, March 2016, American Society of Safety Engineers
Oregon State University Enterprise Risk Services, (2014) Risk Assessment Tool available at file http://risk.oregonstate.edu/risk-assessment-tool
OSHA, 2015. Using the Heat Index. Available at: https://www.osha.gov/SLTC/heatillness/heat_index/using_heat_protect_workers.html
U.S. NRC. (2017) ALARA. NRC Library. https://www.nrc.gov/reading-rm/basic-ref/glossary/alara.html