## Slide 1: Risk Management Tools for Safety Professionals – Part I, Chapter 7
RISK MANAGEMENT METHODS AND TOOLS
Chapter 7 – Risk Treatment
Authors: Bruce K. Lyon, P.E., CSP, ARM, CHMM
Georgi Popov, Ph.D., QEP, SMS, ARM, CMC

## Slide 2: Chapter 7 – Risk Treatment
Introduction
Risk treatment involves the selection and application of risk reduction measures for a risk which is judged to be unacceptable. It is the end result or output of the risk assessment process used to control the identified hazard and reduce its risk.
Without acting upon the risk assessment’s findings and treating risk, a risk assessment is of no value, and in fact may lead to negligence of the organization (Popov, Lyon, Hollcroft, 2016).

## Slide 3: Chapter 7 – Risk Treatment
Introduction
The risk management process from the ISO 31000 Risk Management standard is shown to the right.
Figure 7.1 The ISO 31000 Risk Management Process reprinted with permission from ASSP

## Slide 4: Chapter 7 – Risk Treatment
American Society of Safety Engineers)
The Treatment of Risk
Risk treatment is defined by ISO Guide 73 (ANSI/ASSE Z690.1-2011) as the ‘process to modify risk’. For operational and hazard risks, the process to modify risk involves the selection and application of one or more treatment options to reduce risks to a level that is acceptable to the organization. ISO Guide 73 provides several notes (next 2 slides) that further describe risk treatment options.

## Slide 5: Chapter 7 – Risk Treatment
American Society of Safety Engineers)
The Treatment of Risk
NOTE 1: Risk treatment can involve:
  avoiding the risk by deciding not to start or continue with the activity that gives rise to the risk;
  taking or increasing risk in order to pursue an opportunity;
  removing the risk source (3.5.1.2);
  changing the likelihood (3.6.1.1);
  changing the consequences (3.6.1.3);
  sharing the risk with another party or parties [including contracts and risk financing (3.8.1.4)]; and
  retaining the risk by informed decision.

## Slide 6: Chapter 7 – Risk Treatment
American Society of Safety Engineers)
The Treatment of Risk
NOTE 2: Risk treatments that deal with negative consequences are sometimes referred to as “risk mitigation”, “risk elimination”, “risk prevention” and “risk reduction”. (ANSI/ASSE Z690.1-2011)

## Slide 7: Chapter 7 – Risk Treatment
Risk Treatment Plans
Risk treatment plans can involve a single control or multiple risk reduction measures to accomplish the risk reduction desired. Concepts such as ‘inherently safe design’, ‘layers of protection’, ‘recognized and generally accepted good engineering practices’ and ‘safer technology and alternatives’ along with the hierarchy of controls should be incorporated into the risk treatment plan.
Risk treatment options can include the decision to ‘avoid the risk’ by choosing to not engage in the activity or exposure; ‘eliminating the risk’ by removing the risk source; ‘reducing the likelihood’ or ‘reducing the severity’; ‘sharing the risk’ among other parties such as contracts and risk financing; and ‘retaining the risk’ such as self-funding or other risk-based decisions.

## Slide 8: Chapter 7 – Risk Treatment
Recognized and Generally Accepted Good Engineering Practices
“Recognized and generally accepted good engineering practices" known as RAGAGEP was introduced by OSHA in the CFR 29, 1910.119 Process Safety Management (PSM) standard. RAGAGEP involves the selection and application of appropriate engineering, operating, and maintenance knowledge when designing, operating and maintaining chemical facilities with the purpose of ensuring safety and preventing process safety incidents. As the reader can see, the RAGAGEP approach is in alignment with the PtD concept of designing in such measures, and managing risk throughout a system’s lifecycle.

## Slide 9: Chapter 7 – Risk Treatment
Safer Technology and Alternatives
One risk reduction approach for chemical incident prevention developed and implemented by industry and stakeholders, is the promulgation of requirements for safer technology and alternatives or STAA. The concept of safer technology and alternatives has been incorporated into both the U.S. Environmental Protection Agency’s (EPA’s) Risk Management Plan standard and OSHA’s Process Safety Management standard. STAA refers to risk reduction strategies developed through analysis using a hierarchy of controls model illustrated in the figure next slide.

## Slide 10: Chapter 7 – Risk Treatment
Safer Technology and Alternatives
Adapted from the OSHA document Process Safety Management for Petroleum Refineries: Lessons Learned from the Petroleum Refinery Process Safety Management National Emphasis Program (OSHA, 2017).

## Slide 11: Chapter 7 – Risk Treatment
Identifying Risk Treatment Options
Once hazards have been identified and the risk assessed, proper risk treatment options are considered for selection and implementation. This requires the risk assessment team or decision makers to determine the options available, and their degree of risk reduction, reliability, and associated cost to implement and maintain.
Feasible control options that may reduce or eliminate the risk from the identified hazard(s) are identified using internal and external resources. Existing internal sources include the OSH professional, experienced stakeholders and operators familiar with the hazard and control methods. Input from affected workers knowledgeable in the operation, equipment or process is advised.
Outside resources such as manufacturers' literature and engineering reports; OSH-related research from institutes, and professional organizations such as ASSE and AIHA; regulatory standards and guidance; industry best practices; industry consensus standards; National Institute for Occupational Safety and Health (NIOSH) publications are also available.

## Slide 12: Chapter 7 – Risk Treatment
Selecting Risk Treatment
The primary principle that OSH professionals should apply in the selection of risk treatment is the use of the hierarchy of controls model (Lyon, Hollcroft, 2012).
Risk treatment selection requires a balancing of the overall costs, and the financial and non-financial benefits, including legal and regulatory requirements. This requires some investigation into the suppliers of the risk treatment, and associated costs including purchase price, installation, training, maintenance and services costs, as well as the expected life span of the treatment.
Risks with extremely high severity potential, but low likelihood may warrant risk treatment even when the costs of the treatment are not justified in a typical cost benefit analysis.

## Slide 13: Chapter 7 – Risk Treatment
Selecting Risk Treatment
The process of selecting risk treatment can be performed using a variety of methods, some of which are covered in this chapter and listed in ISO 31010 (ANSI/ASSE Z690.3-2011). Figure to the right illustrates several methods for selecting risk treatments as well as Table 7.1 (next slide) which provides brief descriptions of methods available.

## Slide 14: Chapter 7 – Risk Treatment
Selecting Risk Treatment
Table 7.1 provides brief descriptions of methods available.

## Slide 15: Chapter 7 – Risk Treatment
The Hierarchy of Risk Reduction Strategies
Risk treatment selection should always be linked to the concept of the hierarchy of controls to reduce risk to an acceptable level. Hazard and risk control measures vary in their degree of risk reduction, effectiveness and reliability. The hierarchy of controls (HoC) is structured with the most effective and reliable options at top and descend down to the lowest level of protection.
In descending order, the hierarchy model generally starts with avoidance of risk (excluded in some models), followed by elimination of risk, and then substitution of risk. From there, residual risks are controlled using engineering controls, warning systems (also excluded in some models), administrative controls, and personal protective equipment.’

## Slide 16: Chapter 7 – Risk Treatment
The Hierarchy of Risk Reduction Strategies
models), administrative controls, and personal protective equipment.’
A variety of models exist.
Unfortunately, there continue to be OSH textbooks and professionals that refer to engineering controls as the “highest level of control”.
It is important to recognize and understand the differences among the various HoC models. See next slides.

## Slide 17: Chapter 7 – Risk Treatment
The Hierarchy of Risk Reduction Strategies
models), administrative controls, and personal protective equipment.’
A variety of models exist.
Unfortunately, there continue to be OSH textbooks and professionals that refer to engineering controls as the “highest level of control”.
It is important to recognize and understand the differences among the various HoC models. See next slides.

## Slide 18: Chapter 7 – Risk Treatment
The Hierarchy of Risk Reduction Strategies
A variety of models exist.
Unfortunately, there continue to be OSH textbooks and professionals that refer to engineering controls as the “highest level of control”.
It is important to recognize and understand the differences among the various HoC models. See next slides.

## Slide 19: Chapter 7 – Risk Treatment
The Hierarchy of Risk Reduction Strategies
Figure 7.5, NIOSH Prevention through Design (PtD) Hierarchy of Controls Model

## Slide 20: Chapter 7 – Risk Treatment
The Hierarchy of Risk Reduction Strategies
Figure 7.6, ANSI Z10-2012 (R2017) Hierarchy of Controls Model reprinted with permission from ASSP

## Slide 21: Chapter 7 – Risk Treatment
The Hierarchy of Risk Reduction Strategies

## Slide 22: Chapter 7 – Risk Treatment
The Hierarchy of Risk Reduction Strategies

## Slide 23: Chapter 7 – Risk Treatment
The Hierarchy of Risk Reduction Strategies
Figure 7.9, ANSI Z590.3-2011 (R2016) Prevention through Design Risk Reduction Hierarchy of Controls Model reprinted with permission from ASSP

## Slide 24: Chapter 7 – Risk Treatment
The Hierarchy of Risk Reduction Strategies

## Slide 25: Chapter 7 – Risk Treatment
Risk Treatment Plans and Risk-based Decision Making
The objective of operational risk management is to implement appropriate risk reduction plans to mitigate risks associated with each decision made to achieve an acceptable risk level. OSH professionals should be able to effectively lead risk assessments, develop appropriate risk reduction strategies, and advise decisions makers in making appropriate decisions. Risk treatments (i.e. risk controls) are designed to reduce the risk of a hazard’s effects and/or reduce the likelihood of its occurrence.
A risk treatment plan should include options and alternatives that eliminate the hazard or reduce its risk.

## Slide 26: Chapter 7 – Risk Treatment
Risk Treatment Plans and Risk-based Decision Making
the OSH professional should have an alternate plan as a secondary option to present to decision makers in the event the primary plan is declined. Figure 7.11 depicts the risk-based decision making process in context to the selection of risk treatment options.
Figure 7.11, Risk-Based Decision Making Process

## Slide 27: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #20: Business Impact Analysis
Purpose: Business impact analysis (BIA) provides an understanding of the critical processes that enable an organization to achieve its objectives and provides information needed to plan an organization’s response to a disruptive event.
A BIA is used to predict the consequences of disruption of organization’s operations and processes and identifies critical information needed to develop mitigative strategies. Potential business impact scenarios should be considered during OSH risk assessment. Critical operations may also be interrupted by supply chain failure or delayed deliveries. (Example: South Korean shipper's bankruptcy crisis could affect U.S. holiday sales)

## Slide 28: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #20: Business Impact Analysis
Application: During the initial BIA, the team should consider the impact of negative OSH consequences on key business processes. The team should also consider how disruptive events will affect the capacity and capability of achieving critical business objectives? The BIA emphases on the effects or consequences of the interruption to critical business operations. An attempt should be made to quantify the financial costs and non-financial impact associated with a negative OSH outcome.
One the BIA goals is to identify costs linked to consequences of OSH failures, such as loss of cash flow, decommissioning and replacement of equipment, overtime paid to catch up with a backlog of work, business losses, reputation damage, and so on.

## Slide 29: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #20: Business Impact Analysis
Process: BIA is generally performed by a qualified, knowledgeable group of stakeholders. The goal is to identify the following key elements for BIA:
  Criticality of key business processes and objectives
  How disruptive events can affect the capacity and capability of achieving critical business objectives
  Impact Potential to People, Property and the Environment
  Disruption Duration
  Capacity and capability needed to manage the impact
  Financial and operational consequences of loss of critical processes
  Business Impact Profile or Risk Level
  Management Risk Responses: Avoid, Transfer, Accept, Mitigate
  Mitigative Measures – If the decision is to mitigate the risk
  Risk Level after Mitigative Measures

## Slide 30: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #20: Business Impact Analysis
There is no specific risk management tool provided in ISO 31010. However, the authors may suggest the following tool depicted in Figure 7.12.
Figure 7.12, Business Impact Analysis Tool

## Slide 31: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #20: Business Impact Analysis
Sometimes in the absence of data, only qualitative BIA may be considered. Another reason for qualitative approach may be lack of time or resources. An example of qualitative BIA tool is presented in Figure 7.13.
Figure 7.13, Qualitative BIA

## Slide 32: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #20: Business Impact Analysis
In most cases, some quantification may be possible. If financial data is available, it is advisable to use quantitative analysis and include financial data in the outcomes. An example based on CSB CAPECO investigation is presented in Figure 7.14. The same scenarios as in the qualitative analysis were evaluated.
Figure 7.14, Semi-quantitative BIA example.

## Slide 33: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 21: Cost-Benefit Analysis
Purpose: Cost Benefit Analysis (CBA) weighs the total expected costs of options in monetary terms against their total expected benefits in order to choose the most effective or the most profitable option (ANSI/ASSE Z690.3-2011.)
CBA is usually performed after risk assessment is completed and risk management options are identified based on PtD Hierarchy of Controls (ANSI/ASSE Z590.3-2011(R2016).)
CBA is used to choose between the risk management options. It should include direct and indirect cost of risk management activities or proposal. According to ISO 31010 direct costs are those that are directly associated with the risk management action. Indirect costs are those additional opportunity costs, such as loss of effectiveness, distraction of management time or the diversion of capital away from other potential investments (ANSI/ASSE Z690.3-2011).

## Slide 34: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 21: Cost-Benefit Analysis
Purpose: Cost Benefit Analysis (CBA) weighs the total expected costs of options in monetary terms against their total expected benefits in order to choose the most effective or the most profitable option (ANSI/ASSE Z690.3-2011.)
CBA is usually performed after risk assessment is completed and risk management options are identified based on PtD Hierarchy of Controls (ANSI/ASSE Z590.3-2011(R2016).)
CBA is used to choose between the risk management options. It should include direct and indirect cost of risk management activities or proposal. According to ISO 31010 direct costs are those that are directly associated with the risk management action. Indirect costs are those additional opportunity costs, such as loss of effectiveness, distraction of management time or the diversion of capital away from other potential investments (ANSI/ASSE Z690.3-2011).

## Slide 35: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 21: Cost-Benefit Analysis
Application: CBA is used at operational and strategic levels to help decide between options (ANSI/ASSE Z690.3-2011.) Prior to selecting and a new plant design or location, practical managers conduct a CBA to evaluate all the potential costs and revenues that may be generated if the plant is operational. CBA will determine whether the project is financially feasible or if different options should be considered.
SH&E managers can perform CBA to evaluate whether the proposed initial design or PtD intervention is financially beneficial or different option should be considered. It is advisable to evaluate three to four different proposal for financial benefits. A simple spreadsheet CBA does not require significant effort. However, complete financial analysis of more complex SH&E Interventions involves significant time in collecting SH&E costs, quality and productivity improvements.

## Slide 36: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 21: Cost-Benefit Analysis
Process: The first step of the CBA process is to compile a detailed list of all the costs and benefits associated with the project or decision. Every effort should be made to include direct and indirect costs and opportunity costs. Benefits should include all direct and indirect costs associated with proposed new design or SH&E interventions related to re-design activities.
Increased production from improved employee SH&E conditions, or increased sales due to improved reputation should be considered. It should be noted that double counting or creative accounting must be avoided. For instance, cost avoidance from reduced days away from work, restricted duty or transfer (DART) should not be counted as financial benefit as well. Cost avoidance and cash inflow are very often mixed in SH&E interventions projects.

## Slide 37: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 21: Cost-Benefit Analysis
Process: The final step of the CBA may be considered ROI calculation. CBA steps are presented in Figure 7.15 below.
Figure 7.15. CBA steps
ROI is calculated based on a simple formula:

## Slide 38: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 21: Cost-Benefit Analysis
Process: The figure below and visualizes CBA and ROI calculations.
Figure 7.16, CBA and ROI Calculations (Biofuel Project)

## Slide 39: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 22: Financial Analysis
Purpose: In financial analysis, a monetary value is assigned to all known direct and indirect costs in current state. Financial values in future state may be estimated.
OSH professionals have to be careful not to automatically assume that risk reduction percentage means the same monetary amount reduction in future state. Financial estimates may be a lot more complicated than that. In order to understand financial benefits of proposed SH&E interventions, safety professionals will have to learn to speak business management language and use common financial terminology.

## Slide 40: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 22: Financial Analysis
Application: A new tool for SH&E investment analysis was developed for this manual. The tool allows different solutions to be evaluated and prioritized. The Excel-based tool can help SH&E professionals involved in management decision making process to compare the cost before the improvements/intervention with the cost after the improvements/intervention, and calculate financial benefits and cost savings.
One way to calculate the NPV is to add net savings, new revenue (generated from increased productivity), and other benefits (maintenance, fuel savings, insurance, etc). Again, cost savings should not be confused with cash inflow.

## Slide 41: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 22: Financial Analysis
Process: Financial Analysis is generally performed by a qualified, knowledgeable group of stakeholders. The goal is to complete and calculate the following key financial elements: Cash Flow, Net Present Value (NPV), Internal Rate of Return (IRR) Return on Investment (ROI), and Payback Period (PBP). Financial Analysis steps are presented in the figure to the right.

## Slide 42: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 22: Financial Analysis
Application: A simple example of a cash flow is presented in Fig. 7.18.
Figure 7.18, Cash Flow example

## Slide 43: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 22: Financial Analysis
Application: ISO 31010 states that it is then necessary to discount the costs and benefits to bring them into ― today‘s money‖ so that a valid comparison can be made between costs and benefits. (ISO 31010) The Present Value of all Costs (PVC) and Present Value of Benefits (PVB) to all stakeholders can be combined to produce a Net Present Value (NPV) formula:

## Slide 44: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 22: Financial Analysis
Application: NPV for the safety investment can be easily calculated in Microsoft Excel. It is usually based on the Net Cash Flow. Simple Return on investment (ROI) can calculated next and is displayed as a numerical value as well as percentage. Based on the Cash Flow a variation of previously described ROI formula can be used.

## Slide 45: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 22: Financial Analysis
Application: Internal Rate of Return (IRR) is another business term and is usually considered a simplified alternative to NPV. IRR takes into account the time value of money by considering the cash flows over the lifetime of a program or intervention. It is based on the following formula:

## Slide 46: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 22: Financial Analysis
Application: The payback period (PBP) is basically the time required to recover the cost of an SH&E investment. It is based on the following formula.

## Slide 47: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 22: Financial Analysis
Application: The simple payback period does not consider the value of time; the cash flow entries are not discounted. The discounted payback period uses cash flow entries which have been discounted. PBP example of a simple ventilation system installation in the amount of $25000 is presented in Figure 7.19 below.
Figure 7.19, Example of PBP calculation

## Slide 48: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 22: Financial Analysis
Application: A worksheet to compare four different proposals was developed. NPV’s for the different proposals are compared and displayed as a numerical value, while IRR’s and ROI’s for all proposals/solutions are displayed as a percentage. An example of four different solutions is presented here.

## Slide 49: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 23: Non-Financial Benefits Analysis
Purpose: Non-financial benefits (NFB), also known as “soft” benefits, are positive business impacts that cannot be directly or easily quantified. Evaluation of non-financial benefits provides the missing link for non-profitable projects that add to a business’s sustainability.
Even though these benefits are difficult to measure or quantify, they remain very important to an organization and the OSH professionals.

## Slide 50: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 23: Non-Financial Benefits Analysis
Application: Non-financial benefits are used to help support business cases where financial benefits alone may not be sufficient. In order to show relevance, NFBs should be clearly connected or tied to an organization’s business objectives. By successfully achieving relevant NFBs, the organization is more likely to achieve its objectives. Some examples of NFBs include:
  Corporate Image and Reputation
  Risk Reduction
  Ethical and Legal Standing
  Customer and Employee Satisfaction
  Customer Loyalty
  Employee Trust
  Innovation and Creativity
  Business Sustainability and Resilience
  Low Attrition Rates (Turnover Rate)

## Slide 51: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 23: Non-Financial Benefits Analysis
Process: Non-Financial Benefits (NFB) Analysis is generally performed by a qualified, knowledgeable group of stakeholders. ISO 31010 (ANSI/ASSE Z690.3-2011), Risk Assessment Techniques standard does not contain any specific NFB tools. However, Multi-Criteria Analysis (MCA) featuring NFBs can be used to develop a stronger business case. ISO 31010 states that MCA uses a range of criteria to transparently access and compare the overall performance of a set of options.

## Slide 52: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 23: Non-Financial Benefits Analysis
Process: Non-Financial Benefits (NFB) Analysis
Figure 7.21, Non-Financial Benefits (NFB) Analysis

## Slide 53: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 23: Non-Financial Benefits Analysis
Process: MCA Forced Pairs Comparison tool
Figure 7.22, MCA Forced Pairs Comparison tool

## Slide 54: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 23: Non-Financial Benefits Analysis
Process: NFB contribution to the business objective identified and weighted with Forced Pairs Comparison tool.
Figure 7.23. NFB contribution to the business objectives – Current State (PPE)

## Slide 55: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool # 23: Non-Financial Benefits Analysis
Process: NFB contribution to the business objective identified and weighted with Forced Pairs Comparison tool.
Figure 7.24. NFB contribution to the business objectives – Future State (Powder Coating)

## Slide 56: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #24: Risk Treatment Selection Checklist
Purpose: Developed by the authors, this checklist tool is used to qualify and select risk treatment options that are most appropriate and effective. Its purpose is to simplify, standardize and strengthen the process of selecting risk controls.
Application: As a checklist method, it is useful in screening and narrowing the number of choices available to further decide on the most appropriate measures for the application. It can be applied early on in the review process of available risk control measures, and used throughout the selection process.

## Slide 57: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #24: Risk Treatment Selection Checklist
Process: The checklist process is used to review and test each risk treatment option being considered. Each checklist question is considered and answered by the risk assessment team to determine if it meets the standard of the checklist. There are 13 questions on the checklist. See next slide.

## Slide 58: Chapter 7 – Risk Treatment
TOOLS USED TO ANALYZE RISK FOR SAFETY PROFESSIONALS
Risk Management Tool #24: Risk Treatment Selection Checklist
Process: The checklist process

## Slide 59: Chapter 7 – Risk Treatment
References
AIChE, Center for Chemical Process Safety. Inherently Safer Chemical Processes: A Life Cycle Approach, Second Edition. Wiley Online Library, August, 2010 at http://onlinelibrary.wiley.com/doi/10.1002/9780470925195.app1/pdf
AIHA. Value of the Profession (VOTP) Report. 2008: Available at: https://www.aiha.org/votp_new/pdf/votp_report.pdf
AIHA. Value Strategy Manual. Fairfax, VA: AIHA, 2009
All Values Are Not Created Equal, D.E. Downs, The Synergist. October, 2006, Fairfax, VA: American Industrial Hygiene Association
ANSI/ASSE/AIHA Z10-2012 (R2017). American National Standard—Occupational Health and Safety Management Systems. Fairfax, VA: American Industrial Hygiene Association, 2012.
ANSI/ASSE Z590.3-2011 (R2016). Prevention through Design: Guidelines for Addressing Occupational Hazards and Risks in Design and Redesign Processes. Des Plaines, IL: American Society of Safety Engineers, 2011.
ANSI/ASSE Z690.1-2011. American National Standard - Vocabulary for Risk Management. Des Plaines, IL: American Society of Safety Engineers, 2011.
ANSI/ASSE Z690.2-2011. American National Standard – Risk Management Principles and Guidelines. Des Plaines, IL: American Society of Safety Engineers, 2011.
ANSI/ASSE Z690.3-2011. American National Standard - Risk Assessment Techniques. Des Plains, IL: American Society of Safety Engineers, 2011.
ANSI B11.0-2015. Safety of Machinery. Houston, TX: B11 Standards, 2015.
ASSE’s Risk Assessment Institute website (http://www.oshrisk.org/videos/)

## Slide 60: Chapter 7 – Risk Treatment
References
Communicating & Managing Risk: The Key Result of Risk Assessment, Bruce K. Lyon and Georgi Popov, Professional Safety, December 2017, American Society of Safety Engineers
Dictionary.com. Mitigation Definition. Retrieved from: http://www.dictionary.com/browse/mitigation
Executive Order 13650 Actions to Improve Chemical Safety and Security – a Shared Commitment, May 2014 at https://www.osha.gov/chemicalexecutiveorder/final_chemical_eo_status_report.pdf
Federal Emergency Management Agency (FEMA). 44 CFR Parts 201 and 206 Hazard Mitigation Planning and Hazard Mitigation Grant Program; Interim Final Rule. 2002. Retrieved from https://www.fema.gov/pdf/help/fr02-4321.pdf
Federal Emergency Management Agency (FEMA). What is Mitigation? 2017. Retrieved from: https://www.fema.gov/what-mitigation
Improving Ergo IQ: A Practical Risk Assessment Model, Bruce K. Lyon, Georgi Popov and Kevin Hanes, Professional Safety, December 2013, American Society of Safety Engineers
Investopedia: Cash Flow definition: Available at: http://www.businessdictionary.com/definition/cash-flow.html
Manuele, Fred. A., On the Practice of Safety. Hoboken, NJ: Wiley, 2003.
MIL-STD-882E. Standard Practice for System Safety. Washington, DC: Department of Defense, 2012.
National Institute for Occupational Safety and Health (NIOSH). 2015. Hierarchy of Controls. Retrieved from: https://www.cdc.gov/niosh/topics/hierarchy/
OSHA Publication 3918-08 2017. Process Safety Management for Petroleum Refineries: Lessons Learned from the Petroleum Refinery Process Safety Management National Emphasis Program. https://www.osha.gov/Publications/OSHA3918.pdf

## Slide 61: Chapter 7 – Risk Treatment
References
Risk Assessments – Top 10 Pitfalls & Tips for Improvement, Bruce K. Lyon and Bruce Hollcroft, Professional Safety, December 2012, American Society of Safety Engineers
Risk Reduction Strategies: Past, Present and Future, Roger C. Jensen, Professional Safety, January 2007, American Society of Safety Engineers
Schmidt, M.J., The Business Case Guide, 2nd Edition. Boston, MA, Solution Matrix Ltd., 2002
The Art of Assessing Risk – Selecting, Modifying and Combining Risk Assessment Methods to Assess Risk, Bruce K. Lyon and Georgi Popov, Professional Safety, March 2016, American Society of Safety Engineers
Thurstone, L.L. The Measurement of Values. Chicago, IL: University of Chicago Press. 1959
US Chemical Safety Board (CSB): Caribbean Petroleum Refining Tank Explosion and Fire. 2015. Available at: http://www.csb.gov/caribbean-petroleum-refining-tank-explosion-and-fire/
US Department of Homeland Security. Business Impact Analysis. Available at: http://www.ready.gov/business-impact-analysis
US Environmental Protection Agency (EPA). EPA 550-F-15-003 Chemical Safety Alert: Safer Technology and Alternatives, June 2015 at https://www.epa.gov/sites/production/files/2015-06/documents/alert_safer_tech_alts.pdf