## Slide 1: Risk Management Tools for Safety Professionals – Part II
STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Authors: Bruce K. Lyon, P.E., CSP, ARM, CHMM
Georgi Popov, Ph.D., QEP, SMS, ARM, CMC

## Slide 2: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Introduction
“We cannot solve our problems with the same thinking we used when we created them” Albert Einstein (https://www.brainyquote.com/quotes/quotes/a/alberteins121993.html)
Risk assessment – a science or an art? For the authors, it is a combination of both. Risk assessment requires certain skills, knowledge, and experience that are rooted in system safety, however, it also requires imagination and creativity to successfully anticipate, recognize, assess, and treat existing and potential risks (Lyon, Popov, 2016). The ability to properly select, customize and combine methods to assess operational risks provides OSH professionals a certain advantage and value to their organization.

## Slide 3: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Introduction
With the great amount of diversity and span of risks that are encountered by organizations, OSH professionals must be able to determine which tools are most appropriate for the level of complexity and the intended audience.
To be successful, the OSH professional must be somewhat familiar with the available methods, their strengths and weaknesses, as well as their application. In this section, a review of risk management methodologies is provided, along with guidelines for selecting, modifying and combining methods to achieve acceptable risk.

## Slide 4: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Methods Available
The number of risk management methods and tools available to the OSH professional is somewhat overwhelming.
Many methods are variations of a theme, used in various industries, or situations.
Certain tools have specific applications or purposes, while others are more broadly applied.
Some methods are only useful in specific elements of risk management such as ‘identification’ or ‘treatment’ while others have a broader application in the process.

## Slide 5: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Methods Available
The figure to the right provides an overview of methods and tools associated with each element of the risk management process.

## Slide 6: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
In addition to ISO 31010, other risk-related standards that identify risk assessment methods include ANSI/ASSE Z590.3-2011(R2016) Prevention through Design and ANSI/ASSE Z10-2012(R2017) Occupational Health and Safety Management Systems. Table II.2 provides a comparison of risk assessment methods listed in the three standards. See Part II for details.

## Slide 7: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Table II.2 provides a coded scale for applicability to each component of the risk assessment process for methods covered by ISO 31010, Z590.3 and Z10. (Table codes: SA = Strongly Applicable; A = Applicable; Blank Cells = Not Applicable)

## Slide 8: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Table II.2 (Cont.) provides a coded scale for applicability to each component of the risk assessment process for methods covered by ISO 31010, Z590.3 and Z10. (Table codes: SA = Strongly Applicable; A = Applicable; Blank Cells = Not Applicable)

## Slide 9: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Table II.3, Applicability and Complexity of Methods included in this Manual

## Slide 10: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Table II.3, Applicability and Complexity of Methods included in this Manual (Cont.)

## Slide 11: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Criteria for Selecting Methods
Selection criteria should include the:
  1) process step(s),
  2) application,
  3) complexity of the system,
  4) criticality of exposure,
  5) output necessary to make decision, and
  6) the resources available.

## Slide 12: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS

## Slide 13: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Selecting a Risk Scoring System
As discussed in Chapter 3, a risk scoring system is used to provide a standardized way of measuring and comparing risks.
Such a system provides a consistent and reliable method of risk scoring output that is used by decision makers to manage risk.

## Slide 14: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Selecting a Risk Scoring System
When selecting a risk scoring formula and system, the following variables which are briefly described should be considered.
Qualitative Systems - Qualitative risk models are based on qualitative or subjective descriptions and define risk factor levels using descriptive words such as “high”, “medium” and “low” which are evaluated according to qualitative criteria. These are often used for quick determinations or low-criticality situations.

## Slide 15: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Selecting a Risk Scoring System
When selecting a risk scoring formula and system, the following variables which are briefly described should be considered.
Semi-quantitative Systems - These risk models use qualitative data that is expressed in numerical ratings using a formula to produce a risk score. Advantages of semi-quantitative models include the ability to provide more precision in definitions by including numerical ranges for severity and likelihood, as well as the ability to more easily compare and communicate risk levels. Such semi-quantitative values are determined using qualified judgements and experience and do not rely on quantitative data which is often difficult to obtain.

## Slide 16: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Selecting a Risk Scoring System
When selecting a risk scoring formula and system, the following variables which are briefly described should be considered.
Quantitative Systems - True quantitative risk scoring models are rare since the degree of statistical data and resources necessary to support the quantitative analysis is difficult to obtain or justify. Such models are generally used for high criticality risks where such information is available.

## Slide 17: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Selecting a Risk Scoring System
When selecting a risk scoring formula and system, the following variables which are briefly described should be considered.
Qualitative Systems - Qualitative risk models are based on qualitative or subjective descriptions and define risk factor levels using descriptive words such as:
Two-factor Systems – Risk factors are the variables used to measure risk and produce a risk score. Such factors generally consist of severity of harm, and likelihood or probability of occurrence. Common two-factor risk calculation systems use likelihood (L) or probability (P) of an event occurrence and the severity of consequence (S) to determine risk level. The risk factors can be multiplied or added to produce the risk score.

## Slide 18: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Selecting a Risk Scoring System
When selecting a risk scoring formula and system, the following variables which are briefly described should be considered.
Multiple-factor Systems - More complex systems using three or more risk factors are sometimes selected to incorporate specific factors such as frequency, failure detectability, or control effectiveness. Some of the risk factor variables used include:
  Exposure (E) - measure of exposure events/units.
  Frequency of Exposure (F) - number of exposure events for a unit of time.
  Time Duration of Exposure (T) - time period that a single exposure occurs.
  Vulnerability (V) - weaknesses in a system that are factored into the risk estimation.
  Detection of Failure (D) - estimate of how easily the potential failure could be detected prior to its occurrence.
  Control Reliability (CR) - the reliability of a selected control into the risk estimation.
  Prevention Effectiveness (PE) - a controls effectiveness in preventing a failure from occurring.
  Avoidance (A) – ability to avoid exposure

## Slide 19: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
A Comparison of Risk Scoring Formulas
Various risk scoring formulas and systems are available from operational risk management consensus standards, guidelines, institutes and books. The following scenario is applied to several different scoring systems to illustrate the similarities and difference of systems.
Scenario - Plasma Cutting Welded Parts

## Slide 20: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
A Comparison of Risk Scoring Formulas
Scenario - Plasma Cutting Welded Parts – Qualitative Assessment MIL 882E
• Using the scenario factors, the electrical shock hazard is first assessed without controls as a catastrophic severity category 1 (potential for death), and a probability level category B (probable) resulting in a ‘High’ risk level.
• Considering the existing single engineering control, grounding, the risk is assessed as a severity category 1 and a probability category C resulting in a ‘High’ risk level.
• Resulting residual risk change – no change – still a ‘high’ risk category.

## Slide 21: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
A Comparison of Risk Scoring Formulas
Scenario - Plasma Cutting Welded Parts – Qualitative Assessment ANSI B11
• Using the scenario, the exposure is assessed without controls and rated catastrophic severity and likely probability. Risk level is ‘high’.
• Considering the single engineering control – grounded equipment – the ratings are catastrophic severity and unlikely probability. Risk level is ‘medium’.
• Residual risk change is 75% from ‘high’ to ‘medium’.

## Slide 22: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
A Comparison of Risk Scoring Formulas
Scenario - Plasma Cutting Welded Parts – Semi-Quantitative – PtD
• Using the scenario factors, the exposure is assessed without controls and rated catastrophic severity level 5 (potential death) and likely exposure probability level 4 resulting in a ‘very high’ risk level of 20.
• Considering the single engineering control, the scenario is assessed at a severity level 5 and an exposure probability level 3 resulting in a 15, still a ‘very high’ risk.
• Residual risk change of 75% but still in the ‘very high’ risk category.

## Slide 23: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
A Comparison of Risk Scoring Formulas
Authors’ Risk Scoring System using a Protection Factor - A risk scoring system developed by the authors is presented using the formula Severity x Likelihood x Protection Factor = Risk.
  Assessing the scenario without controls, the severity level is rated a catastrophic level 5, a likelihood level 4, and a protection factor of 1.0, resulting in a ‘very high’ risk level of 20.
  Considering the single engineering control, the scenario is assessed with a severity level of 5, a likelihood level 4, and a protection factor of 0.7 resulting in a ‘high’ risk level of 14.
  Residual risk change is 70% reducing the risk category from ‘very high’ to ‘high’ risk.

## Slide 24: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
A Comparison of Risk Scoring Formulas
Fred Manuele’s Formula from Advanced Safety Management – Manuele presents a three factor risk scoring system using probability (P), frequency of exposure (F) and severity (S). Manuele describes his attempts to maintain a proper weighting of severity by using the formula (P + F) x S = Risk Score.
  Assessing the scenario without controls, the probability level is estimated as likely (9), the frequency of exposure is estimated as often (13) and severity is rated as catastrophic (50). The ratings are entered into the formula to calculate the risk score as follows: (9 + 13) x 50 = 1100 which is in the ‘high’ risk category.
  Considering the single engineering control, the probability is rated as remote (1), with frequency and severity remaining unchanged. The resulting score, (1 +13) x 50 = 700, is ‘serious’ risk category.
  Residual risk change is 64% reducing the risk category from ‘high’ to ‘serious’.

## Slide 25: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Modifying Methods
While there are many methods and tools to choose from, it is rare that any are used without some degree of customization to fit the needs of a specific application.
Every risk management tool has certain variables, including strengths and weaknesses that can modify to optimize effectiveness, and serve the organization’s objectives.
Certain characteristics may be missing in a method that if were present would increase the method’s effectiveness. Such weaknesses or missing components can be opportunities for OSH professionals to incorporate enhancements or additions to tools in addressing risk management needs.

## Slide 26: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Modifying Methods
Example #1: Job Hazard Analysis and Job Risk Assessment
A simple example of customizing a commonly used method follows. Job hazard analysis (JHA) is a ‘hazard analysis’ method that can be upgraded and modified to be a ‘job risk assessment’ (JRA) – next slide.

## Slide 27: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Modifying Methods
Example #1: Job Hazard Analysis and Job Risk Assessment
A simple example of customizing a commonly used method follows. Job hazard analysis (JHA) is a ‘hazard analysis’ method that can be upgraded and modified to be a ‘job risk assessment’ (JRA).

## Slide 28: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Modifying Methods
Example #2: Preliminary Hazard Analysis and Preliminary Job Risk Assessment
According to ISO 31010, preliminary hazard analysis (PHA) is a simple method used to identify hazards and their risk early in the development of a project or to prioritize hazards and risk for further analysis. One of its strengths is the use of a before and after controls risk estimation. PHAs provide a comparative analysis of pre-control risk level and post-control risk level assessments for hazards associated with each task that helps communicate the importance of controlling higher-risk tasks and applying available resources where they are most beneficial. The comparison of before and after controls reveals the importance of following prescribed measures and controls. This modification can be added to other tools. One such example is a preliminary job risk assessment (PJRA) illustrated in Figure II.6 (next slide).

## Slide 29: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Modifying Methods
Example #2: Preliminary Hazard Analysis and Preliminary Job Risk Assessment

## Slide 30: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Modifying Methods
Example #3: Bow Tie Analysis with Risk Scoring
One method that has received attention lately is Bow Tie Analysis partially due to its ability to show the whole picture of a specific hazardous event. A conventional Bow Tie Analysis is a combination of a fault tree analysis (left side of bow-tie) and event tree analysis (right side) used to provide a clear illustration of the risk pathways and control measures in place for situations that do not require a full quantitative fault tree analysis.
Two short-comings of the Bow Tie analysis are that it typically lacks a risk scoring mechanism, and that the effectiveness of control measures is not reflected in the analysis. Higher level controls such as elimination, substitution and engineering are not distinguished from lower level controls such as administrative and PPE which can lead to improper decision making. (Lyon, Popov, 2017)

## Slide 31: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Modifying Methods
Example #3: Bow Tie Analysis with Risk Scoring
To emphasize the importance of the hierarchy of controls, the example of a modified Bow Tie developed by the authors is shown in Figure II.9.

## Slide 32: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Combining Methods
Seldom does one tool adequately meet all the requirements of an entire job, whether it is in construction, manufacturing, or the risk management and OSH professions.
OSH professionals working with risk management are confronted with various problems and challenges in their organizations daily.
The need to not only select and modify tools, but properly combine methods to complete the risk management effort, is often required. Simple risk identification or analysis efforts may only require a single technique.
Many situations will require more than one method.

## Slide 33: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Combining Methods
Seldom does one tool adequately meet all the requirements of an entire job, whether it is in construction, manufacturing, or the risk management and OSH professions.
OSH professionals working with risk management are confronted with various problems and challenges in their organizations daily.
The need to not only select and modify tools, but properly combine methods to complete the risk management effort, is often required. Simple risk identification or analysis efforts may only require a single technique.
Many situations will require more than one method.

## Slide 34: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Combining Methods
The authors had developed and exercise and different methods were selected, modified and combined by the risk assessment team after understanding the needs and establishing the context of the assessment.
The methods include in order; 1) HAZID and RISKID; 2) Risk Assessment Matrix (RAM) and Heat Map; 3) Preliminary Hazard Analysis (PHA) of current state and future state; 4) Layers of Protection Analysis (LOPA); 5) Striped Bow Tie Risk Assessments of current state and future state; and 6) a cascading Bow Tie diagram connecting operational risks to safety, health and environmental (SH&E) risks and resulting business consequences (which are tied to an organization’s objectives).

## Slide 35: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Combining Methods

## Slide 36: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Combined Modified Methods Example
Initial Process

## Slide 37: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Combined Modified Methods Example
HAZID

## Slide 38: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Combined Modified Methods Example
RAM

## Slide 39: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Combined Modified Methods Example
RiskID

## Slide 40: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Combined Modified Methods Example
Risk Heat Map

## Slide 41: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Combined Modified Methods Example
Risk Analysis – PHA Example

## Slide 42: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Combined Modified Methods Example
Risk Analysis – LOPA Example

## Slide 43: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Combined Modified Methods Example
Risk Evaluation – Striped Bow Tie Risk Assessment Current State

## Slide 44: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Combined Modified Methods Example
Risk Evaluation – Striped Bow Tie Risk Assessment Future State

## Slide 45: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Combined Modified Methods Example
Cascading Bow Tie Analysis – For complex situations, a cascading Bow-Tie can be used where the consequences of one event may be the cause or trigger of a secondary event – in essence, a chain-reaction.

## Slide 46: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
Conclusion
There are a multitude of methods and options to consider when selecting risk management tools. Having access and knowledge of available methods and tools is the first step. Being able and willing to considered simplifications or modifications, and improvements to methods is the second step. And finally, the ability to put it all together – selecting the right risk management tools, making appropriate adjustments, and combining the methods to achieve the necessary results – is the future of the OSH profession.

## Slide 47: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
References
ANSI/ASSE/AIHA Z10-2012 (R2017). American National Standard—Occupational Health and Safety Management Systems. Fairfax, VA: American Industrial Hygiene Association, 2012.
ANSI/ASSE Z590.3-2011 (R2016). Prevention through Design: Guidelines for Addressing Occupational Hazards and Risks in Design and Redesign Processes. Des Plaines, IL: American Society of Safety Professionals, 2011.
ANSI/ASSE Z690.2-2011. American National Standard – Risk Management Principles and Guidelines. Des Plaines, IL: American Society of Safety Professionals, 2011.
ANSI/ASSE Z690.3-2011. American National Standard - Risk Assessment Techniques. Des Plains, IL: American Society of Safety Professionals, 2011.
ANSI B11.0-2015. Safety of Machinery. Houston, TX: B11 Standards, 2015.
Communicating & Managing Risk: The Key Result of Risk Assessment, Bruce K. Lyon and Georgi Popov. Professional Safety, November 2017, American Society of Safety Professionals
Effective risk assessment in TA, JHA, JSA, JSEA, WMS, TAKE 5 and Incident Investigation, Jim Whiting, June 2013, Proceedings from Safety 2012 Professional Development Conference, American Society of Safety Professionals

## Slide 48: STRATEGIES FOR SELECTING, MODIFYING AND COMBINING RISK MANAGEMENT METHODS
References
Main, Bruce, W. Risk Assessment: Basics and Benchmarks. Ann Harbor, MI: Design Safety Engineering, Inc. 2004.
Main, Bruce, W. Risk Assessment: Challenges and Opportunities. Ann Harbor, MI: Design Safety Engineering, Inc., 2012.
Methanol Hazards & Safeguards: Lessons Learned from the Global Supply Chain, E. Medina, Professional Safety, June 2014, American Society of Safety Professionals
MIL-STD-882E. Standard Practice for System Safety. Washington, DC: Department of Defense, 2012.
Popov, Georgi, Bruce K. Lyon and Bruce Hollcroft, Risk Assessment: A Practical Guide to Assessing Operational Risks. Hoboken, NJ: Wiley, 2016.
Risk Assessments – Top 10 Pitfalls & Tips for Improvement, Bruce K. Lyon and Bruce Hollcroft, Professional Safety, December 2012, American Society of Safety Professionals
The Art of Assessing Risk – Selecting, Modifying, and Combining Methods to Assess Operational Risks, Bruce K. Lyon and Georgi Popov. Professional Safety, March 2016, American Society of Safety Professionals