## Slide 1: Risk Management Tools for Safety Professionals – Part III
CASE STUDY #1
Large Winery Operation
Authors: Bruce K. Lyon, P.E., CSP, ARM, CHMM
Georgi Popov, Ph.D., QEP, SMS, ARM, CMC

## Slide 2: Winery Case Study
Large Winery
Concerns
  Chemical Exposures in Bottling
  Close Calls
  Complaints
  Uncertain of Risks
Notes: SO2 is used to protect the wine from yeast and microbial growth which can spoil or reduce the quality of wine.

## Slide 3: Winery Case Study
Conducted Risk Assessment
Identified FSI-Level Exposures & Existing Controls
Analyzed Risk Levels
Discussed Additional Controls – Proposed ‘Higher Level’ Controls
Re-assessed Risk
Notes: SO2 is used to protect the wine from yeast and microbial growth which can spoil or reduce the quality of wine.

## Slide 4: Risk Criteria
Severity Level | Definition
Catastrophic (4) | Fatalities; Damage to Community, Environment, and Reputation
High (3) | Permanent Disability Injury or Illness; Multiple Injury Events
Moderate (2) | Injury or Illness Requiring Medical Attention
Low (1) | Minor Injury or First Aid Incident
Likelihood Level | Definition
Very Likely (4) | Will happen under right situations; has occurred multiple times
Likely (3) | Likely to happen under right circumstances; has occurred in past
Possible (2) | Can happen in certain situations
Unlikely (1) | Unlikely to happen; remotely possible
 | Low (1) | Moderate (2) | High (3) | Catastrophic (4)
Very Likely (4) | 4 | 8 | 12 | 16
Likely (3) | 3 | 6 | 9 | 12
Possible (2) | 2 | 4 | 6 | 8
Unlikely (1) | 1 | 2 | 3 | 4
Risk Criteria defined by the Winery to be used in the risk assessment
Notes: SO2 is used to protect the wine from yeast and microbial growth which can spoil or reduce the quality of wine.

## Slide 5: Risk Criteria – Action Levels
Notes: SO2 is used to protect the wine from yeast and microbial growth which can spoil or reduce the quality of wine.

## Slide 6: Identified FSI-Level Exposures
Using:
  Past Incidents
  Chemicals & Materials
  Review of Process Steps
  Procedures, Instructions, JSAs
  Site Observations, Audits
  Brainstorming
Hazard Inventory

## Slide 7: Hazard Inventory

## Slide 8: Identified Associated Controls
  Existing Controls
  Warning Alarms
  SOPs for Handling
  Training in Chemical Use
  PPE

## Slide 9: Concern #1 - Pure Liquid Sulfur Dioxide
Used for dosing tanks inside buildings
Filling and Dispensing
Notes: SO2 is used to protect the wine from yeast and microbial growth which can spoil or reduce the quality of wine.

## Slide 10: Concern #1 - Pure Liquid Sulfur Dioxide
Risks
  Potential for releases during filling and dispensing
  Lethal dose = 100 ppm (Cal-OSHA PEL = 2 ppm) (ACGIH TLV = 0.25 ppm)
  Can cause blindness
  Environmental concerns
  Transporting, dispensing, handling, storage concerns
Notes: SO2 is used to protect the wine from yeast and microbial growth which can spoil or reduce the quality of wine.
45 gallons which weighs 548 lbs. exceeds the Threshold Planning Quantity (TPQ) of 500 lbs. for U.S. EPA SARA Title III, Sections 302 and 304, Extremely Hazardous Substances.

## Slide 11: Concern #1 - Pure Liquid Sulfur Dioxide
Sulfur dioxide (SO2) gas is heavier than air and can accumulate in closed areas.
The configuration and lack of ventilation in the bottling area presented a significant risk to employees should a SO2 release occur in the area.
Notes: SO2 is used to protect the wine from yeast and microbial growth which can spoil or reduce the quality of wine.

## Slide 12: Preliminary Hazard Analysis
Task | Hazard | Current Severity | Current Likelihood | Current Risk Level | Recommended Controls | Future Severity | Future Likelihood | Future Risk Level
SO2 Dosing using 100% SO2 liquid | Health risk from leak or release; 2 ppm PEL; 100 ppm lethal dose; Heavier than air. EPA regulated product. | 4 | 3 | 12 |  |  |  | 
Notes: SO2 is used to protect the wine from yeast and microbial growth which can spoil or reduce the quality of wine.

## Slide 13: Preliminary Hazard Analysis
Task | Hazard | Current Severity | Current Likelihood | Current Risk Level | Recommended Controls | Future Severity | Future Likelihood | Future Risk Level
SO2 Dosing using 100% SO2 liquid | Health risk from leak or release; 2 ppm PEL; 100 ppm lethal dose; Heavier than air. EPA regulated product. | 4 | 3 | 12 |  |  |  | 
Unacceptable FSI Risk
Notes: SO2 is used to protect the wine from yeast and microbial growth which can spoil or reduce the quality of wine.

## Slide 14: Proposed Control – Substitute with Less Hazardous Product
Task | Hazard | Current Severity | Current Likelihood | Current Risk Level | Recommended Controls | Future Severity | Future Likelihood | Future Risk Level
SO2 Dosing using 100% SO2 liquid | Health risk from leak or release; 2 ppm PEL; 100 ppm lethal dose; Heavier than air. EPA regulated product. | 4 | 3 | 12 | Substitute 100% SO2 with 6% liquid SO2 and K2S2O5 (potassium meta-bisulfite) effervescent tables, granular, powder | 2 | 2 | 4
Notes: SO2 is used to protect the wine from yeast and microbial growth which can spoil or reduce the quality of wine.

## Slide 15: Proposed Control – Substitute with Less Hazardous Product
Task | Hazard | Current Severity | Current Likelihood | Current Risk Level | Recommended Controls | Future Severity | Future Likelihood | Future Risk Level
SO2 Dosing using 100% SO2 liquid | Health risk from leak or release; 2 ppm PEL; 100 ppm lethal dose; Heavier than air. EPA regulated product. | 4 | 3 | 12 | Substitute 100% SO2 with 6% liquid SO2 and K2S2O5 (potassium meta-bisulfite) effervescent tables, granular, powder | 2 | 2 | 4
67% risk reduction
Notes: SO2 is used to protect the wine from yeast and microbial growth which can spoil or reduce the quality of wine.

## Slide 16: Proposed Control – Substitute with Less Hazardous Product
Task | Hazard | Current Severity | Current Likelihood | Current Risk Level | Recommended Controls | Future Severity | Future Likelihood | Future Risk Level
SO2 Dosing using 100% SO2 liquid | Health risk from leak or release; 2 ppm PEL; 100 ppm lethal dose; Heavier than air. EPA regulated product. | 4 | 3 | 12 | Substitute 100% SO2 with 6% liquid SO2 and K2S2O5 (potassium meta-bisulfite) effervescent tables, granular, powder | 2 | 2 | 4
Notes: SO2 is used to protect the wine from yeast and microbial growth which can spoil or reduce the quality of wine.

## Slide 17: Concern #2 –DMDC Dosing
Dimethyl Dicarbonate (DMDC) - used to prevent spoilage
DMDC inhibits yeast with half-life of 3 hours which converts to CO2 and methanol
Highly specialized metering equipment and training operators

## Slide 18: Concern #2 –DMDC Dosing
Metering equipment located in the bottling area
Bottling Area had limited ventilation and limited means of escape
Exposure ceiling limit is 0.04 ppm
Releases have occurred due to operator error and equipment failure

## Slide 19
Task | Hazard | Current Severity | Current Likelihood | Current Risk Level | Recommended Controls | Future Severity | Future Likelihood | Future Risk Level
DMDC metering equipment in bottling area | Health risk to bottling employees from leak or release in area; 0.4 ppm exposure ceiling limit | 4 | 3 | 12 |  |  |  | 
Preliminary Hazard Analysis
Unacceptable FSI Risk

## Slide 20
Task | Hazard | Current Severity | Current Likelihood | Current Risk Level | Recommended Controls | Future Severity | Future Likelihood | Future Risk Level
DMDC metering equipment in bottling area | Health risk to bottling employees from leak or release in area; 0.4 ppm exposure ceiling limit | 4 | 3 | 12 | Eliminate exposure - relocate DMDC unit outside building (connected with hose) with open ventilation away from bottling area; continue to follow safety protocols and PPE for operator. | 3 | 1 | 3
Preliminary Hazard Analysis

## Slide 21
Task | Hazard | Current Severity | Current Likelihood | Current Risk Level | Recommended Controls | Future Severity | Future Likelihood | Future Risk Level
DMDC metering equipment in bottling area | Health risk to bottling employees from leak or release in area; 0.4 ppm exposure ceiling limit | 4 | 3 | 12 | Eliminate exposure - relocate DMDC unit outside building (connected with hose) with open ventilation away from bottling area; continue to follow safety protocols and PPE for operator. | 3 | 1 | 3
Preliminary Hazard Analysis
75% risk reduction

## Slide 22: As a Result Eliminated two FSI Risks
Task | Hazard | Current Severity | Current Likelihood | Current Risk Level | Recommended Controls | Future Severity | Future Likelihood | Future Risk Level
SO2 Dosing using 100% SO2 liquid | Health risk from leak or release; 2 ppm PEL; 100 ppm lethal dose; Heavier than air. EPA regulated product. | 4 | 3 | 12 | Substitute 100% SO2 with 6% liquid SO2 and K2S2O5 (potassium meta-bisulfite) effervescent tables, granular, powder | 2 | 2 | 4
DMDC metering equipment in bottling area | Health risk to bottling employees from leak or release in area; 0.4 ppm exposure ceiling limit | 4 | 3 | 12 | Eliminate exposure - relocate DMDC unit outside building (connected with hose) with open ventilation away from bottling area; continue to follow safety protocols and PPE for operator. | 3 | 1 | 3
Notes: SO2 is used to protect the wine from yeast and microbial growth which can spoil or reduce the quality of wine.

## Slide 23: Case Study Results
Removed two Fatal or Serious Incident (FSI) level risks
66% risk reduction for SO2 exposure to employees and community
75% risk reduction for DMDC exposure risk
Improved employee morale
Eliminated EPA reporting requirements for SO2
Low costs for K₂S₂O₅ effervescent tables and ease of use
Low costs to relocate and shelter DMDC metering machine outside