## Slide 1
PtD Business Case: Reducing Cr VI Exposure in a Tailpipe Assembly Facility
Presented by: Dr. Georgi Popov, QEP, SMS, ARM

## Slide 2: Session No. 593 Summary
Advanced Risk Assessment/Risk Management Session
This session builds on previous Fundamental and Intermediate Risk Assessment sessions
This Session gives participants the foundation to become familiar with SH&E hazards identification, risk assessment, risk management, and Business Case Development tools.

## Slide 3: Session No. 593 Summary
To demonstrate the elements of RA/RM and PtD Business Case tool, a Cr VI and Ergo Risks reduction case study will be presented
Eliminating or reducing risk of injury or illness in the workplace is critical to maintaining a safe work environment.
This project examined existing hazards and determined through visual observations and sampling results at hand welding stations that most welding fumes are not captured using the current strategies.
New engineering control solution was implemented.
These engineering controls reduced the risk of Hexavalent Chromium (Cr VI) exposure to welders in an exhaust tailpipe and muffler assembly facility. The ergonomic risks were also addressed.
The project ended by determining the Business Case associated with that solution or more succinctly “what was the value to the company for implementing this solution”.

## Slide 4: Introduction to the PtD Business Case Model
Before we proceed to the case study and PtD BC model description, couple of important clarifications

## Slide 5: Introduction to the PtD Business Case Model
What is the SH&E Business Case?
A Business Case in occupational safety and health can be defined as a structured method used to justify a project (intervention or solution) for decision-makers.
It captures the effects of implementing programs or activities on employee health (injury or illness), hazards present, risk level, risk management, and the business process. The effects include customary financial business metrics, such as net present value (NPV), internal rate of return (IRR), return on investment (ROI), Payback Period (PbP), which are meaningful to business management.
In reality, the Business Case answers the question: What’s in it for the company?

## Slide 6: Introduction to the PtD Business Case Model
Why Develop the Business Case?
A well-developed Business Case links safety, health, and environmental (SH&E) investments in protecting worker safety and health to Business Value.
The Business Case will assist in demonstrating that SH&E activities are more than an expense but can indeed have a positive return on the investment.
The Business Case provides support that SH&E professionals are integral partners in the organization and essential contributors to the bottom line.

## Slide 7: Introduction to the PtD Business Case Model
When to Develop the Business Case?
If a SH&E protection project will be or has been implemented by business, on business premises, or under the direction of business, then a Business Case should be developed.
Business managers may request a logical and well considered argument—the Business Case—to justify funding to continue or expand existing solutions.
Necessary resources for a new SH&E investment under consideration can be identified through the development of the Business Case.
The Business Case can also be used to support the overall SH&E function when competing for resources against other functions, such as production, within the organization.

## Slide 8: Introduction to the PtD Business Case Model
How to Use the PtD Business Developer Model?
The Business Case Developer Model uses 5 Steps to determine and illustrate the Business Value of SH&E projects, programs and activities designed to eliminate or mitigate the risks to reduce the associated occupational injuries and illnesses.
For each step, the purpose is described, Modules with data collection forms are provided to derive the necessary information, and additional support is available through the following Instructions that includes a Glossary.

## Slide 9: Introduction to the PtD Business Case Model
PtD Business Case model includes the following steps
To demonstrate the use of PtD Business Case Developer Model, the authors would like to present the following case study.

## Slide 10: PtD Case Study Description
This PtD effort was conducted by a mid-size manufacturer of exhaust tailpipe and muffler assemblies for pick-up trucks. The 20,000 ft2 facility receives pre-cut tubing and mufflers, bends and sizes the tubing, and then assembles and welds the completed muffler/exhaust units.
The facility runs two 8.5-hour work shifts per day (including 30 minutes for lunch and breaks).
Risk assessment, SH&E intervention, risk reduction, financial and non-financial benefits from the improvements were presented using a well-established PtD Business Case methodology.

## Slide 11: PtD Case Study Description – Step 1
Step 1 – Describe Current SH&E Condition
Five production welders work on each work shift, four are hand welders and one operates a Melton welder.
During the morning shift four welders use a handheld, trigger-activated GMAW/ MIG gun, equipped with an automatic filler wire feed. The welding stations were not equipped with local exhaust ventilation.
Exposure assessment was performed as a part of the risk assessment process.

## Slide 12: PtD Case Study Description – Step 1
Step 1 – Describe Current SH&E Condition
Beginning on November 27, 2006, OSHA implemented significantly reduced the Permissible Exposure Limit (PEL) for Cr VI from 52 to 5 µg/m3, and an Action Limit (AL) of 2.5 µg/m3. Exposures above these values mandated a variety of follow-up and corrective actions.

## Slide 13: PtD Case Study Description – Step 1
Step 1 – Describe Current SH&E Condition
Exposure Assessment Results

## Slide 14: PtD Case Study Description – Step 1
Step 1 – Describe Current SH&E Condition
Management wanted to reduce welder’s Cr VI exposure below OELs.
The design of the work stations was evaluated to address ergonomics risks.
Using multiple risk assessment methods, the risk of Cr VI exposure and Musculoskeletal Disorders (MSDs) was determined to be moderate to high.
A team of IH consultants, ergonomics consultants, EHS and Quality manager, engineers, operations manager and a welder was formed.

## Slide 15: PtD Case Study Description – Step 1
Step 1 – Describe Current SH&E Condition
Project objectives included:
Health and Safety Objectives
Cr VI exposure reduction below OSHA PELs.
Reduce lower back injuries (LBI) associated with the welding stations
Reduce shoulder and neck injuries (S&N Inj.) associated with the welding stations
Operational Objectives
Improve company reputation
Improve Process Cycle Efficiency (PCE)
Retain talented employees

## Slide 16: Step 2 – Conduct Risk Assessment
Initial risk assessment was conducted using a modified Preliminary Hazard Analysis (PHA) method. Three hazards were selected for further analysis.
  Irritation and damage to respiratory tract due to Cr VI exposure (1 RT Cr VI)- Chemical/Physical
  Lower Back Injuries (LBI) – Ergonomics
  Shoulder and Neck Injuries (S&N Inj.)- Ergonomics

## Slide 17: Step 2 – Conduct Risk Assessment
Current state hazard assessment PHA

## Slide 18: Step 2 – Conduct Risk Assessment
After the initial risk assessment, the health risk of the current operation was considered not acceptable.
Two of the welding station’s exposure exceeded the Cr VI PEL.
All four of the welding stations exceeded the Action Limit for Cr VI.
Lower back and shoulder/neck injuries were reported. Cr VI, and MSDs health outcomes were included in the risk assessment matrix.

## Slide 19: Step 2 – Conduct Risk Assessment

## Slide 20: Step 2 – Conduct Risk Assessment
SH&E hazards and risks impact on the business operations

## Slide 21: Step 2 – Conduct Risk Assessment
A Business Impact Risk Assessment Matrix (BRAM) was used to evaluate the SH&E risk on the business operations.

## Slide 22: Step 2 – Conduct Risk Assessment
It was apparent that control measures had to be implemented.
The welders experimented with a new welding helmet with supplied air system.
Such controls measures were very unpopular with the welders. The supplied air system was inconvenient for the welders and productivity was negatively affected.
Source: 3M: http://solutions.3m.com

## Slide 23: Step 2 – Conduct Risk Assessment
Striped Bow Tie – SH&E Consequences
Source: Lyon, B.K., Popov, G. (2016, March). The Art of Assessing Risk: Selecting, Modifying & Combining Methods to Assess Operational Risks. Professional Safety, 61(3), 40-51.

## Slide 24: Step 2 – Conduct Risk Assessment
Striped Bow Tie – Business Consequences
Source: Lyon, B.K., Popov, G. (2016, March). The Art of Assessing Risk: Selecting, Modifying & Combining Methods to Assess Operational Risks. Professional Safety, 61(3), 40-51.

## Slide 25: Step 2 – Conduct Risk Assessment
To present a 36,000-ft. view of the current state, SH&E risks and business consequences are then presented utilizing a modified Bow-Tie risk assessment methodology.
ISO 31010 2017 update: Sources of risk (or hazards/ threats in a safety context) are listed at the left hand side of the knot and joined to the knot by lines representing the different mechanisms by which sources of risk can lead to the event

## Slide 26: Step 2 – Conduct Risk Assessment
Bow-tie risk assessment methodology presents opportunities to safety professionals to present OSH hazards and business consequences in one diagram as suggested in ANSI Z10 Section 4.2. (ANSI/AIHA Z10-2012)
It was apparent that higher levels of controls had to be implemented.
Source: 3M: http://solutions.3m.com

## Slide 27: Step 3 – Identify Changes from Current OSH Conditions
To reduce the Cr VI exposure and eliminate the use of respirators, each weld station had to be equipped with unique local exhaust ventilation (LEV).
Captured air is transported overhead to a conventional branched and tapered duct system, where it is filtered, and then exhausted.
To address musculoskeletal disorders of the back, neck and shoulders, adjustable welding work stations were designed. As a result, the following PtD Solutions were agreed upon to reduce risk to welding operators:

## Slide 28: Step 3 – Identify Changes from Current OSH Conditions
PtD solution regarding Cr VI exposure
An inlet pipe with a flare on the end goes into 4x4 inches support frame on the front of the fixture. It also has a few perforated holes on underside of 4x4 to capture some of the welding fumes.

## Slide 29: Step 3 – Identify Changes from Current OSH Conditions
PtD solution regarding Cr VI exposure

## Slide 30: Step 3 – Identify Changes from Current OSH Conditions
As a result of the PtD intervention, Cr VI levels were reduced below the PEL and even below the Action Limit.
Chart: Cr VI µg/m3
| W1 | W2 | W3 | W4 | W5
Cr VI µg/m3 | 1.9 | 2.2 | 0.1 | 0.15 | 0.51

## Slide 31: Step 3 – Identify Changes from Current OSH Conditions
PtD solution regarding Musculoskeletal Disorders
All welding work stations were modified, including height adjustments.
Risk assessment was conducted after the intervention as well. The same risk assessment methodology was followed to assess risk after the intervention.

## Slide 32: Step 3 – Identify Changes from Current OSH Conditions
Risk assessment after the intervention.

## Slide 33: Step 4 – Determine Value
Value of the PtD Solution:
The proposed changes led to substantial risk reduction, financial and non-financial benefits to the company. Risk reduction is considered the most important non-financial benefit. SH&E risk levels before and after the interventions were compared

## Slide 34: Step 4 – Determine Value
Value of the PtD Solution:
Risk reduction #1 Non-Financial Benefit SH&E

## Slide 35: Step 4 – Determine Value
Value of the PtD Solution:
Risk reduction #1 Non-Financial Benefit Business

## Slide 36: Step 4 – Determine Value
Solution costs – Year 0

## Slide 37: Step 4 – Determine Value
Solution costs – Year 1

## Slide 38: Step 4 – Determine Value
Changes in Incident costs

## Slide 39: Step 4 – Determine Value
Changes in Incident costs

## Slide 40: Step 4 – Determine Value
Changes in Incident costs

## Slide 41: Step 4 – Determine Value
Cash Flow

## Slide 42: Step 4 – Determine Value

## Slide 43: Step 4 – Determine Value
Non-Financial Benefits (NFB)

## Slide 44: Step 5 – Develop Recommendations Report
5 min Elevator Speech

## Slide 45: Step 5 – Develop Recommendations Report
5 min Elevator Speech

## Slide 46: Conclusion
Using the PtD Business Case Developer Tool, the proposed changes were shown to lead to substantial risk reduction, financial and non-financial benefits to the company. Risk reduction was considered the most important non-financial benefit.
The project team determined that adoption of this PtD solution would be beneficial to the organization.

## Slide 47: Bibliography
American Industrial Hygiene Association (2009). Strategy to Demonstrate the Value of Industrial Hygiene. Information available at http://www.ihvalue.org
ANSI/ASSE/AIHA Z10-2012. American National Standard—Occupational Health and Safety Management Systems. Fairfax, VA: American Industrial Hygiene Association, 2012.
ANSI/ASSE Z590.3-2011. (2011). Prevention through Design: Guidelines for Addressing Occupational Hazards & Risks in Design & Redesign Processes. Information available at: http://www.asse.org/shoponline/products/Z590_3_2011.php
Biddle E, Carande-Kulis V, Woodhull D, Newell S, and Shroff R. (2011). The Business Case for Occupational Safety, Health, and Environment and Beyond. In S.Clark, R.J. Burke & C.L. Cooper (Eds), Occupational Health and Safety. Famham, England: Ashgate Publishing Ltd.
NIOSH PtD (n.d.). Retrieved February 21, 2017, from: http://www.cdc.gov/niosh/docs/2011-121/pdfs/2011-121.pdf
Popov, G., Lyon, B.K. & Hollcroft, B. (2016). Risk assessment: A practical guide to assessing operational risks - Hoboken, NJ: John Wiley & Sons. Supplemental risk assessment tools available at: http://centralspace.ucmo.edu/xmlui/handle/123456789/407