## Slide 1: Risk Management Tools for Safety Professionals – Part III
CASE STUDY #3
PtD in Construction
Authors: Bruce K. Lyon, P.E., CSP, ARM, CHMM
Georgi Popov, Ph.D., QEP, SMS, ARM, CMC

## Slide 2: PtD RA Quotes
“People who don’t take risks generally make about two big mistakes a year. People who do take risks generally make about two big mistakes a year.” – Peter F. Drucker
“A ship is always safe at the shore - but that is NOT what it is built for." Albert Einstein

## Slide 3: PtD RA Tool Overview
The PtD tool highlights a 4-step approach to risk assessment:
Most importantly, this tool requires the user to develop balanced process and a logic based risk assessment methodology designed to engage the participants through the hazard assessment and risk prioritization process.

## Slide 4: Why PtD Risk Assessment Tools?
ANSI/ASSE Z590.3-2011 Prevention through Design standard addresses occupational safety and health needs and RA methodologies
ANSI/ASSE/ISO (Z690-2011) Risk Management Standards Package - This standard provides principles and generic guidelines on risk management.
ANSI/AIHA/ASSE Z10-2012: The standard defines minimum requirements for an OSHMS. It also includes risk assessment components not previously included.
ISO 45001 OSHMS also includes risk assessment components .

## Slide 5: ANSI Z10 Requirements – Section 4.1

## Slide 6: ANSI Z10 Requirements – Section 4.2

## Slide 7: ANSI Z10 Section 4.2 Recommended Practices
Notice:
Multiple RA methods
Financial Impact
Regulatory compliance
Include:
Business Issues
Setting Priorities
High Severity

## Slide 8: ANSI Z10 Section 4.2 Recommended practices
Establish priorities based on levels of risk (RAM)
Potential for system improvements (PtD HofC)
Business consequences (Bow – tie analysis).

## Slide 9: ANSI Z10 & PtD

## Slide 10: Risk Assessment Process and the PtD Model
ISO 31000/ANSI Z690.2 and ANSI Z590.3 -2011 Integration

## Slide 11: Risk Assessment Process and the PtD Model
As illustrated in the previous slide and Figure to the right, the two standards are similar in the process steps with a few differences.
Comparisons of Risk Assessment in ISO 31000/ANSI Z690.2 and ANSI Z590.3

## Slide 12: Hazard ID -OSHA 300 Form

## Slide 13: OSHA 300 Incidence Rate Comparison
Source: http://data.bls.gov/iirc/

## Slide 14
Financial Losses
Non- Financial Losses???
Notes: https://www.osha.gov/dcsp/smallbusiness/safetypays/estimator.html

## Slide 15: PtD RA Tool
Notes: Source: OSHA Training Materials http://ehs.okstate.edu/training/oshaback.htm

## Slide 16: Hand-Operated Grinders: Identify Tasks and Hazards
Silica Dust: “Activities that may produce crystalline silica dust include jack hammering, rock/well drilling, concrete mixing, concrete drilling, and brick and concrete block cutting and sawing.”
Electric and pneumatic hand operated grinders used for surface finishing and cutting jobs may produce silica dust.
Sources: https://www.osha.gov/dsg/topics/silicacrystalline/hazard_recognition_silica.html
https://www.osha.gov/Publications/3362silica-exposures.pdf

## Slide 17: Hand-Operated Grinders: Identify Tasks and Hazards
Vibration Hazards: Extent of Exposure
Based on a 1974 study of occupational exposures to vibration, NIOSH estimates that 1.2 million workers in the United States are potentially exposed to hand-arm vibration
Source: http://www.cdc.gov/niosh/docs/83-110/

## Slide 18: Hand-Operated Grinders: Identify Tasks and Hazards
Noise:
According to OSHA “Prolonged exposures to loud noise can lead to a gradual, but permanent, loss of hearing.”
Current State controls:
Source: https://www.osha.gov/Publications/3498noise-in-construction-pocket-guide.pdf

## Slide 19: Hand-Operated Grinders: Identify Tasks and Hazards
Employees produce dusts containing silica when they grind on concrete and similar materials.
Data compiled by the Occupational Safety and Health Administration (OSHA) indicate that, among employees who grind concrete, most are exposed to silica at levels that exceed OSHA’s benchmark of 0.1mg/m³ (milligrams of silica per cubic meter of air)
Source: https://www.osha.gov/Publications/3362silica-exposures.pdf

## Slide 20: H&S Risk Assessment

## Slide 21: Risk of business continuity loss from Hazardous Work Environment

## Slide 22: Hazards and Consequences 30,000 ft. overview

## Slide 23: PtD HoC

## Slide 24: H&S Hazards - New Controls

## Slide 25: H&S Risk Assessment - New Controls

## Slide 26: Risk of business continuity loss from Work Environment – New Controls

## Slide 27: Hazards and Consequences 30,000 ft. overview – New Controls

## Slide 28: Assess Residual Risk and Risk Reduction

## Slide 29: Conclusion
Risk Assessment is a critical component of ANSI/AIHA Z-10, ANSI/ASSE Z690.3-2011, and PtD standards.
Through the use of the PtD risk assessment, newly designed power tools, and improved controls can successfully reduce injuries and illnesses within construction industry.
Additional steps: Cost-benefit analysis can demonstrate the need for tool replacement and highlight financial and non-financial benefits.
Notes: Source: OSHA Training Materials http://ehs.okstate.edu/training/oshaback.htm