## Slide 1: Risk Management Tools for Safety Professionals – Part III
CASE STUDY #4
Meatpacking Operation
Authors: Bruce K. Lyon, P.E., CSP, ARM, CHMM
Georgi Popov, Ph.D., QEP, SMS, ARM, CMC

## Slide 2: CASE STUDY #4 Meatpacking Operation
One of the primary exposures in meatpacking operations (beef, pork, poultry) is bio-mechanical or musculo-skeletal hazards. Standard risk assessment methods are not designed to identify and analyze such hazards. Therefore, methods that pinpoint ergonomic risk factors such as the screening and assessment tools, Ergonomics Risk Assessment Tool (ERAT) can be used.
ERAT was developed by the authors and is based on the draft ANSI Z365 Ergonomics Checklist that was part of the “Management of Work-Related Musculoskeletal Disorders Accredited Standards Committee Z365 Working Draft” withdrawn in 2003.

## Slide 3: CASE STUDY #4 Meatpacking Operation
Tool Selection - In this case study, the authors selected the ERAT tool to perform an ergonomic risk assessment of a pork processing task. ERAT, which provides a standardized method of quickly identifying, assessing and scoring ergonomic risks to upper extremities, uses an Initial Assessment Worksheet, and a Post-Controls Assessment Worksheet to establish risk factor scores.
A Hierarchy of Ergonomic Risk Controls is included to define risk treatment options.

## Slide 4: CASE STUDY #4 Meatpacking Operation
- ERAT is a ‘targeted’ assessment of ergonomic risk factors impacting the upper extremities, which can be applied to office environments, and assembly type work.
The Initial Assessment (IA Worksheet) is used to develop a baseline risk score and action level with possible control measures to reduce risk factor scores.
The Post-Controls Assessment (PCA Worksheet) is used after the Initial Assessment and implementation of control measures to establish a current risk factor score.

## Slide 5: CASE STUDY #4 Meatpacking Operation
Tasks Selected and Studied - Tasks with a history of muculo-skeletal disorders (MSDs) and employee complaints were reviewed and targeted for the assessment. The risk assessment team using digital video, recorded task cycles of the jobs selected from a variety of angles to capture normal work activities and conditions. Weights of objects handled, tools used, distances and dimensions were collected to further analyze.
A video was used to study task repetition, postures, lifts, pulls, pushes, carries, and other factors covered by the assessment tool.

## Slide 6: CASE STUDY #4 Meatpacking Operation
Task Description – Pork Belly Grading involves two operators standing at the end of an incoming conveyor approximately waist high. Each worker manually grabs individual pork bellies using one hand and then turn and place on an adjacent weighing scale.
The work visually grades the belly quickly and then tosses it with one arm into one of several bins approximately 6 to 8 feet away.
The work pace for each worker is approximately 10 bellies a minute equating to approximately 60 per hour or 480 bellies per 8 hour shift.
Pork bellies weigh between 11 and 14 pounds each, with average around 13 pounds.

## Slide 7: ERAT Initial Assessment Scores
Notes: The students will select scores for all different categories and perform initial evaluation. The total Action Level (AL) score will determine potential Ergo intervention. AL in this case requires intervention in the near future.

## Slide 8: Ergonomics Risk Controls Selection and Implementation
Notes: Read briefly potential sollutions

## Slide 9: CASE STUDY #4 Meatpacking Operation
Intervention – The resulting interventions involved engineering controls including in-line weighing scales placed in a new conveyor system, placement of chutes and bins beneath the conveyor system eliminating the need for the excessive handling and throwing tasks.
The engineering control measures also helped to eliminate or reduce a number of extreme, repetitive postures.

## Slide 10: Post-Control Assessment
Notes: The students use the same scoring system to evaluate the risk level after the improvements. In this case we were able to reduce the risk level. However, further analysis is still required.